## Slide 1: 20 MHz Tone Plan and Pilot Design for DRU Follow Up
Date: 2024-05-12
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In the last F2F meeting, various topics for DRU were extensively discussed [1-12]
  Tone plan designs [5][7][8][12] and pilot designs [5][8][11] were discussed
  In particular for 20 MHz, we introduced approaches on how to design DRU tone plan and pilot in [5]
In this contribution, we propose a 20 MHz DRU tone plan and its pilot tones
  We compare our proposed tone plan with that in [7]
  We also discuss some benefits of the proposed pilot tones

## Slide 3: Design Principle for 20 MHz DRU Tone Plan
Basically, we follow the general principle introduced in [5]
We also consider minimizing the PAPR and achieving mirror symmetry at the same time
To this end, we allocate DRUs to {-121 ~ -5, +5 ~ +121}
Also, we place four null tones which are additionally allocated to 106 DRUs on -4, -3, +3, +4

## Slide 4: Proposed 20 MHz DRU Tone Plan
Proposed 20 MHz DRU tone plan
  26 DRU_1: {-121:9:-13, 5:9:113}
  26 DRU_2: {-116:9:-8, 10:9:118}
  26 DRU_3: {-119:9:-11, 7:9:115}
  26 DRU_4: {-114:9:-6, 12:9:120}
  26 DRU_5: {-117:9:-9, 9:9:117}
  26 DRU_6: {-120:9:-12, 6:9:114}
  26 DRU_7: {-115:9:-7, 11:9:119}
  26 DRU_8: {-118:9:-10, 8:9:116}
  26 DRU_9: {-113:9:-5, 13:9:121}
  52 DRU_1: 26 DRU_1 + 26 DRU_2
  52 DRU_2: 26 DRU_3 + 26 DRU_4
  52 DRU_3: 26 DRU_6 + 26 DRU_7
  52 DRU_4: 26 DRU_8 + 26 DRU_9
  106 DRU_1: 52 DRU_1 + 52 DRU_2 + {-4, 3}
  106 DRU_2: 52 DRU_3 + 52 DRU_4 + {-3, 4}
Tone spacing of 26 DRU is multiples of nine even around DC for low PAPR and better smoothing gain
Each pair is mirror symmetric
{26 DRU_a, 26 DRU_10-a}
{52 DRU_a, 52 DRU_5-a}
{106 DRU_1, 106 DRU_2}

## Slide 5: PAPR Comparison
PAPR comparison
  Two tone plans have almost same PAPR
26 DRU
106 DRU
52 DRU
26 DRU
106 DRU
52 DRU
BPSK
QAM

## Slide 6: Comparison for 20 MHz DRU Tone Plans
Comparison
 | PAPR | Channel smoothing | Implementation
Proposed tone plan | Similar | Possible | Simpler w/ mirror symmetry
Tone plan in [7] | Similar | Possible | Not symmetric

## Slide 7: Proposed Pilot Tones for 20MHz DRU Tone Plan (1/3)
Design approach for pilot tones
  We apply a tone shift to 7th and 20th tones to determine pilot tones as shown in [5]
    Pilot tone gap in each 26 DRU is 126
  Pilot tone gap between two adjacent pilot tones is 10
  By using this approach we can have sufficiently distributed pilot tones which have mirror symmetry
Pilot tones for 26 DRUs
  Both pilot and data tones are mirror symmetric in the following pair
    {26 DRU_a, 26 DRU_10-a}  These are also the same DRU type
26 DRU_1
26 DRU_6
26 DRU_3
26 DRU_8
26 DRU_5
26 DRU_2
26 DRU_7
26 DRU_4
26 DRU_9
Note that the proposed pilot tones are the same as option 2 in [12]
In forward or backward order of DRU, data and pilot tones are aligned with other DRUs

## Slide 8: Proposed Pilot Tones for 20MHz DRU Tone Plan (2/3)
Pilot tones for 52 DRUs
  Pilot tones are sufficiently spaced within DRU as well as among different DRUs
  Also, both pilot and data tones are mirror symmetric in the following pair
    {52 DRU_a, 52 DRU_5-a}  These are also the same DRU type
52 DRU_1
52 DRU_3
52 DRU_2
52 DRU_4

## Slide 9: Proposed Pilot Tones for 20MHz DRU Tone Plan (3/3)
Pilot tones for 106 DRUs
  For a sufficient gap between pilot tones and mirror symmetry, we propose the following pilot tones (red tones)
    106 DRU_1: {-103, -53, 23, 73}
    106 DRU_2: {-73, -23, 53, 103}
  As a result, both pilot and data tones are mirror symmetric between two 106 DRUs and these are also the same DRU type
106 DRU_1
{-4, 3} tones are added
106 DRU_2
{-3, 4} tones are added

## Slide 10: Discussion on Pilot Tones (1/2)
The proposed pilot tones are sufficiently spaced within DRUs as well as among different DRUs
  They can overcome residual CFO impact and provide reliable performance
  See Appendix for performance comparison between our pilot tone design approach and pilot tones in [11]
Also, since the proposed pilot tones have a mirror symmetric property, our complete tone plan is totally mirror symmetric
  This is the traditional design method and thus it may be desirable for implementation
    Merits may be reduced when only one part (i.e., either data tones or pilot tones) has this property
  Also, we saw that this property makes no harmful impact on PAPR
    While in some tone plans having this property can degrade the PAPR performance

## Slide 11: Discussion on Pilot Tones (2/2)
In addition, the proposed pilot tones can significantly reduce DRU types in the proposed DRU tone plan
  Basically, most of the RRUs with the same size are the same type
    Implementation may be unified for a certain size RRU
  Thus, minimizing DRU types would be helpful to complexity reduction
  In [12], the same pilot tones are applied to the tone plan in [7] and there are five 26 DRU, four 52 DRU and two 106 DRU types
    We found that it can be easily achieved under various kinds of pilot tones
  Whereas in our proposed tone plan DRU types can be further reduced by using the proposed pilot tones and there are five 26 DRU, two 52 DRU and one 106 DRU types
    From this perspective, the proposed pilot tones are more suitable to our tone plan

## Slide 12: Conclusion
We have proposed the 20 MHz DRU tone plan and have compared it with the tone plan proposed in [7]
  Two tone plans have similar performance in terms of PAPR
  From the implementation point of view, our proposed tone plan may be more desirable based on the mirror symmetric property
We have also proposed the design approach for pilot tones and have provided specific pilot tones for 20 MHz DRU tone plan
  The proposed pilot tones are mirror symmetric and sufficiently spaced within DRU and among different DRUs as well
  The proposed pilot tones can significantly reduce DRU types in our proposed tone plan

## Slide 13: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  11bn supports 20 MHz distribution bandwidth for DRU
Y/N/A: //

## Slide 14: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  In 20 MHz distribution bandwidth, the following DRUs are defined
    Nine 26 DRUs
    Four 52 DRUs
    Two 106 DRUs
Y/N/A: //

## Slide 15: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  In 20 MHz distribution bandwidth, 52 / 106 DRUs are defined as follows
    52 DRUs are defined by combining two 26 DRUs
      Different 52 DRUs consist of different 26 DRUs
    106 DRUs are defined by combining two 52 DRUs and two null tones
      Different 106 DRUs consist of different 52 DRUs and different null tones
    Tone indices for 26 DRUs and four null tones are TBD
    Exact DRU combinations are TBD
Y/N/A: //

## Slide 16: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  DRU tone plan for 20 MHz bandwidth is defined as follows
    26 DRU_1: {-121:9:-13, 5:9:113}
    26 DRU_2: {-116:9:-8, 10:9:118}
    26 DRU_3: {-119:9:-11, 7:9:115}
    26 DRU_4: {-114:9:-6, 12:9:120}
    26 DRU_5: {-117:9:-9, 9:9:117}
    26 DRU_6: {-120:9:-12, 6:9:114}
    26 DRU_7: {-115:9:-7, 11:9:119}
    26 DRU_8: {-118:9:-10, 8:9:116}
    26 DRU_9: {-113:9:-5, 13:9:121}
    52 DRU_1: 26 DRU_1 + 26 DRU_2
    52 DRU_2: 26 DRU_3 + 26 DRU_4
    52 DRU_3: 26 DRU_6 + 26 DRU_7
    52 DRU_4: 26 DRU_8 + 26 DRU_9
    106 DRU_1: 52 DRU_1 + 52 DRU_2 + {-4, 3}
    106 DRU_2: 52 DRU_3 + 52 DRU_4 + {-3, 4}
    The RU indices within parentheses stand for the RRU indices which are mapped to DRUs
Y/N/A: //

## Slide 17: Straw Poll #5
Do you agree to add the following text to the TGbn SFD?
  Pilot tone gap in each 26 DRU is 126
  Tone gap between two adjacent pilot tones is 10 except for around DC tones
  Exact pilot tone indices are TBD
Y/N/A: //

## Slide 18: Straw Poll #6
Do you agree to add the following text to the TGbn SFD?
  Pilot tones for DRUs in 20 MHz bandwidth are defined as follows
    26 DRU_1: {-103, 23}
    26 DRU_2: {-53, 73}
    26 DRU_3: {-83, 43}
    26 DRU_4: {-33, 93}
    26 DRU_5: {-63, 63}
    26 DRU_6: {-93, 33}
    26 DRU_7: {-43, 83}
    26 DRU_8: {-73, 53}
    26 DRU_9: {-23, 103}
    52 DRU_1: {-103, -53, 23, 73}
    52 DRU_2: {-83, -33, 43, 93}
    52 DRU_3: {-93, -43, 33, 83}
    52 DRU_4: {-73, -23, 53, 103}
    106 DRU_1: {-103, -53, 23, 73}
    106 DRU_2: {-73, -23, 53, 103}
Y/N/A: //

## Slide 19: Appendix

## Slide 20: Performance Comparison for Pilot Tones (1/7)
Pilot tones were proposed in [11] based on the tone plan [7]
  In the next slide, we show the pilot tones in detail
Here, we compare the performance between our proposed pilot tone design and those in [11]
  Since pilot tones in [11] are based on the tone plan in [7], we use that tone plan for PER comparison
    To this end, we apply our proposed pilot design approach to the tone plan in [7]
  We compare the performance for 52 DRUs
    The performance for 26 DRUs may be similar since the pilot tone gap within each 26 DRU is the same for both proposals
    [11] doesn’t provide pilot tones for 106 DRUs

## Slide 21: Performance Comparison for Pilot Tones (2/7)
In [11], pilot tones were proposed based on the tone plan in [7]
  We can see that the pilot tones within 52 DRUs are closely located
26 DRU_1
26 DRU_6
26 DRU_3
26 DRU_8
26 DRU_2
26 DRU_7
26 DRU_4
26 DRU_9
26 DRU_5
52 DRU_1
52 DRU_3
52 DRU_2
52 DRU_4

## Slide 22: Performance Comparison for Pilot Tones (3/7)
We compare the PER performance between our proposed tone plan and tone plan proposed in [7]
Simulation Assumptions
  20 MHz UL TB PPDU with four 52 DRUs
  SISO under Channel D NLoS
  1000 data bits per each STA
  MCS 0/8 with LDPC coding
  No channel smoothing
  Residual CFO for each STA: [+rCFO –rCFO +rCFO –rCFO]
    Different rCFO values are considered depending on the MCS level
  PERs for all 52 DRUs are provided

## Slide 23: Performance Comparison for Pilot Tones (4/7)
52 DRU_1
  It seems that the proposed pilot tones have slightly better performance at 10 % PER especially with high rCFO although they look almost similar
    Pilot tones for 52 DRUs in [11] are located relatively close to each other compared to our proposal
MCS 0
MCS 8

## Slide 24: Performance Comparison for Pilot Tones (5/7)
52 DRU_2
  We can see that proposed pilots have slightly better performance
MCS 0
MCS 8

## Slide 25: Performance Comparison for Pilot Tones (6/7)
52 DRU_3
  We can see that proposed pilots have slightly better performance
MCS 0
MCS 8

## Slide 26: Performance Comparison for Pilot Tones (7/7)
52 DRU_4
  We can see that proposed pilots have slightly better performance
MCS 0
MCS 8

## Slide 27: References
[1] 11-23-2200-03-00bn-distribution-bandwidth-of-dru
[2] 11-24-0332-00-00bn-discussion-on-drus
[3] 11-24-0400-00-00bn-hybrid-ppdu-and-distribution-bandwidth-for-dru
[4] 11-24-0401-00-00bn-multiple-dru-follow-up
[5] 11-24-0402-01-00bn-20-mhz-tone-plan-and-pilot-design-for-dru
[6] 11-24-0429-00-00bn-range-extension-with-dru
[7] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[8] 11-24-0476-01-00bn-tone-plan-design-principles-for-distributed-ru
[9] 11-24-0477-02-00bn-high-level-perspective-on-dru-follow-up
[10] 11-24-0500-00-00bn-follow-up-on-high-level-thoughts-on-dru-design
[11] 11-24-0501-02-00bn-pilot-design-considerations-for-dru
[12] 11-24-0520-01-00bn-discussion-on-dru
[13] 11-24-0800-01-00bn-dsicussions-on-dru-pilot-design-principles