## Slide 1: UHR preamble design follow-up
Date: 5/15/2024
Authors:

## Slide 2: Introduction
11be introduced a generic, forward compatible preamble structure to be used for 11be and subsequent PHY amendments
  PHY Version ID, Version-dependent and Version-independent fields, …
    See [1] for details
Within this framework, a new preamble type can be defined by using a new PHY Version ID Value
Additionally – or alternatively – features could be added to 11be using existing reserved bits
  Even without change in PHY Version ID
  See [1]

## Slide 3: What should the preamble for 11bn transmissions look like?
Some possible options:
  New PHY Version ID (e.g., 1) for any transmission between 11bn capable systems?
  Keep PHY Version ID = 0 and possible use of reserved bits (see [1])?
  A combination of the above?

## Slide 4: Drawbacks of using a new PHY Version ID
A new PHY version ID for all 11bn transmissions will create duplication
  Example: SU PPDU
    11bn may introduce new PHY modes (MCS, coding, …)
    11bn will continue to support existing PHY modes
    A PPDU sent using an existing mode would be identical to 11be (with the possible exception of the preamble)
  Duplication involves extra testing during verification, certification, …
A new PHY version ID for all 11bn transmissions also means we need sufficient bits to signal all legacy + new modes
  Number of available bits is very limited

## Slide 5: A general working principle
To avoid undesirable duplication and to reduce the need for signaling a large number of modes, we could adopt the following general principle:
“Any 11bn transmission that uses only functionality that is already available in 11be shall use the 11be format to send the frame.”
For new functionality we then have the option(s) of either defining a new PHY Version ID or using reserved bits (or a combination of both)

## Slide 6: Possible PPDU formats
PHY Version ID = 0, no change in reserved bits
  “pure” 11be
PHY Version ID = 0, modify some reserved bits
  “extended 11be”
PHY Version ID = 1
  “pure” 11bn
Allowing 11bn-capable systems to use some or all of these formats makes it possible to:
  avoid duplication
  focus the preamble design (and the limited number of available bits) on accommodating the new modes

## Slide 7: Proposal
11bn uses a mix of PHY Version ID value 0 and a newly defined value for PHY Version ID (presumably 1) when sending frames.
This value may change on a per-PPDU basis. The exact use of each of the PHY version IDs (and the available reserved bits for PHY Version ID = 0) is up for further discussion
  The use of value 0 and 1 is implemented such that functionality from 11be needs not be duplicated
Additional use of reserved bits with PHY Version ID value 0 is TBD

## Slide 8: References
[1] 802.11-24/0428r0, UHR preamble design options