## Slide 1
Discussion of AID Obfuscation
Date: 2024-05-12
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission proposes making use of a reserved bit to improve EDP operation.

## Slide 3: Summary
There are 2 AID bits unused in MLD operation. This presentation discusses potential ways to make use of at least one of these bits to allow moree efficient epoch transitions.

## Slide 4: Requirements
The following requirement deals with changing a STA’s AID.
11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.

## Slide 5: AID Subfield discussion - background
In our discussions, we have targeted initially MLDs as the only devices to have access to MAC randomization during association.
A MLD gets a single AID to use for all of its associated STAs. (35.3.5.1 in TGbeD5.0)
We have discussed reserving a block of AIDs for EDP MLDs so that the AP can rotate the AIDs while not disturbing the legacy STAs and legacy MLDs.
The issue is that during a transition period, we need space for 2x MAC addresses (not a problem) and 2x AIDs (a problem).
This problem is important because it will restrict the number of STAs and MLDs that an AP MLD can associate.

## Slide 6: AID and AID IE
An AID is nominally 16 bits, but:
The AID field for a non-DMG and non-S1G STA associated to a non-EHT AP is in the range 1 to 2007. The AID field for a STA associated to an EHT AP or for a non-AP MLD associated to an AP MLD is in the range 1 to 2006. This value is placed in the 14 LSBs of the AID field, with the two MSBs of the AID field set to 1.*
1
1
AID 11
AID 12
While AID11 is used in several messages, extra bits are reserved in most of those messages, so we can get 12 bits.
* Text from TGbeD5.0

## Slide 7: MLD messaging using AID
Multi-Link Traffic Indication Control field format specifies AID 11, but has a reserved bit, so it could use AID12.
The AID Bitmap element refers to a bitmap of 2008 bits using 7 bits in the Bitmap Control field of the AID Bitmap element. There is again a reserved bit that could be added to the active bits in the AID Control field to expand the size of the AID bitmap and thus the number of AIDs available.

## Slide 8: Discussion
We could use the extra bit in at least two possible ways:
We could use that bit essentially as a flag during transitions.
    if the bit set, the AID should get special treatment during the transition period at the beginning of an epoch because it is the old AID (or it’s a new AID).
2) Alternately, we could use the bit to expand the AID space for EPD MLDs.
    if the MLD is an EPD MLD, it always gets an AID from that number space (2049 to 4096).

## Slide 9: Discussion – Flag Transition AIDs
Bit 12 of the AID is a flag that marks an old AID.
    if the bit is set in an AID during the transition period at the beginning of an epoch, it marks the AID as an old AID.
    When would it be used: an AP MLD would set that bit in any messages sent during the transition using the old AID
    If bit 12 is set in the old AID during a transition, an observer would not gain information about the new MAC/AID, other than by inference.
  Advantages:
  No decrease to the number of devices that an EDP AP MLD will be able to support over and above any MLO restrictions
  The use of the additional bit could be restricted to the transition period. For simplicity, some features that use AID11 could only be disabled during the transition period versus altering them to allow the use of AID12 or we can take advantage of the reserved bit(s).
  Disadvantage:
  The use of a different value for the bit might lead to HW level changes

## Slide 10: Discussion – Expand the AID space
2) Alternately, we could use the bit to expand the AID space for EPD MLDs.
    if the MLD is an EPD MLD, it gets an AID from that number space (2049 to 4096).
  Advantages:
    Increases the number of MLDs and STAs that an EDP AP MLD can support
    Could be used for MLO in general to improve the number of devices supported per AP
  Disadvantage:
    Messages that use AID11 would need to be altered to take advantage of the reserved bits, but reserved bits are available
    It would clearly separate EDP MLDs from other MLDs and STAs

## Slide 11: Other Investigation
The AID in the form of Partial AID, AID11, AID12, and AID13 are used a many places in the text.
I have started working on text updates, but wanted to get an impression from the group of the feasibility of these changes, and whether the group prefers a flag-based operation or a straight expansion of the AIDs used.

## Slide 12: Example Text for use of bit 12
The AID field for a non-DMG and non-S1G STA associated to a non-EHT AP is in the range 1 to 2007. The AID field for a STA associated to an EHT AP or for a non-AP MLD associated to an AP MLD is in the range 1 to 2006. This value is placed in the 14 LSBs of the AID field, with the two MSBs of the AID field set to 1. The AID for a non-AP MLD supporting EDP associated to an AP MLD supporting EDP is in the range 2049 to 4095.

## Slide 13: Straw Poll
Do you support considering using bit 12 in the AID to enhance EDP operation?
Would you prefer using bit 12 to expand the AID space or to be a flag for AID transitions?