## Slide 1
Discussion of AID obfuscation during the transition period
Date: 2024-09-05
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This submission proposes a combination of techniques including making use of a reserved bit to improve EDP operation during the transition period between epochs.

## Slide 3: Summary
During a transition period, the same AID might be assigned to two different non-AP MLDs from two different FA parameter sets.
This submission proposes a method of handling that overlap, through a combination of restricting which FA parameter set is used during a transition period, suspending AID-related messaging during the transition period and/or using a spare bit in AID-related messages.

## Slide 4: Requirements
The following requirement deals with changing a STA’s AID.
11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.

## Slide 5: AID Subfield discussion - background
In our discussions, we have targeted initially MLDs as the only devices to have access to MAC randomization during association.
A non-AP MLD gets a single AID to use for all of its associated non-AP STAs. (35.3.5.1 in TGbeD7.0. p550.26)
We have discussed reserving a block of AIDs for EDP non-AP MLDs so that the AP can rotate the AIDs while not disturbing the legacy STAs and legacy non-AP MLDs.
The issue is that during a transition period, we need space for 2x MAC addresses (not a problem) and 2x AIDs (a problem).
This problem is important because it will restrict the number of STAs and non-AP MLDs that an AP MLD can associate.

## Slide 6: Summary of Transition Period assumptions
The transition period happens when a new EDP epoch begins.
An MLD is expected to be able to receive and correctly act upon frames with its new AID once the transition period has begun.
The purpose of the transition period is to allow stored/buffered frames or frames subject to retransmission an opportunity to be transmitted versus just being deleted to clear the buffers.

## Slide 7: AID and AID IE
An AID is nominally 16 bits, but:
The AID field for a non-DMG and non-S1G STA associated to a non-EHT AP is in the range 1 to 2007. The AID field for a STA associated to an EHT AP or for a non-AP MLD associated to an AP MLD is in the range 1 to 2006. This value is placed in the 14 LSBs of the AID field, with the two MSBs of the AID field set to 1. (TGbeD7.0)
1
1
AID 11
AID 12

## Slide 8: Discussion – PS-Poll frame
9.3.1.5 NDP PS-Poll frame format
Since the PS-Poll frame is generated by the non-AP MLD’s affiliated STA, the STA can always choose to use the AID from the new FA parameter set.
Proposed text adds a requirement to that affect to the Non-BDT variant of the PS-Poll frame format (9.3.1.5.2).

## Slide 9: Discussion – Multi-STA BlockAck
Multi-STA BlockAck variant (9.3.1.8.6) –
    This variant is the only BlockAck frame making use of AID11. But for this frame type, the TID_INFO subfield in the BA Control field is reserved. A bit from that field can be used to indicate that the AID11 values are from the previous epoch.
    If the AP MLD does mark a multi-STA BlockAck as containing AIDs from the previous epoch, it should only contain AIDs from the previous epoch and AIDs of legacy STAs.
    Alternatively, the AP could be directed to not use this frame during the transition period. That approach could be problematic depending upon how often the AP uses the Multi-STA BlockAck frame.
    Recommended text: use a bit to indicate if the AIDs in the frame are from the previous set of FA parameters during an EDP transition period.

## Slide 10: Discussion – NDP Announcement frame
9.3.1.19 NDP Announcement frame format
Based on the changes in TGbeD7.0, there are not any easily reclaimed bits that can be used in 9.3.1.19.5 EHT NDP Announcement frame format to mark the use of an outdated AID during the transition period.
The rules for EHT sounding in 35.7.3 make it clear that only an AP sends EHT NDP Announcement frames that use AID11 identifiers for STAs. It is sufficient to add an additional rule restricting the use of EHT sounding during transition periods.
Recommended text makes no change to the NDP Announcement frame format, but adds a restriction in 35.3.7.4.

## Slide 11: Discussion – Trigger frame
9.3.1.22 Trigger frame format
Based on the changes in TGbeD7.0, a Special User Info field is always present when an EHT User Info field is used. One of the reserved bits in that field can be used by the AP to indicate if the EHT AIDs of EDP non-AP STAs are from the current FA parameter set or from the previous set.
Proposed text defines a currently reserved bit for use to indicate the presence of AIDs from the previous FA parameter set.
Because of the variety of Trigger frames and Trigger frame uses, this change would contain the needed text alterations to a single section versus trying to note the change in all of the different uses.
Alternatively, the AP could be instructed to only use AIDs from the current FA parameter set. This approach would use text similar to the NDP Announcement frame text added to 35.2.1.2.1, 35.2.2.1, and maybe other sections as appropriate.

## Slide 12: Discussion – AID Bitmap element and TIM element with Multi-Link Traffic Indication element
TIM element (9.4.2.5) and AID Bitmap element (9.4.2.328)
Both can be used within Multi-Link Traffic Indication element (9.4.2.325)
These two elements apply to MLD Link recommendation and buffered traffic indication.
AID Bitmap element has a spare bit that could indicate that old AIDs are in use.
Link recommendation (35.3.7.4)
    Includes the AID Bitmap element and ML Traffic Indication element
    Propose to not send this message during transition – though the Link Recommendation frame also contains the AID Bitmap element which could tag the message as either using old or new AIDs
Traffic indication (35.3.12.4)
    Propose to direct the AP MLD to only use the new AIDs in this message because both sides should be able to handle this use.

## Slide 13: Straw Poll
Do you support the text amendments in 24/1511r0 to enable AID management during EDP transition periods?