## Slide 1: Discussions on DRU pilot design principles
Date: 2024-05
Authors:
Name | Affiliation | Address | Phone | Email
Chenchen Liu | Huawei Technologies Co., Ltd | Huawei Base, Bantian, Shenzhen |  | liuchenchen1@huawei.com
Bo Gong |  |  |  | 
Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
DRU pilot design has been extensively discussed in previous contributions [1]~[5]. Based on these discussions, the following principles have been identified
  Equal Pilot Count
  Non-clustered Pilot Distribution/Even Distribution
  Hierarchical Structure
  Frequency Diversity(within one RU)
  Avoiding Impairment Zones
In this presentation, we will also discuss some additional pilot design principles that are intended to enhance performance further

## Slide 3: Recap on the RRU pilot
The pilots of RRU have the following features:
  Uniform Structure: Identical structure across same –sized RRUs through shift and inversion
  Symmetry Around DC: Pilot positions are symmetric around DC from global view
Definition of RU types:
If one RU’s index can be shifted and/or reversed to match another RU’s index, and their data and pilot subcarriers align exactly, then the two RUs are considered the same type.

## Slide 4: Proposed DRU
Benefits of RRU pilot Design:
  Simplified Tone Mapping/Demapping: Reuse of the same tone mapper and demapper across same size RUs, Reducing system complexity
  Streamlined LTF Design: Efficient sequence design for small Rus, concatenated to form complete LTF
  Enhanced System Efficiency: Uniform and symmetric pilot placement lead to enhanced channel estimation accuracy, improve robustness to frequency offset and simplify the signal processing
Given the significant benefits observed in RRU pilot design, it is advisable to adopt similar principles in the design of DRU pilots.
We will explore how there principles can be effectively implemented in DRU pilot design in the following section

## Slide 5: DRU pilot design principles
Non-Uniform Structure Necessity:
  Unlike RRUs, DRUs cannot always adopt a uniform pilot structure. Attempting to do so can result in pilots being squeezed into a local area
  Moreover, some DRU tone plans are inherently non-uniform
Minimizing DRU Types:
  Despite these challenges, it's beneficial to minimize the number of smallest DRU types in the design
  This approach helps in maintaining simplicity while adhering to other pilot design principles, thus optimizing system efficiency
Symmetry Around DC
  Where possible, DRU pilots should be designed to be symmetric around the DC subcarrier
  Symmetry around DC enhances channel estimation accuracy and robustness to frequency offsets, similar to RRU designs
  This principle does not conflict with other design requirements and is feasible for some DRU tone plans

## Slide 6: Proposed DRU Pilot for 20MHz
Pilot indices with DRU tone plan in[6]:
  Option 1: [-107:11:-19, 19:11:107]
  Option 2: [-103:10:-23, 23:10:103]
Relative Pilot Tone Indices for DRU in 20MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  |  | 
26-tone DRU（i=1:9） | DRU 1 (11,24) | DRU 2 (2,15) | DRU 3 (12,25) | DRU 4 (3,16) | DRU 5 (4,18) | DRU 6 (6,19) | DRU 7 (8,21) | DRU 8 (7,20) | DRU 9 (9,23)
52-tone DRU（i=1:4） | DRU 1 (4,21,30,47) |  | DRU 2 (6,23,32,49) |  |  | DRU 3 (11,16,37,42) |  | DRU 4 (13,18,40,45) | 
106-tone DRU（i=1:2） | DRU 1 (7,41,61,95) |  |  |  |  | DRU2 ( 21,31,76,86) |  |  | 
Relative Pilot Tone Indices for DRU in 20MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  |  | 
26-tone DRU（i=1:9） | DRU 1 (4,17) | DRU 2 (8,21) | DRU 3 (6,19) | DRU 4 (10,23) | DRU 5 (2,16) | DRU 6 (5,18) | DRU 7 (9,22) | DRU 8 (7,20) | DRU 9 (11,25)
52-tone DRU（i=1:4） | DRU 1 (7,16,33,42) |  | DRU 2 (11,20,37,46) |  |  | DRU 3 (9,18,35,44) |  | DRU 4 (13,22,40,49) | 
106-tone DRU（i=1:2） | DRU 1 (13,31,67,85) |  |  |  |  | DRU2 ( 17,35,72,90) |  |  | 
Option1
Option2

## Slide 7: Proposed DRU Pilot for 20MHz
Key Features of this pilot Design:
  Adherence to the old principles(same number as RRU, non-clustered, hierarchical structure, relative distance 13 or 14 to make use of frequency diversity, uniform distribution, no pilot in impairment zones)
  The 26-tone DRU types are reduced(same type DRUs are mark with same color in the tables)
  Symmetry around the DC
The pilots for 106-tone DRU can be any 4 out of the 8 pilots for the corresponding two 52-tone DRU

## Slide 8: Proposed DRU Pilot for 40MHz
Pilot indices with DRU tone plan in[6]:[-214:11:-27, 38:11:225]
Key Features of this pilot Design:
  Adherence to the old principles(same number as RRU, non-clustered, hierarchical structure, relative distance 13 for all 26-tone DRU, uniform distribution, no pilot in impairment zones)
  The 26-tone DRU types are reduced(same type are mark with same color)
  Almost symmetry around the DC(only two pilots are not symmetric)
Relative Pilot Tone Indices for dRU in 40MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  |  |  | 
26-tone DRU（i=1:18） | DRU 1 (5,18) | DRU 2 (10,23) | DRU 3 (6,19) | DRU 4 (11,24) | DRU 5 (12,25) |  | DRU 6 (11,24) | DRU 7 (5,18) | DRU 8 (12,25) | DRU 9 (6,19)
 | DRU 10 (8,21) | DRU 11 (2,15) | DRU 12 (9,22) | DRU 13 (3,16) | DRU 14 (7,20) |  | DRU 15 (3,16) | DRU 16 (8,21) | DRU 17 (4,17) | DRU 18 (9,22)
52-tone DRU（i=1:8） | DRU 1 (9,20,35,46) |  | DRU 2 (11,22,37,48) |  |  |  | DRU 3 (10,21,36,47) |  | DRU 4 (12,23,38,49) | 
 | DRU 5 (4,15,30,41) |  | DRU 6 (6,17,32,43) |  |  |  | DRU 7 (5,16,31,42) |  | DRU 8 (7,18,33,44) | 
106-tone DRU（i=1:4） | DRU 1 (17,39,71,93) |  |  |  |  |  | DRU 2 (24,46,78,100) |  |  | 
 | DRU 3 (7,29,61,83) |  |  |  |  |  | DRU 4 (14,36,68,90) |  |  | 
242-tone DRU（i=1:2） | DRU 1 (38,54,87,104,162,178,211,228) |  |  |  |  | DRU 2 (16,32,65,82,139,155,188,205) |  |  |  | 

## Slide 9: Proposed DRU Pilot for 80MHz
Pilot indices with DRU tone plan in[8]:
  Option 1:[ -440, -429, -418, -407, -396, -385, -366, -355, -344, -333, -322, -311, -300, -289 ,-278, -267, -240, -229, -218, -207, -196, -185, -174, -163, -152, -133, -122, -111, -100, -89 , -78 , -67 ,72, 83, 94, 105, 116, 127, 146, 157, 168, 179,190, 201, 212, 223,234,245, 272, 283, 294, 305, 316, 327, 338, 349, 360, 379, 390, 401 , 412 , 423 , 434 , 445 ]
  Option 2:[-449 ,-437, -425 ,-413, -400, -388, -376, -356, -343, -331, -319, -307, -294, -282, -270, -258, -249, -237, -225, -213, -200, -188, -176, -164, -151, -131, -119, -107, -94 , -82 , -70 , -58 ,63 ,75, 87,99 , 112 , 124 , 136, 156 , 169 , 181 , 193 , 205 , 218 , 230 , 242 , 254 , 263 , 275 , 287 , 299 , 312 , 324 , 336 , 348 , 361 , 381 , 393 , 405 , 418 , 430 , 442 , 454]
Option1: Relative Pilot Tone Indices for DRU in 80MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  | 
52-tone DRU（i=1:16） | DRU 1 (5,17,31,43) | DRU 2 (10,22,36,48) | DRU 3 (13,25,39,51) | DRU 4 (7,19,33,45) | DRU 5 (6,18,32,44) | DRU 6 (11,23,37,49) | DRU 7 (9,21,35,47) | DRU -8 (3,15,29,41)
 | DRU 9 (7,19,33,45) | DRU 10 (12,24,38,50) | DRU 11 (4,16,30,42) | DRU 12 (9,21,35,47) | DRU 13 (8,20,34,46) | DRU 14 (2,14,28,40) | DRU 15 (11,23,37,49) | DRU 16 (5,17,31,43)
106-tone DRU（i=1:8） | DRU 1 (20,45,74,98) |  | DRU 2 (25,50,79,103) |  | DRU 3 (11,35,64,89) |  | DRU 4 ( 6,30,59,84) | 
 | DRU 5 (24,49,78,102) |  | DRU 6 (18,43,72,96) |  | DRU 7 (4,28,57,82) |  | DRU 8 (10,34,63,88) | 
242-tone DRU（i=1:4） | DRU 1 (48,59,98,109,168,179,218,229) |  |  |  | DRU 2 (18,29,68, 79,138,149,188,199) |  |  | 
 | DRU 3 (45,56,95,106,165,176,215,226) |  |  |  | DRU 4 (15,26,65,76,135,146,185,196) |  |  | 
484-tone DRU（i=1:2） | DRU 1 (36,58,95,117,136,158,195,217,276,298,335,357,376,398,435,457) |  |  |  | DRU 2 (30,52,89,111,130,152,189,211,270,292,329,351,370,392,429,451) |  |  | 

## Slide 10: Proposed DRU Pilot for 80MHz
Key Features of this pilot Design:
  Adherence to the old principles(same number as RRU, non-clustered, hierarchical structure, relative distance the same for all 52-tone DRU, near uniform distribution, no pilot in impairment zones)
  The 52-tone DRU types are reduced(same type are mark with same color)
  Option2 spans a slightly larger range than option1
Option2: Relative Pilot Tone Indices for DRU in 80MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  | 
52-tone DRU（i=1:16） | DRU 1 (10,22,36,48) | DRU 2 (8,20,34,46) | DRU 3 (9,21,35,47) | DRU 4 (10,22,36,48) | DRU 5 (2,14,28,40) | DRU 6 (3,15,29,41) | DRU 7 (3,15,29,41) | DRU -8 (4,16,30,42)
 | DRU 9 (13,25,39,51) | DRU 10 (11,23,37,49) | DRU 11 (12,24,38,50) | DRU 12 (13,25,39,51) | DRU 13 (5,17,31,43) | DRU 14 (6,18,32,44) | DRU 15 (6,18,32,44) | DRU 16 (7,19,33,45)
106-tone DRU（i=1:8） | DRU 1 (16,40,70,94) |  | DRU 2 (20,45,74,98) |  | DRU 3 (3,27,56,81) |  | DRU 4 (8,32,61,86) | 
 | DRU 5 (22,47,76,100) |  | DRU 6 (26,51,80,104) |  | DRU 7 (9,33,62,87) |  | DRU 8 (14,38,68,92) | 
242-tone DRU（i=1:4） | DRU 1 (40,49,88,99,160,169,208,219) |  |  |  | DRU 2 (13,22,63,72,133,142,183,192) |  |  | 
 | DRU 3 (52,61,102,111,172,181,222,231) |  |  |  | DRU 4 (25,36,75,84,145,156,195,204) |  |  | 
484-tone DRU（i=1:2） | DRU 1 (26,44,79,97,126,144,175,197,266,284,319,337,366,384,415,437) |  |  |  | DRU 2 (50,72,103,121,150,168,203,221,290,312,343,361,390,408,443,461) |  |  | 

## Slide 11: Summary
Introduction of New Principles: We proposed two additional DRU pilot design principles that complement existing guidelines without conflicting with them. These principles enhance the design's robustness and efficiency.
Practical Design Solutions: Our proposal includes detailed DRU pilot designs tailored for 20MHz, 40MHz, and 80MHz bandwidths. These designs adhere to both the newly introduced and existing principles.

## Slide 12: References
[1] 11-23-1115-00-0uhr-cfo-impact-and-pilot-design-for-dru
[2] 11-23-1447-00-0uhr-cfo-impact-and-pilot-design-for-dru-follow-up
[3] 11-23-1511-01-0uhr-pilot-tone-allocation-and-other-considerations-of-tone-distributed-rus-for-uhr
[4] 11-24-0402-01-00bn-20-mhz-tone-plan-and-pilot-design-for-dru
[5] 11-24-0501-02-00bn-pilot-design-considerations-for-dru
[6] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[7] IEEE P802.11be™/D5.0
[8] 11-24-0799-00-00bn-DRU-Tone-Plan-from-the-perspective-of-PAPR

## Slide 13: SP1
Do you agree to reduce the DRU types of smallest DRU size for all the spreading BW?

## Slide 14: SP2
Do you agree to DRU pilots should be designed to be symmetric around the DC subcarrier where possible?

## Slide 15: Appendix：DRU Pilot for 80MHz tone plan in ref[6]
Pilot indices with DRU tone plan in[6]:
  Option 1:[-452 ,-437, -426, -411, -400, -389, -374, -363, -352, -337, -326, -315, -300, -289, -278, -263, -236, -221, -210, -195, -184, -173, -158, -147, -136, -121, -110, -99 , -84 , -73 , -62 , -47 , 48, 63,74 ,89, 100, 111, 126, 137 , 148 , 163 , 174 , 185 , 200 , 211 , 222 , 237 , 264 , 279 , 290 , 305 , 316 , 327 , 342 , 353 , 364,379, 390, 401, 416, 427, 438, 453]
  Option 2:[-461, -445, -433, -421, -404, -392, -380, -364, -351, -335, -323, -311, -294, -282, -266, -254, -245, -229, -217, -205, -188, -176, -164, -148, -135, -119, -107, -95 , -78 , -66 , -50 , -38 , 39, 55, 67, 79 ,96 , 108 , 120, 136 , 149 , 165 , 177 , 189 , 206 , 218 , 234 , 246 , 255 , 271 , 283 , 295 , 312 , 324 , 336 , 352 , 365 , 381 , 393 , 405 , 422 , 434 , 450 , 462]
Option1: Relative Pilot Tone Indices for DRU in 80MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  | 
52-tone DRU（i=1:16） | DRU 1 (5,17,31,43) | DRU 2 (10,22,36,48) | DRU 3 (13,25,39,51) | DRU 4 (7,19,33,45) | DRU 5 (6,18,32,44) | DRU 6 (11,23,37,49) | DRU 7 (9,21,35,47) | DRU -8 (3,15,29,41)
 | DRU 9 (7,19,33,45) | DRU 10 (12,24,38,50) | DRU 11 (4,16,30,42) | DRU 12 (9,21,35,47) | DRU 13 (8,20,34,46) | DRU 14 (2,14,28,40) | DRU 15 (11,23,37,49) | DRU 16 (5,17,31,43)
106-tone DRU（i=1:8） | DRU 1 (21,45,73,97) |  | DRU 2 (26,50,78,102) |  | DRU 3 (12,36,64,88) |  | DRU 4 (7,31,59,83) | 
 | DRU 5 (25,49,77,101) |  | DRU 6 (19,43,71,95) |  | DRU 7 (5,29,57,81) |  | DRU 8 (11,35,63,87) | 
242-tone DRU（i=1:4） | DRU 1 (47,60,101,114,164,177,218,231) |  |  |  | DRU 2 (16,28,70,82,133,145,187,199) |  |  | 
 | DRU 3 (44,56,98,110,161,173,215,227) |  |  |  | DRU 4 (12,25,66,79,129,142,183,196) |  |  | 
484-tone DRU（i=1:2） | DRU 1 (32,56,93,119,140,164,201,227,266,290,327, 353,374,398,435,461) |  |  |  | DRU 2 (24,50,87,111,132,158,195,219,258,284,321,345,366,392,429,453) |  |  | 

## Slide 16: Appendix：DRU Pilot for 80MHz tone plan in ref[6]
Option2: Relative Pilot Tone Indices for DRU in 80MHz (start tone index is 1) Hierarchical Structure |  |  |  |  |  |  |  | 
52-tone DRU（i=1:16） | DRU 1 (10,22,36,48) | DRU 2 (8,20,34,46) | DRU 3 (9,21,35,47) | DRU 4 (10,22,36,48) | DRU 5 (2,14,28,40) | DRU 6 (3,15,29,41) | DRU 7 (3,15,29,41) | DRU -8 (4,16,30,42)
 | DRU 9 (13,25,39,51) | DRU 10 (11,23,37,49) | DRU 11 (12,24,38,50) | DRU 12 (13,25,39,51) | DRU 13 (5,17,31,43) | DRU 14 (6,18,32,44) | DRU 15 (6,18,32,44) | DRU 16 (7,19,33,45)
106-tone DRU（i=1:8） | DRU 1 (17,41,69,93) |  | DRU 2 (21,45,73,97) |  | DRU 3 (4,28,56,80) |  | DRU 4 (9,33,61,85) | 
 | DRU 5 (23,47,75,99) |  | DRU 6 (27,51,79,103) |  | DRU 7 (10,34,62,86) |  | DRU 8 (15,39,67,91) | 
242-tone DRU（i=1:4） | DRU 1 (38,48,92,102,155,165,209,219) |  |  |  | DRU 2 (10,20,64,74,127,137,181,191) |  |  | 
 | DRU 3 (52,62,106,116,169,179,223,233) |  |  |  | DRU 4 (24,34,78,88,141,151,195,205) |  |  | 
484-tone DRU（i=1:2） | DRU 1 (20,40,75,95,128,148,183,203,254,274,309,329,362,382,417,437) |  |  |  | DRU 2 (48,68,103,123,156,176,211,231,282,302,337,357,390,410,445,465) |  |  |