## Slide 1: The Transmission of Preemption Request Frame
Date: 2024-04-26
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
A uniform preemption procedure is proposed in doc 11-24/0390r0;
For simplicity, the preemption allowed PPDU without a response frame is used in the illustrations;
The potential procedures when the response frame exists will be discussed in this presentation.
PR: Preemption Request frame

## Slide 3: Issues When A Response Frame Exists
Hidden node issue between two different associated STAs in same BSS may exists;
When the AP transmits preemption allowed PPDU to STA1 and STA1 reply a response frame
  STA 2 can receive both the PPDU and the response frame
  STA 3 can only receive the PPDU
  When STA 3 send a PR frame, STA1 can not receive the PR frame
When STA 1 transmits preemption allowed PPDU to AP and the AP reply a response frame
  STA 2 can receive both the PPDU and the response frame
  STA 3 can only receive the response frame
  When STA 3 send a PR frame, STA1 can not receive the PR frame
There are two options in high level
  Option 1: PPDU / Response frame / PR frame
  Option 2: PPDU / PR frame / Response frame

## Slide 4: Option 1: PPDU/Response frame/PR frame
Different MAC frame can be carried in the preemption allowed PPDU, it is hard for a low latency (LL) STA to determine whether a response frame exists based on the MAC contents of the preemption allowed PPDU
  Also, some new MAC frames may be introduced after 11bn, so a 11bn LL STA can not understand these new MAC frames
An explicit response indication in the preemption allowed PPDU will help the LL STAs to know whether a response frame follows;
Below are some potential sub-options:
  Opt 1a: the LL STAs that receive the PPDU can send PR
  Opt 1b: the LL STAs that receive the response frame can send PR
  Opt 1c: the LL STAs that receive both the PPDU and the response frame can send PR

## Slide 5: Option 1: PPDU/Response frame/PR frame
Opt 1a: the LL STAs that receive the PPDU can send PR
Due to the exists of response frame, the LL STAs need to identify the length of response frame and then send PR after response frame;
It is easy for a LL STA that can directly receive response frame;
For a LL STA that hidden from response frame, it needs a way to identify the length of response frame
  Base on the content in preemption allowed PPDU? E.g. A Manage frame will solicit a ACK; an A-MPDU with Ack Policy set to 0 will solicit a BA. It is complex to understand all MAC frames types, and not easy to determine the length of a response frame when it has a variable length;
  The explicit indication of the duration of response frame will make it easy for a LL STA, but will cause some signaling overhead;
  Hard to know whether failure happens for the response frame.

## Slide 6: Option 1: PPDU/Response frame/PR frame
Opt 1b: the LL STAs that receive the response frame can send PR
Need to add preemption allow indication in response frame;
Some response frame (e.g. ACK and CTS) only carry RA field, may not able to be identified as a inter-BSS PPDU or intra-BSS PPDU;
When a LL STA that send PR is hidden from the PPDU, the TXOP holder who transmitted the PPDU can not aware of the PR frame.

## Slide 7: Option 1: PPDU/Response frame/PR frame
Opt 1c: the LL STAs that receive both PPDU and response frame can send PR
This solution is simple;
A LL STA that hidden from the PPDU or the response frame can not send PR;
But remember that hidden node STAs also exist in Opt 1a and Opt 1b;
An Opt 1d that allow the STAs receive either the PPDU or the response frame send PR can allow all LL STA in the BSS get a chance to send PR. But this option looks not realistic, it is too complex.

## Slide 8: Option 2: PPDU/PR frame/Response frame
For the case of DL PPDU and UL response frame, the STA transmit response frame and the LL STA may hidden from each other;
  After transmit the preemption allowed PPDU, the AP need to send a poll frame to solicit the response frame; Or,
  The response STA directly send response frame if no PR frame is received. In that case, AP decodes the PR frame or response frame base on frame capture. Because both frames are robust control frames, the frame with higher RSSI may be correctly received.
For the case of UL PPDU and DL response frame, the AP can hear all associated STA, so the AP will send response frame only when no PR frame is received
  The LL STAs that hidden from the STA transmitted UL PPDU will not have a chance to send PR

## Slide 9: Summary
How to transmit a preemption request frame is discussed when the preemption allowed PPDU with a response frame;
Hidden node issue is a main consideration for the procedure design;
Some details are provided for each potential procedures for discussion.