## Slide 1
SCS proxy for Relay
Name | Affiliations | Address | Phone | Email
Yan Li | ZTE |  |  | li.yan16@zte.com.cn
Yurong Qian |  |  |  | 
Jay Yang |  |  |  | 
Yaodong Zhang |  |  |  | 
Date: 2024-07-20
Authors:

## Slide 2
Introduction
The main objectives within the scope of 11bn are to
  improve reliability
  increase throughput at different SNR levels (Rate-vs-Range)
  reduce latency, etc. [1]
There have been several contributions discussing the significant role of relays in enhancing RvR throughput. [2] – [8]
SCS enables the AP to classify and handle specific MSDUs based on parameters provided by the STA, significantly improving QoS for real-time applications.
In this contribution, we present our insights on QoS management for relay to enhance the relay operation of 11bn.

## Slide 3
Problem statement 1
As an intermediate node, relay lacks explicit knowledge of the traffic classification and QoS requirement of STA.
  In 11bn relay operation, relay performs only partial MAC processing functions. [2]
  STA associates with AP while utilizing DF(decode forward) Relay functionality through the relay.
  SCS agreement is established between the associated AP and STA, while the relay operates without knowledge of the traffic classification and QoS requirements for the SCS stream.
  The traffic transmission across the two links between the AP and the relay, and between the relay and the STA, needs to collectively ensure the QoS requirements of the traffic.
  Relay serves other STAs to extend their range while simultaneously managing its own traffic as a regular STA. [3]
  Relays struggle to ensure the QoS requirements of SCS stream.

## Slide 4
Problem statement 2
This issue typically arises in cross-link relay architectures.
  MLO is applied on the relay, utilizing different links for backhaul and fronthaul in relay operation [4-6].
  Relay needs to reliably schedule STAs' SCS streams on the fronthaul link to meet QoS requirements.

## Slide 5
Proposal
Relay should be aware of the traffic classification and QoS requirements of the SCS streams of STA.
Method 1: AP, in behalf of STA, proxy negotiates with relay for SCS streams between relay and STA.
AP sends a Proxy SCS Request frame to relay, providing details about the STA's SCS agreement.
The frames should include essential information, such as proxy SCS indicator, Proxy STA MAC address or AID, SCS stream parameters for the link between the relay and STA.
Method 2 : AP notifies the relay of established SCS agreement between AP and STA.
  Relay may schedule the fowarded frames based on the SCS agreement notified by the AP
  Especially for relay candidates(opportunistic relay)[9], it reduces the overhead of frequent establishment and torn-down of SCS agreement between STA and relay as Method 1 proposed

## Slide 6
Proposal (cont’d)
For Proxy SCS stream(method 1), it should keep consistent with the lifetime of corresponding SCS stream
  if SCS stream is terminated, the corresponding proxy SCS stream should also be terminated
Case 1: termination initiated by AP
Case 2: termination initiated by relay
Case 3: termination initiated by STA

## Slide 7: Summary
The contribution presents some insights on QoS management for relay to enhance the relay operation of 11bn.
It is recommended to ensure that relay is aware of the traffic classification and QoS requirements of the established SCS stream of STA, and provides two methods for QoS management on relay
  proxy SCS negotiation
  notify SCS agreement

## Slide 8
THANK YOU

## Slide 9: Reference
[1] 23/0480r3, UHR proposed PAR
[2] 24/0385r1, Discussion on 11bn Relay Operation
[3] 23/1955r0, Considerations for Relay Operation in Next Generation Wi-Fi Networks – Part 3
[4] 23/1840r0, Relay for 11bn
[5] 23/1969r0, Consideration on UHR Relay Architecture
[6] 24/0074r1, Relay Operation Follow-up
[7] 23/2217r1, some thoughts on relay improvement
[8] 27/1175r0, UHR relay follow up
[9] 24/0650r1, A case for opportunistic relaying