## Slide 1: Adapted Trigger based uplink transmission follow up
Date: 2024-05-06
Authors:

## Slide 2: Recap
In [1], we have discussed the spectrum underutilization issue for trigger based uplink transmission.
Once only one portion of the assigned RU is busy, then the whole assigned RU can’t be used for transmission
Take the following transmission for example, the whole 996+484 tone MRU at the STA 1 will be wasted just because 484 tone RU is busy.
Trigger
160 MHz
STA 1, 996-tone
STA 2, 484-tone
STA 1, 484-tone
Idle
busy
Idle

## Slide 3: Recap Cont.
In [2], we proposed to
  focus on large RU/MRU that is assigned for uplink transmission given that the CCA is 20 MHz channel based
  consider limited combinations that exclude busy 242-tone RU such that to maintain same U-SIG for each 20 MHz in an 80 MHz
  In this contribution, we continue to provide more details and clarify how it works
RU/MRU greater than 242-tone
484+242-tone
996+484-tone
996+484+242-tone
2*996
2×996+484-tone
3×996-tone
3×996+484-tone
4×996-tone
Other RUs: 484-tone and 996 tone

## Slide 4: Adapted TB Uplink Transmission
We propose limited MRU/RU pattern for adapted TB uplink transmission
  The limited MRU/RU is greater than 996-tone
  Proposed adapted TB PPDU only happens when only 996, 2*996 or 3*996 is idle within the limited MRU/RU
MRU | Note
484+242-tone | Non-OFMDA, OFDMA
996+484-tone | Non-OFMDA, OFDMA
996+484+242-tone | Non-OFMDA
2*996 | Non-OFMDA, OFDMA
2×996+484-tone | Non-OFMDA, OFDMA
3×996-tone | Non-OFMDA, OFDMA
3×996+484-tone | Non-OFMDA, OFDMA
4×996-tone | Non-OFMDA, OFDMA
Other RUs | 242-tone, 484-tone, 996-tone*

## Slide 5: Adapted TB Uplink Transmission
To keep the same U-SIG in each 20 MHz of an 80 MHz segment, we propose to provide explicit signaling to support adapted TB uplink transmission
  Add puncture info in U-SIG
  For example, 4-bit bitmap where each bit represents 80 MHz
If the whole MRU/RU is used, then the bitmap is set to all “0”- default value

## Slide 6: Summary
In this contribution, we propose explicit signaling to support adapted TB uplink transmission within limited RU/MRU
  4-bit bitmap puncture info where each bit represents 80 MHz

## Slide 7: References
[1] 11-23-1967-00-00bn-trigger-based-uplink-adapted-transmission

## Slide 8: SP
Do you agree to allow that the STA responds with the TB PPDU to its received Trigger frame on part of the assigned RU/MRU based on CCA results?