## Slide 1: Design target and device capabilities for AMP IoT
Date: 2024-05-10
Authors:
Name | Affiliation | Address | Phone | Email
Weijie Xu | OPPO |  |  | xuweijie@oppo.com
Yinan Qi |  |  |  | v-qiyinan@oppo.com
Chuanfeng He |  |  |  | 
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 2: Abstract
This submission is to discuss the design target of AMP IoT and the device capabilities of AMP client STA.
Doc.: IEEE 802.11-24/0853r0

## Slide 3
Background: The target of the study[1]
 | RFID | AMP IoT | Existing WLAN IoT(e.g. 802.11 ah)
Coverage | <10 m | 10m~30m (RF power); Up to 200m(other ambient power) | >=1000m
Power Source | RF power only | Various ambient power | Battery
Techniques | RF power harvesting Backscattering | Backscattering/Active transmitter WUR receiver Enhanced power saving Power management | OFDM/Narrow bandwidth Relaxed processing eDRX(TWT) PS-Poll Energy limited operation
Power Consumption | 1uw~10uw | <1mw | 100x mw
Device Cost (Relatively) | Low | Medium | High
Maintenance/operation cost | Labor cost for operation | Maintenance-free Automated operation | Replace/Recharge the battery/Automated operation
Weijie Xu (OPPO)
Slide 3
Doc.: IEEE 802.11-22/1960r2
November 2022
During TIG and SG, the design target of AMP IoT is proposed: AMP IoT should aim for the use cases that can’t fully addressed by existing technologies.

## Slide 4
Use cases and requirements
  Based on previous discussion during the TIG and SG phase, mainly 3 different use case scenarios have been identified for Ambient IoT.
  Use case scenario 1: Short/medium range Ambient IoT[2][3][4][5][6][7][8][9]
    Coverage: 10m~100m
    Need to process hundreds of AMP device each seconds
  Use case scenario 2: Close range Ambient IoT[10]
    Coverage: 20cm~50cm
    Process one AMP device at one time
  Use case scenario 3: Compatible Ambient IoT[11]
    Coverage: 10m~100m
    Be able to communicate with legacy WiFi network
Weijie Xu (OPPO)
Slide 4
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 5
What will differentiate Ambient IoT with existing technologies
  Compared with existing WALN IoT technologies: Battery-less, ultra-low complexity, small size, maintenance-free device etc.
  Compared with RFID:
    Potential longer range, via using
      Advanced techniques such as reflection amplifier, spreading, UL coding etc.
      Energy storage ( which help can lower energy harvesting threshold)
      Other kinds of ambient power such as light, heat etc.
      Higher sensitivity receiver (with different receiver Arch.)
    Potential higher system capacity/system efficiency
      Techniques such as FDM/CDM
      Higher peak data rate?
    Lower deployment cost
      Low-complexity AMP AP (e.g. by avoiding full-duplex operation)
    Enable more application, e.g. can link ambient IoT device with a smart phone
Weijie Xu (OPPO)
Slide 5
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 6
Key capabilities of AMP STA
  The following capabilities are important for AMP STA:
    Receiver architecture
    Supported uplink transmission mechanism
    Supported waveform
    Whether have Energy storage
    Whether have Reflection amplifier
    Clock accuracy
Weijie Xu (OPPO)
Slide 6
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 7
DL receiver
  Generally, two receiver architectures can be used for Ambient IoT
    Option 1: RF envelope detector (RF ED)
      The receiving bandwidth can be tens of MHz. It is applicable with the existing WUS which has 4MHz signal bandwidth and 8MHz guard band on both lower and higher sides
      The achievable receiver sensitivity is -45~-35dBm, which is better than energy harvesting
      The power consumption is several µW
Weijie Xu (OPPO)
Slide 7
Doc.: IEEE 802.11-24/0853r0
May 2024
Figure: RF envelope detector

## Slide 8
DL receiver
    Option 2: (Zero) IF Receiver
      Applicable using existing WUS design, and have much better receiver sensitivity, e.g. lower than -Y dBm. Y can be smaller than 82 in order to further reduce the complexity of receiver compared with 11ba WUR.
      The power consumption is hundreds of µW
  Both of RF envelope detector and (Zero) IF Receiver can be used for ambient IoT. Which one is used can be determined based on the applicable ambient power and the required coverage.
Weijie Xu (OPPO)
Slide 8
Doc.: IEEE 802.11-24/0853r0
May 2024
Figure: (Zero) IF Receiver

## Slide 9
UL transmission
  Generally, two transmission mechanisms for Ambient IoT uplink.
    Option 1: Backscattering
      Option 1-1: without reflection amplifier
        The power consumption is several µW
      Option 1-2: with reflection amplifier
        The power consumption is hundreds of µW, dominated by that of reflection amplifier
    Option 2: Active transmission
      Power amplifier and local oscillator are needed
      The power consumption is several hundreds of µW
  Although the power consumption of Option 2/1-2 is higher than that of Option 1-1, it is still feasible for most of the use cases since uplink transmission is duty-cycle based and only take a very few percentage of whole operation time of the device.
Weijie Xu (OPPO)
Slide 9
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 10
Link budget
  Observation: In case of WPT@920MHz and backscattering communication @2.4GHz, reflection amplifier is needed.
Weijie Xu (OPPO)
Slide 10
Doc.: IEEE 802.11-24/0853r0
May 2024
WPT@920MHz, backscattering@2.4GHz | 
WPT Frequency | 920MHz
EIRP of Energizer (dBm) | 33
Communication frequency | 2.4GHz
EIRP of carrier wave@2.4GHz (20dBm) | 20
Receiver sensitivity of AMP AP (dBm) | -95 (Note 1)
Antenna gain of AMP STA (dBi) | 2
Shadowing factor | 3dB@920MHz 4dB@2.4GHz
Minimum receiving WPT power @AMP STA (dBm) | -20
Maximum WPT distance(m) | 10.33
Backscattering loss at IoT device (dB) | 5
Maximum Backscattering distance (m) without reflection amplifier@ Maximum WPT distance | 1.92
Gain of reflection Amplifier factor (dB) | 15
Maximum Backscattering distance (m) without reflection amplifier@ Maximum WPT distance | 10.78

## Slide 11
Reflection amplifier
  Based on theoretical analysis and practical experiment, the achievable maximum gain of reflection amplifier is 10~15dB. It will become unstable with higher gain.
Weijie Xu (OPPO)
Slide 11
Doc.: IEEE 802.11-24/0853r0
May 2024
Figure : reflection Amplifier
(15dB gain, Power consumption:100uw[12])

## Slide 12
Waveform
  Different AMP STA device may have the capabilities to support different waveforms, especially in the uplink. While taking the difference of device capabilities into account, it needs to try to achieve a harmonized waveform as much as possible as proposed in [16].
    In DL, MC-OOK is suitable for all devices.
    In UL, OOK will be suitable for AMP STA in close range AMP IoT and short/medium range AMP IoT.
    For legacy-compatible AMP IoT, OFDM can be used for both DL and UL after wake-up.
Weijie Xu (OPPO)
Slide 12
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 13
Energy storage
  For close range Ambient IoT, no need to have dedicated energy storage. The instant harvested power is sufficient to drive the AMP STA.
    DL data signal or DL carrier wave signal needs to be continuously send to the AMP STA to guarantee continuous power transfer.
      Instant/temporal (e.g. several us) power interrupt due to MC-OOK ON-OFF switch or channel fading can be tolerated by AMP STA since there is tiny capacitor in the energy harvesting circuit
  For short/medium range Ambient IoT and compatible Ambient IoT, dedicated energy storage is needed[13].
    It can help to collect very weak ambient power and boost the peak power for AMP STA.
    It extend the coverage when RF power is used by lowering the energy threshold.
    The capacity of energy storage may depend on the type of ambient power, traffic period, coverage etc. It will based on implementation.
Weijie Xu (OPPO)
Slide 13
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 14
Clock accuracy of AMP STA(1)
  Due to the limited complexity and power consumption, the clock accuracy of AMP STA is worse than that of a legacy WLAN devices(20ppm). In addition, the clock accuracy of RFID device is 10^4~10^5 ppm[14]. The clock accuracy of 11ba WUR is 200ppm.
  Since the clock accuracy at the reader side can be guaranteed, the DL signal can provide clock reference for AMP STA to receive DL signal. For UL transmission, the device needs to generate the clock itself.
    Therefore, the required clock accuracy for DL receiving and UL transmission may be different.
Weijie Xu (OPPO)
Slide 14
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 15
Clock accuracy of AMP STA(2)
  For DL, for two different receiver types, the required clock accuracy will be different.
      For RF ED, although the initial clock accuracy can be 10^4~10^5, which is similar as that of RFID, AMP STA can still derive clock based on DL signal (e.g. based on its raising and falling edge of OOK signal, similar as RFID’s implementation)
      For IF Rx, when receiving, a relatively good clock accuracy is needed for the AMP STA to convert the RF signal to an IF signal. 10^3 ppm is proposed.
        10^3 ppm corresponds to a maximum frequency shift of 2.4MHz, the receiver sensitivity degradation (about 3dB due to doubled noise power) is acceptable considering the bandwidth of WUS is 4MHz.
        Compared with the 200ppm of 11ba WUR, it can further reduce the implementation requirement and the power consumption.
          It may slightly affect DL receiver sensitivity, but AMP IoT doesn’t have to achieve the same coverage of legacy WiFi.
Weijie Xu (OPPO)
Slide 15
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 16
Clock accuracy of AMP STA(3)
  For AMP STA uplink transmission, the following clock accuracy is proposed:
    For close range use case, clock accuracy (i.e. SFO) is 10^4~10^5 ppm
      For AMP and RFID dual-mode device, reasonable to follow the capability of RFID device[11].
    For short/medium range Ambient IoT, clock accuracy is <10^3 ppm
      Based on the proposed value in [15] and the practical experience, it is very feasible to achieve such accuracy with some calibration method and only very few power consumption for calibration.
    For legacy-compatible AMP IoT,
      For main radio, reuse 20ppm or one relaxed value (to reduce the power consumption) can be considered.
      For WUR to receive the wake-up signal, clock accuracy is <10^3 ppm or 200ppm.
Weijie Xu (OPPO)
Slide 16
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 17
Summary of device capabilities of AMP client STA
Weijie Xu (OPPO)
Slide 17
Doc.: IEEE 802.11-24/0853r0
May 2024
Use case | Short/Medium range AMP IoT |  | Close range AMP IoT | Compatible AMP IoT (i.e. 11n compatible)
UL Transmitter | Active Tx | Backscattering | Backscattering | Legacy OFDM Tx
UL Amplifier | Y(May) | Y (Reflection) | N | Y(Legacy)
DL Amplifier | Y(May) | Y(May) | N | Y(Legacy)
RF ED Rx：Sens. of ~-40dB | Y(Opt 1) | Y(Opt1) | Y | Y for wake-up
(Zero-) IF Rx: sens. of ~-70dB | Y(Opt 2) | Y(Opt2) | N | OFDM receiver after wake-up
Energy storage | Y | Y | N | Y
Clock accuracy | IF Rx and UL:<10^3 ppm RF ED :10^4~10^5 ppm |  | 10^4~10^5 ppm | <10^3 ppm for WUR ~20ppm for MR
Waveform | DL: MC-OOK UL:OOK/BPSK |  |  | MC-OOK for wake-up, then OFDM
Power consumption | 100X µW | 100X µW | X µW | X mW~10X mW

## Slide 18
Summary and proposals
  Propose to support the following PHY modes in 802.11bp with the device capabilities in slides 17:
    One low power receiving mode with Rx sensitivity of [-40]dB or [-70]dB
      SFO can be 10^4~10^5 ppm or <10^3 ppm
    One low power active transmission mode with uplink CFO(carrier frequency offset) of <10^3 ppm
    One backscattering mode with uplink SFO of 10^4~10^5 ppm or <10^3 ppm
Weijie Xu (OPPO)
Slide 18
Doc.: IEEE 802.11-24/0853r0
May 2024

## Slide 19: Reference
IEEE 802.11-22/1960r6
IEEE 802.1122/1339r0, Use Cases of smart manufacturing
IEEE 802.1122/1341r1, Use Cases of Data Center Infrastructure Management.
IEEE 802.11-22/0963r0, Use Cases for AMP IoT Devices.
IEEE 802.11-22/1559, Updated Use Cases for AMP IoT Devices.
IEEE 802.11-22/1800r0, New Use Case for AMP IoT Devices: Smart Grid
IEEE 802.11-22/2133r0, New Use Case for AMP IoT Devices
IEEE 802.11-23/1192r0 Distributed Microphone Smart Home Application for AMP IoT devices
IEEE 802.11-23/1521r0 AMP Use Case in Smart Photovoltaics
IEEE 802.11-23/2038r0 Close-range AMP Backscattering in 2.4GHz
IEEE 802.11-23/1195r0 Thoughts on AMP IOT and PAR
IEEE 802.11-22/1893r0 Ambient Power Enabled IoT Technologies
IEEE 802.11-22/1799r0 On energy harvesting and the differentiation with RFID
Specification for RFID Air Interface Protocol for Communications at 860 MHz – 960 MHz
IEEE 802.11-23/1140r0 Considerations for AMP Devices
IEEE IEEE 802.11-24/0849r0 Harmonization of Waveform
Doc.: IEEE 802.11-24/0853r0
May 2024