## Slide 1: Coexistence considerations of AMP data communication
Date: 2024-xx-xx
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
There are still many topics in AMP SG are not clear. For example, power storage, channel access mechanism, wake-up mechanism, bandwidth of the AMP PPDU, or synchronize patterns designs.
In our previous contribution [1] in AMP SG. We strongly suggested that the amendment shall provide coexistence with deployed devices compliant with IEEE802.11.
In this presentation, we will review some contributions from AMP SG and discuss our thought on coexistence with IEEE802.11 STAs operating at 2.4GHz.

## Slide 3: Recap: AMP PAR [2]
  Operation in sub-1 Gigahertz (GHz) and 2.4 GHz is defined. Specifically, at least one mode of data communication in the sub-1 GHz band is defined and at least one mode of data communication in the 2.4 GHz band with the AMP communication access category (AC) being set to AC_BK (background) is defined. At least one mode of wireless power transfer in the sub-1 GHz band is defined to support RF energy harvesting.
  This amendment defines mechanisms for the coexistence of an AMP STA and deployed STAs compliant with IEEE Std 802.11™-2020 that operate in the same radio frequency band as the AMP STA.
  Wireless power transfer is out of 2.4GHz. However, the PAR language of 2.4GHz data communication is still very broad.

## Slide 4: Contributions related to spoofing preamble
In [3], DL/UL are using the existing IEEE802.11 standards, e.g., 11b/n. Additional wake up link need to be standardized.
In [4], DL applies IEEE802.11ba-like design and UL applies OOK/PSK/FSP/DSSS.
In [5], DL using 11b/OFDM waveforms, which are more like an energy (or carrier) source for backscattering signal.
WUR PHY was reviewed in [6,7].
Under current discussions, consensus seems can be reached is that DL PPDU needs to includes a spoofing preamble.
For DL data communication, we suggest IEEE802.11ba-like PPDU as well.
For UL, we also suggest that IEEE802.11bp transmissions at 2.4GHz carry a backward compatible preamble.

## Slide 5: Summary
We review some AMP SG contributions and proposed our prefer schemes for a better coexistence in 2.4GHz.
DL waveforms should include spoofing preamble. For data communication in 2.4GHz, we suggest a IEEE802.11ba-like PPDU.
We suggest to apply the existing IEEE802.11 standards, e.g., 11b/n, for UL data communication as a starting point.

## Slide 6: SP1
Do you agree to define a IEEE802.11ba-like PPDU as the AMP DL PPDU for data communication?
  IEEE802.11ba-like PPDU consists of a 20MHz spoofing preamble, and a narrow band portion using OOK.

## Slide 7: SP2
Do you agree that IEEE802.11bp UL transmissions at 2.4GHz also carry a backward compatible preamble?

## Slide 8: References
[1] 11-23/1534r1, Discussion on AMP IoT PAR, You-Wei Chen, et al.
[2] p802.11bp-PAR
[3] 11-23/1195r0, Thoughts on AMP IOT and PAR, Bin Tian and Steve Shellhammer.
[4] 11-23/1190r4, Further Discussion on AMP PAR, Yinan Qi and Weijie Xu.
[5] 11-24/537r0, Close-range AMP WiFi Reader Feasibility Study, Rui Cao, et al.
[6] 11-24/0452r0, Overview of the 802.11ba PHY, Steve Shellhammer et al.
[7] 11-24/56r0, How 802.11ba Handled SNR, Steve Shellhammer et al.