## Slide 1: AMP DL PPDU consideration
Date: 2024-05-10
Authors:
Name | Affiliations | Address | Phone | Email
You-Wei Chen | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | You-Wei.Chen@mediatek.com
Jianhan Liu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Introduction
Under current AMP discussions, one general consideration is to apply 802.11ba-like PPDU format for DL [1]. And thus, spoofing preamble is applied.
802.11ba PHY was overviewed in the previous meeting [2]. Some BPSK-marks related questions were discussed.
In this presentation, we try to review the history of BPSK-marks and would like to discuss our thought on DL PPDU format.

## Slide 3: Recap: 802.11ba DL PPDU [2]
L-STF
20MHz
L-LTF
L-SIG
BPSK-Mark1
BPSK-Mark2
AMP-SIG
WUR package
4MHz
802.11 spoofing
OFDM format
OOK format
PHY header
MAC header
payload
FCS
20MHz OFDM spoofing preamble + 4MHz MC-OOK package.

## Slide 4: Recap: BPSK-Marks consideration
Initially, only BPSK-mark1 is added. The design target of BPSK-mark1 is used to spoof 802.11 STAs to treat 802.11ba PPDU as 802.11a PPDU.
Since 802.11ba data is narrow band and depending on its implementation, the next 4us symbol duration after BSPK-mark1 may be treated as Q-BPSK. In that case, 802.11ac STA recognizes 802.11ba PPDU as 802.11ac PPDU and cause unspecified behavior [3].
Therefore, BPSK-mark2 is added to spoof 802.11ac STAs.
TGbe wants to use the RL-SIG with its LENGTH field divisible by 3. Thus, the BPSK-mark content is changed [4] to avoid confusing 802.11be STAs.

## Slide 5: If AMP DL PPDU using 802.11ba-like preamble
802.11be and future generations STAs waste its power to decode AMP PPDU (treats it as 802.11a PPDU).
802.11be and future generations STAs may apply TWT for power saving; however, if they receive a OBSS AMP PPDU (if it uses only BPSK-marks), they will waste their time processing the data portion and may miss the intended PPDUs in myBSS
    There is a power drop in between spoofing preamble and OOK data. In a fadding channel, the RX power of the ON-duration may be lower than a certain threshold, which combines with OFF-duration may cause some 802.11 STA detect channel idle.
    In above case, LENGTH field in L-SIG may not be trusted by 802.11 STAs. (no MAC information for third-party STAs, since they cannot decode OOK data). It is desired to have TXOP information (third-party STAs to set NAV) to protect AMP PPDU reception.

## Slide 6: Proposed AMP DL PPDU
We propose that AMP PPDU employ the spoofing preamble design like 802.11be, which provides additional information in U-SIG, e.g., PHY version, BSS color, DL/UL, TXOP. Third-party STAs (e.g., 802.11be/bn) can make an early determination of the incoming PPDU format and terminate the RX processer.
This design may increase 4us as compared to 802.11ba design; however, it is a very small portion as compared to a low-rate AMP data.
L-STF
20MHz
L-LTF
L-SIG
RL-SIG
U-SIG1
AMP-sync
AMP-SIG
AMP package
Narrow bandwidth, e.g., 4MHz
802.11 spoofing
U-SIG2
AMP package: OOK format

## Slide 7: SP1
Do you agree to apply L-STF, L-LTF, L-SIG, RL-SIG, and U-SIGs in AMP DL PPDU?

## Slide 8: References
[1] 11-23/2203r1, 802.11ba is considered as a starting point of AMP DL PPDU design, Yinan Qi et al.
[2] 11-24/0452r0, Overview of the 802.11ba PHY, Steve Shellhammer et al., Qualcomm.
[3] 11-19/0423r1, PHY Misclassification Issue, Steve Shellhammer et al., Qualcomm.
[4] 11-19/1586r0, Comment Resolutions on Contents of BPSK Mark Symbols, Steve Shellhammer, Qualcomm.

## Slide 9: Additional bit indicator in U-SIG
A Validate bit in U-SIG can be used to indicate 802.11bp DL PPDU. 802.11be STA see the Validate bit will terminate its RX processer.
When 802.11be STAs receive an 802.11bp DL PPDU, it will honor the TXOP duration indicated in U-SIG, or it can do SR if the power under the SR threshold and OBSS.
L-STF
20MHz
L-LTF
L-SIG
RL-SIG
U-SIG1
AMP-sync
AMP-SIG
AMP package
Narrow bandwidth, e.g., 4MHz
802.11 spoofing
U-SIG2
AMP package: OOK format