## Slide 1: Feedback-based triggered access Optimization using SCS
Date: 2024-04-08
Authors:

## Slide 2: Abstract
In this submission, we discuss methods for a STA to provide real-time feedback (such as HOL Delay) to an AP providing uplink triggered access (TUA) scheduling via SCS. Simulations have shown its benefit to latency sensitive applications, such as real-time voice/video and AR/VR/XR applications in a congested environment.

## Slide 3: Problem Statement
SCS can be used to provision 11ax/be triggered uplink access and has been shown to improve latency under congestion
While this scheduling mode can reduce or eliminate the need for Buffer Status Report (BSR), instantaneous conditions at the STA such as excess delay may not be considered for imminent (e.g., next TXOP) STA scheduling.
Since BSRP/BSR exchanges are often suppressed during SCS TUA operation, we can’t always guarantee an UL delay bound outcome.
Can we do better for SCS-based streams with low excess delay tolerance ?

## Slide 4: Limitations of existing SCS QoS Characteristics
A naïve approach by a STA would be to request a new or modified SCS service via revised QoS characteristics when excess delay is accrued (e.g. reduce the max Service Interval)
However, such a request would be processed by host/network level processes and could take multiple SIs to complete and would still result in the target delay being exceeded causing undue application degradation.
In addition, reducing the Max SI to below the applications actual tolerance quickly leads to priority inversion in a dense network
A timely low-complexity method seems needed to alleviate these concerns

## Slide 5: How Feedback-based SCS Works
A STA starts an SCS session for the latency-sensitive traffic at the period (Min/Max Service/Interval) appropriate for EACH flow (e.g. 20-25ms for voice, 30-35ms for video, etc.) and an acceptable Delay Bound (e.g., 50ms for voice, 70ms for video)
  Ideally, the STA starts traffic only after the SCS session is established
  The AP uses the Min/Max SI to schedule initial triggering accordingly
As the session progresses, the STA reports the experienced Delay (e.g. per AC/TID, SCSID, etc)
  This could be expressed as one or more of the following:
    E.g., MSDU Delay: MSDU arrival – BA time
    E.g., HOL Delay: MSDU arrival at HOL – BA time
    E.g., Trigger Offset: MSDU Arrival – Trigger time
The AP collates the delay reports from multiple STA to inform subsequent trigger schedules
  The AP is aware of the UL OFDMA RU allocations and can decide if more RUs are needed (at the same frequency)
  The AP is aware of the requested Delay Bound and reported Delay and can compute a temporal or persistent trigger advance
  The AP is aware of the Delay Bound, last trigger time and reported offset and can compute a temporal advance

## Slide 6: How Feedback-based SCS Works
A new “Delay Report” could be designed and signaled to the AP opportunistically (e.g., when Delay > Bound), this could be any one of:
  MSDU Delay: MSDU arrival – BA time
  HOL Delay: MSDU arrival at HOL – BA time
  Trigger Offset: MSDU Arrival – Trigger time
This is complementary to the Min/Max Service Interval and Delay Bound of the SCS QoS Characteristics IE
AP
STA
DATA
BA
Delay report
Trigger
Excess queue
build up
MSDU arrival
Trigger
MSDU arrival
DATA
BA

## Slide 7: Summary
In this submission, the Feedback-based triggered access optimization (SCS+TUA) is discussed to reduce excess uplink delay for latency sensitive traffic

## Slide 8: Straw Poll 1 (example only)
Do you support definition of an Uplink Delay Report element that can be used within a control frame (e.g., A-Ctrl, QoS-Ctrl) to help the AP better schedule Trigger Frames?
Y
N
A