## Slide 1: Preemption for Coordinated TDMA
Date: 2024-09-10
Authors:

## Slide 2: Abstract
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to Extremely High Throughput (EHT) MAC/PHY operation [1].
Coordinated time-division multiple-access (C-TDMA) has been discussed [2-8] as one of the candidate schemes of multi-AP operation (aka. Multi-AP coordination/transmission) to meet the requirement of UHR capability.
Meanwhile, preemption have been proposed as a general solution to solve the problem of large delays when a large PPDU is transmitted in a TXOP [9-16].
In this contribution, we discuss some methods of preemption for C-TDMA.

## Slide 3: Background
MU-RTS triggered TXOP sharing (TXS) has been proposed for use in C-TDMA to allow the sharing AP to share an allocation duration of the TXOP to the shared AP.
CF-end may be used by the shared AP to return the remaining allocation duration to the sharing AP.
In C-TDMA, a sharing AP (e.g., AP1 ) that is TXOP owner coordinate with one or more shared APs (e.g., AP2 that is an OBSS AP) by sharing a portion of TXOP for use of transmission.

## Slide 4: Low-Latency Traffic in C-TDMA
In C-TDMA, the sharing AP (AP1) owns TXOP and shares a period of TXOP to the shared AP (AP2).
When implementing preemption in C-TDMA, AP2 may allow preemption within its own BSS (e.g., allow AP2 or STA2 to preempt) the on-going transmission if necessary.
However, when AP1 has a low latency(LL) traffic arriving during the period shared with AP2, AP2 doesn’t allow AP1 to preempt.
As a result, AP1 has to wait until the end of the shared period to send a data frame of LL traffic to STA1.

## Slide 5: Preemption for C-TDMA - Method 1
AP1 sends to AP2 an MU-RTS TXS trigger (MRTT) frame specifying an allocation duration and recommending, a preference of AP1 for the allowance of preemption within the allocation duration.
  The preemption is allowed by the AP1 only, and disallowed by a non-AP STA.
After responding a CTS to MRTT, AP2 decides that whether allow preemption based on the preference. For example,
  AP2 allows the preemption: AP2 transmits short PPDUs and set preemption is allowed in the PPDU.
  AP2 doesn't allow the preemption: AP1 can not preempt (not shown).

## Slide 6: Preemption for C-TDMA - Method 2
AP1 sends to AP2 a request frame requesting AP2 to allow preemption.
  The preemption is allowed by the AP1 only, and disallowed by a non-AP STA.
AP2 decides that whether AP2 allows preemption or not, and responds to AP1.
Based on the response of AP2, AP1 sends a MRTT to AP2 and decides the allocation duration to AP2. For example:
  If AP2 accepts the request, AP1 sets the allocation duration to be larger than a value and so that the allocation duration is sufficiently long for AP2 to participate in C-TDMA with preemption.
  If AP2 rejects the request, AP1 sets the allocation duration to be shorter than the value (not shown).

## Slide 7: Summary
In this contribution, we shared some thoughts of preemption for C-TDMA.
  MRTT with a preference/recommendation of preemption allowance
  A request/response of preemption allowance frame exchange before MRTT

## Slide 8: References
23/0480, UHR proposed PAR, Laurent Cariou (Intel)
23/0041, Yanjun Sun (Qualcomm), Considerations on Coordinated TDMA (C-TDMA), 2023-01
23/0261, Dibakar Das (Intel), C-TDMA procedure in UHR, 2023-01-25
23/0739r1, Yanjun Sun (Qualcomm), Follow-up on Coordinated TDMA (C-TDMA), 2023-05-15
23/1085, Geonhwan Kim (LG Electronics), Thoughts on Coordinated TDMA, 2023-08-07
23/1327, Si-Chan Noh (Newracom), Considerations on Return TXOP between multiple APs, 2023-08-07
24/0382, Serhat Erkucuk (Ofinno), Further Considerations on Coordinated TDMA, 2024-02-28
24/0512, Rubayet Shafin (Samsung Electronics), Considerations for Coordinated TDMA, 2024-04-28
23/1229r1, Juan Feng (Intel), Preemption for Low Latency Application, 2023-08-10, (23/0092, follow up, 2023-03-13)
22/0018r1, Kiseon Ryu (NXP), Low Latency Support in UHR, 2023-02-05, (23/1174, follow up, 2023-07-06)
23/1886, Giovanni Chisci (Qualcomm), Preemption techniques to meet low-latency (LL) targets, 2024-01-10
23/1950, Leonardo Lanante (Ofinno), Considerations on Preemption Request, 2023-11-13
24/0131, Insun Jang (LG Electronics), Signaling of Preemption, 2024-03-11
24/0389, Mohamed Abouelseoud (Apple), Preemption for Low Latency, 2024-04-10
24/0390, Yunbo Li (Huawei), A Uniform Procedure for Preemption, 2024-02-08
24/0391, Yunbo Li (Huawei), Legacy STA and OBSS Issues for Preemption, 2024-02-18