## Slide 1: Beamforming Feedback for UL Beamforming
Date: 2024-05-03
Authors:

## Slide 2: Abstract
UL Beamforming has been discussed as a potential feature in 802.11bn [1-4]. In [1,2], it was shown that STAs applying beamforming using both SU PPDUs or UL MU-MIMO can have considerable throughput gains.
In [3], it was shown that a coordinated precoding approach can provide even higher throughput gains by designing the precoding matrix independently.
In [4], a protocol design for UL Beamforming was discussed
In this contribution, we discuss how to support multiple types of beamforming approaches in the UL.

## Slide 3: HE/EHT TB sounding for DL MU-MIMO transmission
AP
STA 1
STA 2
NDPA
NDP
BA
MU PPDU
BFR
HE/EHT TB sounding for DL MU-MIMO transmission is shown above.
1. The AP sounds the composite DL channel to multiple STAs.
2. The STAs generates beamforming feedback reports and send back to the AP.
3. The AP generates steering matrices and link parameters (Nss, MCS, RU) for the following MU PPDU.
beamformed
BFRP
BFR
BA

## Slide 4: UHR UL sounding for UL TB transmission
AP
STA 1
STA 2
TF
NDP
NDP
TF
TB PPDU
TB PPDU
BA
A possible procedure for UHR UL sounding for UL TB transmission is shown above.
1. The AP sounds the composite UL channel from multiple STAs.
2. The AP generates beamforming feedback for use by the STAs during UL TB transmissions.
3. The AP sends the beamforming feedback to the STAs and associated link parameters (Nss, MCS, RU)
Each STA then uses the indicated beamforming feedback and link parameters to transmit the TB PPDU.
beamformed
beamformed
BFR

## Slide 5: Problem with Beamforming Feedback in UL Sounding
As mentioned in [2], non-AP STAs during UL TB PPDU simply follows the indications by the AP (e.g. MCS, NSS in the trigger frame). This includes whether the non-AP STAs should apply beamforming or not.
Thus, it is possible for an AP to generate custom steering matrices and send this to the non-AP STAs instead of the V matrices (e.g. AP coordinated precoding matrices in [3]).
In contrast, if we restrict the AP from generating custom steering matrices (i.e. only regular V matrix support), the non-AP STA may reuse the V matrix feedback when transmitting beamformed SU PPDUs.
AP
STA 1
STA 2
TF
TB PPDU
TB PPDU
BA
beamformed
beamformed
BFR
SU PPDU
Not beamformed

## Slide 6: Feedback of Multiple UL Beamforming Codebooks
To enable STAs to perform both UL SU and UL MU beamforming robustly, the AP may send two or more sets of UL beamforming feedback
- one set can be the set of right singular V matrices used for SU PPDU or in non-MU-MIMO UL TB PPDU transmission.
- another set can be for AP coordinated precoding or any implementation dependent precoding.
AP
STA 1
STA 2
TF
TB PPDU
TB PPDU
BA
Beamformed
(BFR MU)
Beamformed
(BFR MU)
BFR
MU
SU PPDU
Beamformed (BFR SU)
BFR
SU

## Slide 7: Other solutions
While feedback of multiple beamforming codebooks can enable the non-AP STA to perform both SU and TB PPDU beamforming, it is more complex to implement for both APs and non-APs (e.g. memory requirements). Other possible solutions include
Solution 1: Restrict the AP operation to only feedback right singular V matrices during UL sounding.
  The STA uses the V matrices corresponding as steering matrices regardless of the type of PPDU it transmits.
Solution 2: The AP indicates to the STA the type of BFR (e.g. whether the BFR comprises right singular V matrices or not).
  The non-AP STA uses the BFR for beamforming in SU PPDU based on the indication.

## Slide 8: Other issues
The non-AP STAs may not know when to discard UL BFRs that are no longer useful (e.g. channel aging reasons).
  The AP can indicate during a TB PPDU exchange whether the BFR can or will no longer be used after the TB PPDU exchange (e.g. due to channel aging, etc.)
The non-AP STA may also discard UL BFRs without telling the AP to free up its memory resources.
  The AP/STA can also negotiate a timeout value for the UL BFRs. Within the timeout value, the non-AP STA will keep a received BFR in its memory.

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0263-00-0uhr-triggered-beamforming-in-uhr.pptx
[2] https://mentor.ieee.org/802.11/dcn/24/11-24-0108-00-00bn-triggered-beamforming-in-tgbn-follow-up.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-0725-00-0uhr-uplink-mu-mimo-precoding-follow-up.pptx
[4] https://mentor.ieee.org/802.11/dcn/24/11-24-0243-00-00bn-protocol-design-for-ul-beamforming.pptx