## Slide 1: Further Considerations on Preemption
Date: 2024-05-10
Authors:

## Slide 2: Introduction
Preemption has been mainly considered for preempting within a TXOP (i.e., TXOP level preemption) rather than preempting within a PPDU [1] – [17].
For TXOP level preemption, while a TXOP holder can easily preempt its own TXOP for low latency (LL) data, transmitting LL data by a TXOP responder needs further investigation.
In addition, it is widely assumed that all the STAs and the AP in a BSS may preempt if they have buffered low latency data. However, the efficiency of preemption procedure for such a consideration also needs further investigation.

## Slide 3: Recap: Preemption during DL TXOP
(TXOP holder)
When an AP is the TXOP holder, it may transmit an indication in a PPDU to its associated STAs that it allows preemption a SIFS after the current PPDU.
STAs that have LL data (having buffered data with high AC or TID values) transmit preemption request (PR) frames.
Receiving the PR frames, AP sends a BSRP frame. After evaluating the BSRs, AP may trigger one or more of STAs for transmission depending on the allowed preemption duration or the urgency of the LL data.
Lower TID
Higher TID

## Slide 4: Recap: Preemption during UL TXOP
(TXOP holder)
When a STA is the TXOP holder, it may transmit an indication in a PPDU to the AP and STAs in the same BSS that it allows preemption a SIFS after the current PPDU.
AP and/or STAs that have LL data transmit PR frames.
If AP has LL data for the TXOP holder or other STAs, it may send it after the PR frame. AP may then send a BSRP frame. After evaluating the BSRs, AP may trigger one or more of STAs for transmission depending on the allowed preemption duration or the urgency of the LL data.

## Slide 5: Preemption During UL TXOP
In the current preemption procedures, during an UL TXOP, preemption request can be made by AP for DL transmission to TXOP holder (e.g., STA1) or other STAs, and/or by other STAs for UL transmission to the AP. Being the TXOP holder, STA1 may have to wait a long duration before it regains the control of the TXOP.
  For example, TXOP holder (STA1) may prefer to receive LL frames only to itself during preemption.
  Accordingly, TXOP holder (STA1) needs to define some categories of stations that can preempt.
STA1 cannot TX/RX although it is the TXOP holder
(TXOP holder)

## Slide 6: Category of Stations for Preemption
AP and its associated STAs receive from the TXOP holder STA an indication of category of stations allowed to preempt the next PPDU of the TXOP holder STA.
  Category of stations may include only AP STAs, only non-AP STAs, STAs with specific AC and/or TID values, STAs having buffered data for the TXOP holder STA, etc.
  The field indicating the category of stations may be in the U-SIG, UHR-SIG or MAC header of the PPDU.
If the AP and/or any of its associated STAs are a member of category of stations allowed to preempt the next PPDU, they may transmit their buffered data during preemption.
Indic. of category of stations allowed preemption
(TXOP holder)

## Slide 7: Conclusion
For an efficient operation of the preemption procedure, TXOP holder may determine and announce category of stations allowed to preempt the next PPDU of the TXOP holder.
  Category of stations may include only AP STAs, only non-AP STAs, STAs with specific AC and/or TID values, STAs having buffered data for the TXOP holder STA, etc.
Based on the AP/STA being a member of the category of stations allowed to preempt the next PPDU, the AP/STA may transmit its buffered data during preemption.

## Slide 8: References
[1] 23/0018r1, Low Latency Support in UHR
[2] 23/0092r0, Preemption for Low Latency Application
[3] 23/1174, TXOP Preemption Follow Up
[4] 23/1194r0, Overlapped Indication to Support Preemption
[5] 23/1229r1, Preemption for Low Latency Application (follow up)
[6] 23/1242r1, Considerations on Inter-PPDU based Preemption Scheme
[7] 23/1434r2, Discussions on Low Latency Traffic Delivery in UHR
[8] 23/1886r3, Preemption techniques to meet low-latency (LL) targets
[9] 23/1939r1, Priority Based Preemption Method
[10] 23/1950r0, Considerations on Preemption
[11] 24/0103r1, TXOP Level Pre-emption for Low Latency Application
[12] 24/0168r0, TXOP preemption in 11bn
[13] 24/0390r0, A Uniform Procedure for Preemption
[14] 24/0391r0, Legacy STA and OBSS Issues for Preemption
[15] 24/0416r0, Target STA Prioritization in EDCA-based Preempt. Mech. during a DL TXOP
[16] 24/0431r0, Signal for preemption request
[17] 24/0470r0, Re-thinking latency: the missing pieces

## Slide 9: Straw Poll
Do you agree to define category of stations that are allowed to preempt the next PPDU of the TXOP holder in the preemption procedure?
  The procedure for defining the category of stations is TBD.
  The field(s) to be used in the procedure is/are TBD.
  Yes
  No
  Abstain
  Y/N/A: