## Slide 1: MAC aspects for AMP
Date: 2024-05-11
Authors:
Name | Affiliation | Address | Phone | Email
Chuanfeng He | OPPO |  |  | hechuanfeng@oppo.com
Weijie Xu |  |  |  | 
Yinan Qi |  |  |  | 
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 2: Abstract
In this contribution, we discuss MAC aspects for AMP generally.
Doc.: IEEE 802.11-24/0872r0

## Slide 3
Background
  Project 802.11bp was approved by IEEE SA standards Board on 21 Mar 2024.
  The TG of 802.11bp will kick off during 2024 July IEEE 802 Plenary Session.
  The scope of the project is to define modifications to both the IEEE 802.11 Medium Access Control layer (MAC) and Physical Layers (PHY) to enable the operation of an Ambient Power communication (AMP) station (STA) that is powered using energy harvesting.
Chuanfeng He (OPPO)
Slide 3
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 4
Potential MAC aspects for AMP
  Frame format
    Legacy frame format includes MAC header, frame body and FCS. For AMP operation, legacy frame format can be reused with some potential optimization, e.g.:
      Short MAC header, e.g. short identity of AMP STA
      Short management frame, e.g. Short Beacon
    New fields and elements are to be studied to support AMP operation, e.g.
      Capability of uplink transmission, backscatter or active transmission
      Power management related fields and elements
Chuanfeng He (OPPO)
Slide 4
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 5
Potential MAC aspects for AMP
  Channel access
    AMP non-AP STA can not perform legacy CSMA/CA based channel access before transmission, since it can not demodulate legacy preamble and MAC header, which are modulated using OFDM.
    TXOP holder, such as AP, can protect the channel and allocate service periods to AMP STAs for UL transmission.
    At least AC_BK is defined for AMP communication access category (AC).
Chuanfeng He (OPPO)
Slide 5
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 6
Potential MAC aspects for AMP
  Synchronization
    Short timestamp for less power consumption of AMP STA
      64bits->32bits(S1G)->?bits(AMP)
    The time span of TSF timer for AMP STA
      Considering the working time is limited by power storage, TSF timer may only need to cover working time after each wake up.
    Periodical or triggered timestamp acquisition
      Power efficient timestamp acquisition is needed. Maintenance of TSF timer by periodical timestamp acquisition has a little bit more power consumption.
Chuanfeng He (OPPO)
Slide 6
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 7
Potential MAC aspects for AMP
  Authentication and association
    Without authentication and association
      For inventory use case, fast label identification of the items is required. AMP STA may have no sufficient power and time to perform authentication and association.
      AMP STA can deliver instant UL traffic without being associated with a BSS.
    With authentication and association
      For environmental monitoring use case, the data of a sensor may be reported frequently.
      AMP STA can associate with a BSS by authentication and association, and deliver frequent UL traffic.
  The requirement of authentication and association can be use case specific.
Chuanfeng He (OPPO)
Slide 7
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 8
Potential MAC aspects for AMP
  Legacy scanning to discover a BSS
    Passive scanning: AMP beacon, discovery frame
    Active scanning: Probe request/response
  Power efficient scanning is needed for AMP STA, such as
    Use case specific scanning, e.g. passive scanning on pre-determined channels.
    Passive scanning assisted by discovery frame on pre-determined channels.
Chuanfeng He (OPPO)
Slide 8
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 9
Potential MAC aspects for AMP
  Power management
    Several power management modes have been developed in 802.11, e.g.
      PS-poll
        Page slicing(802.11ah)
      TWT(802.11ah,ax)
        NDP paging
      APSD(802.11e)
      PSMP(802.11n)
    Power management is important for AMP STA to use limited power storage to guarantee UL traffic from AMP STA . Efficient power management mode is needed for AMP operation, if legacy ones do not work well for AMP communication.
Chuanfeng He (OPPO)
Slide 9
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 10
Potential MAC aspects for AMP
  Security
    Legacy 4-Way Handshake is required to generate and exchange key between AP and STA for security, after authentication and association procedure.
    It is challenging and costly for AMP STA to establish conventional secure association, with limited power and instant small volume data.
    For AMP communication, the establishing and maintaining secure association can be simplified, considering the procedure
      without authentication and association
      with authentication and association
Chuanfeng He (OPPO)
Slide 10
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 11
Summary
  In this submission, potential MAC issues for AMP operation are observed and generally discussed on the following aspects
    Frame format
    Channel access
    Synchronization
    Authentication and association
    Scanning
    Power management
    Security
Chuanfeng He (OPPO)
Slide 11
Doc.: IEEE 802.11-24/0872r0
May 2024

## Slide 12: Reference
https://development.standards.ieee.org/myproject-web/app#viewpar/11414
Doc.: IEEE 802.11-24/0872r0
May 2024