## Slide 1: Quo vadis, LC in 802.11?
Date: 2024-05-14
Authors:
Name | Affiliations | Address | Phone | email
Volker Jungnickel | Fraunhofer HHI |  |  | volker.jungnickel@hhi.fraunhofer.de
Andreas Bluschke | self |  |  | andreas.bluschke@signify.com
Matthias Wendt | Signify |  |  | matthias.wendt@signify.com

## Slide 2: Abstract
This contribution summarizes recent discussions in 802.11 on LC evolution, taking market needs and recent developments into account. The proposal is to form a study group to define the PAR and CSD for Integrated Light Communication (ILC).

## Slide 3: Current status of LC
Recent IEEE LC standards finished
  IEEE Stds 802.15.13-2023 and 802.11bb-2023 focusing on industrial applications and mass market [1, 2]
LC gained traction in various niche markets, where light has unique selling points
  Military, secure conference rooms (governments, banks): LC cannot be wiretapped/jammed
  fixed wireless access: LC goes through windows (no outdoor unit), LC can offload traffic from RF
  platooning, train-to-train: LC is not interfered by RF (reliable channel access, suitable for wireless control)
Chicken-and-egg problem (No chipset = No market / No market = No chipset)
  Both new IEEE LC standards compete with ITU-T Rec. G.9991 (legacy of G.hn)
    ITU-chipset allows simpler integration with LC optical frontends, 802.11bb needs costly up-down conversion
    802.11bb is likely to become single-vendor scenario. But standards should enable interoperability
How to make IEEE LC standards more attractive for mass market adoption?

## Slide 4: Previous developments related to LC
Recently proposed new features
  Distributed MIMO [3]
  Integration of LC and RF [4]
  Integration into MLO [5] and with mm-wave [6]
  Higher bandwidth (320, 640, …MHz): Non-overlapping channels [7]
  Reuse original BB for sub-7 GHz or up-clocked BB for mm-wave [8]
  Unified IF interface for LC and mm-wave [9], new wavelength for LC [10]
LC to continue as separate project
  IMMW supporters did not want to risk extending the scope that was backed up by a 802.11 WG Motion
Issues to be regarded towards new LC study/task group
  will run in parallel to two mainstream projects (11bn, immw)  offload contributions into teleconferences

## Slide 5: Proposed scope of new project
Make LC more attractive for mass market adoption
  Native support for LC IF  Solve chicken-and-egg problem
    specify LC IF interface in more detail
    interoperability of LC optical frontends with any 802.11 chipset (infrastructure and device side)
    taking EMI concerns seriously into account
  Enable new features in 11be and 11bn for LC  Integrate LC deeper with 802.11
    320 MHz (and possibly more), integration into MLO, coordinated multi-AP
    Develop 802.11bb further into generic LC spec.: transport any 802.11 version over light
  Support of distributed MIMO for LC  Improve reliability (LOS blockage), reduce latency
    centralized infrastructure chipset based on 802.11, distributed optical frontends
    specify electrical/optical fronthaul interface over diverse media (CATx, POF, PLC, FttR)
    consider amplify-and-forward vs. decode-and-forward approaches

## Slide 6: Summary
The evolution of LC in 802.11 should focus onto features which primarily make LC more attractive for mass market adoption.
This contribution has summarized previously proposed features and suggested priorities towards the above mentioned goal, which maybe further detailed in new study group.

## Slide 7: Straw Poll
Do you support the creation of an Integrated Light Communication (ILC) study group that will be tasked with the creation of a PAR and CSD for a standards project to specify operation of 802.11 in optical bands between 800 nm and 1550 nm and simplify the integration with LC optical frontends?
Y / N / A

## Slide 8: References
[1] IEEE Std 802.11bb-2023, https://standards.ieee.org/ieee/802.11bb/10823/
[2] IEEE 802.11-23/0277r1 IEEE 802 Tutorial “IEEE 802 Standards on Light Communication” March 2023 Plenary Meeting
[3] IEEE 802.11-23/0091r New Light Communication Features
[4] IEEE 802.11-23/1068r0 Experiment Results with Wi-Fi to Li-Fi Offloading in an Office Environment,
[5] IEEE 802.11-23/0221r1 Hybrid LC and RF in UHR
[6] IEEE 802.11-23/2016r2 Extend IMMW scope to include optical bands
[7] IEEE 802.11-24/0062r0 Channelization to include optical bands
[8] IEEE 802.11-24/0077r0 Numerology to include optical bands
[9] IEEE 802.11-24/0406r1 Unified IF interface for mm- and light-wave
[10] IEEE 802.11-24/0571r0 March 2024 LC proposal
[11] IEEE 802.11-23/0098r0 WNG Meeting Minutes 2023-Jan Baltimore meeting