## Slide 1: AIML PHY Operational Parameter Recommendations
Date: 2024-05-13
Authors:

## Slide 2: Abstract
Proposed mechanism allowing APs to provide PHY operational parameters range recommendations to the STAs.
Intended use cases include energy saving and privacy.
AIML techniques applied to estimate the impact of the changes to the STAs uplink transmissions.

## Slide 3: Background
The AP can use different mechanisms to influence the STAs Tx power (e.g., BSS coloring, Transmit Power Envelope), aimed at enforcing regulatory limits as well as controlling interference in OBSS operations.
When a STA modifies its operating parameters, there may be unintended impacts to the link quality, which are detected only after such parameters are applied.

## Slide 4: AP-assisted PHY parameter selection
The proposed mechanism allows the AP to provide the STA with recommendations about the PHY settings that can be used to minimize energy consumption, while maintaining the performance impact within the STA’s desired range.
The acceptable impact is specified by the STA, according to the application requirements.
The AP-generated recommendation considers current BSS status as well as receiver-side STA connection statistics.

## Slide 5: Use cases
In addition to increased energy efficiency, the proposed recommendation mechanism allows implementing privacy-related use cases, such as the “TX power randomization” scheme currently being discussed in the TGbi [1].

## Slide 6: Operation: STA request
Proposed extension to the dot11SpectrumManagement, adding flag to advertise the AP capability to provide PHY parameters recommendations to STAs.
STA to send a PHY recommendation request:
Indicating its current transmit power and link margin (similar to TPC report)
Indicating the acceptable performance degradation (e.g., for metrics such as retry rate)
Indicating what parameters can be changed (e.g., Tx Power, SS, Channel width, MCS range)

## Slide 7: Operation: AP response
The AP responds with a recommendation including the indication of the settings expected to meet the STA’s request, for instance:
  Min Tx power for each bandwidth
  Min SS
  Max MCS
  …
Recommendation means that the receiving STA maintains full control as to what PHY parameters to use.

## Slide 8: Operation: Accuracy
The confidence on the recommendation’s accuracy and longevity depends on the available link statistics (e.g., the longer a STA has been connected, and as stable the connection has been, the more accurate the prediction can be).
The algorithm used to generate the recommendation at the AP side would also compute a confidence metric, to be shared on the response to the STA.
In case the accuracy is too low, the AP doesn’t return any recommendation and can optionally add a reason code to provide an explanation (e.g., too few datapoints, too high variation, too small link margin, etc..)

## Slide 9: AIML relevance
AIML is proposed as the method to generate the recommendations discussed so far, given the number of parameters involved.

## Slide 10: Summary
Proposed method to allow the AP to assist the STAs to pick its PHY parameters, aligned with discussions happening in other groups:
  TGbn: Energy efficiency
  TGbi: STA identity obfuscation by TX power randomization [1]
Recommendations to include multiple PHY parameters
Proposed use case making use of AIML to generate recommendations

## Slide 11: References
[1] IEEE 802.11-24/0550-r1 - TX Power Randomization