## Slide 1: TXOP Sharing Group – Shared AP Selection
Date: 2024-05-16
Authors:

## Slide 2: Introduction
There have been multiple contributions on TXOP sharing and coordinated TDMA (C-TDMA) e.g. [1]-[11].
A Multi-AP Coordination (MAPC) set has been proposed in [6]; MAPC can be used to coordinate PS, channel use, TWT, NPRCA… TXOP Sharing is hyper-local for BSS on the same channel
TXOP can be rather long (5ms) and low latency traffic may arrive at a potential Shared AP which is unknown to the Sharing AP
In this contribution we discuss the need for a TXOP Sharing Group that takes newly arrived low latency traffic into account

## Slide 3: TXOP Sharing Group
TXOP Sharing Group
OBSS operating on the same primary channel
Can be a subset of MAPC group
Defines a mechanism to share TXOP between OBSS participating in the TXOP Sharing Group
AP1
STA1
AP2
STA2
AP3
STA3

## Slide 4: Recap) Multi-AP C-TDMA MAC procedure [12]
Discussion on extending the 11be Triggered TXOP Sharing (TXS) framework to Coordinated Time Division Multiple Access (C-TDMA) in 11bn
  An MU-RTS TXS Trigger frame can be used for a sharing AP to allocate a time duration to a selected single shared AP.
Potential signaling sequence
  A sharing AP transmits an MU-RTS TXS Trigger frame to a shared AP for C-TDMA time allocation.
  The shared AP responds with a CTS frame in response to the MU-RTS TXS Trigger frame.
  The shared AP can do frame exchange with its associated non-AP STAs during the allocation time indicated in the MU-RTS TXS Trigger frame.
  Often the Sharing AP does not know which of the Shared AP in the vicinity needs the TXOP and has e.g. low latency traffic to transmit
AP1
AP2
AP3
STA1
STA2
STA3
AP4
STA4

## Slide 5: TXOP Sharing with Probe
Form a TXOP Sharing Group
Offer TXOP Sharing to group or individual members of TXOP Sharing group
Receive TXOP request from these TXOP group members
Grant remainder or fraction of the remaining TXOP to Shared AP
Possibility to reuse existing frames or to define new frames for that exchange
Sharing AP
(BSS1)
TXOP Sharing offer
Shared AP
(BSS2)
TXOP request
Shared AP
(BSS3)
TXOP request
TXOP grant
C-TDMA allocation
Data
STA
(BSS2)
BA

## Slide 6: TXOP Sharing with Probe – MU-RTS
Sharing AP sends adaptation of MU-RTS TXS frame to probe TXOP Sharing Group members
MU-CTS is used by Sharing Group members to indicate request to get the TXOP
Sharing AP sends an (adapted) MU-RTS TXS message to indicate which Shared AP(s) get (part of) the TXOP
  Could include TDMA allocation to multiple Shared APs
Sharing AP
(BSS1)
MU-RTS TXS
Shared AP
(BSS2)
MU-CTS
Shared AP
(BSS3)
MU-CTS
MU-RTS
TXS
C-TDMA allocation
Data
STA
(BSS2)
BA
Data
BA
STA
(BSS3)

## Slide 7: TXOP Sharing with non-primary channel operation
Shared AP can operate on a non-primary channel
Sharing AP sends adaptation of MU-RTS TXS frame to probe TXOP Sharing Group members
MU-CTS is used by Sharing Group members to indicate request to get the TXOP
Sharing AP sends an (adapted) MU-RTS TXS message to indicate which Shared AP(s) get (part of) the TXOP and share of bandwidth
  Here the assumption is all BSS use 80MHz and the Sharing AP allocates lower 40MHz to BSS2 and upper 40MHz to BSS3
Sharing AP
(BSS1)
MU-RTS TXS
Shared AP
(BSS2)
MU-CTS
Shared AP
(BSS3)
MU-CTS
MU-RTS
TXS
C-TDMA allocation
Data on lower 40MHz
STA
(BSS2)
BA on lower 40MHz
STA
(BSS3)
BA on upper 40MHz
Data on upper 40MHz

## Slide 8: Summary
Multiple AP form a TXOP Sharing Group
Sharing AP can probe members of TXOP Sharing Group, e.g. to find out which TXOP Sharing Group member has low latency traffic and needs the TXOP
Sharing AP can grant (part of) TXOP to Shared AP based on the received responses from TXOP Sharing Group members

## Slide 9: Strawpoll
Do you agree that a TXOP Sharing Group which may be a subset of a MAPC group should be established to coordinate the sharing of TXOPs?
YES
No
Abstain

## Slide 10: References
[1] 23/0041r0, “Considerations on Coordinated TDMA (C-TDMA)”
[2] 23/0249r1, “Extended TXOP Sharing”
[3] 23/0261r0, “C-TDMA procedure in UHR”
[4] 23/0739r1, “Follow-up on Coordinated TDMA (C-TDMA)”
[5] 23/1962r1, “Gain analysis for coordinated AP transmissions”
[6] 23/1912r1, “Coordinated TDMA Procedure”
[7] 23/1085r0, “Thoughts on Coordinated TDMA”
[8] 23/1910r1, “Coordinated TDMA (Follow up)”
[9] 24/0441r0, “TXOP Return in C-TDMA”
[10] 24/0093r1, “NAV setting for Coordinated TDMA”
[11] 24/0227r1, “TXOP Protection in C-TDMA”
[12] 24/0387r0, “TXOP Sharing for C-BF transmission”