## Slide 1: C-TDMA Follow-up: Additional Details on Framing Sequence
Authors:
Date: 2024-02-20
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Duncan Ho |  |  |  | 
Giovanni Chisci |  |  |  | 
Sherief Helwa |  |  |  | 

## Slide 2: C-TDMA Frame Exchange Sequence
Previous contributions discussed the following framing sequence [1, 2, 4, 9-11, 13]:
  The sharing AP polls candidate shared APs via Poll/Ann. frame
  The sharing AP triggers TXOP sharing via TXOP Allocation frame
  The shared AP returns unused TXOP (if any) via TXOP Return frame
This contribution provides next-level details for the Poll/Ann. frame
*Polling of in-BSS STAs of the sharing AP is optional

## Slide 3: Details of Polling/Announcement Frame
Sharing AP sends Poll/Ann. frame at the start of the TXOP to:
  Announce its intent to share a part of its TXOP
  Poll candidate AP(s) to check their interest in participation
  Optionally, poll its in-BSS STA(s)
The Poll/Ann. frame may specify traffic priority for the shared TXOP, e.g.,:
  AC, SCSID, TID of the traffic
A response from a polled AP may indicate:
  Its intent to participate in C-TDMA
  Relevant information about its traffic
The Poll/Ann. frame helps shared AP(s) make scheduling decisions:
  whether to participate in sharing during the current TXOP
    A shared AP will not participate if it has no traffic for the indicated traffic type
  If participating, the AP identifies suitable client(s) to serve during the shared TXOP

## Slide 4: Need for Polling/Announcement Frame
An AP can have an agreement with multiple APs in its neighborhood to perform TXOP sharing (i.e., participate in C-TDMA)
  Two participating APs might have knowledge of each other’s long-term traffic profiles, e.g., SCS agreements
Having knowledge of long-term traffic needs of an AP is not an indicator of its resource needs AP during the sharing AP’s TXOP
  Actual traffic arrival fluctuates around the expected traffic arrival due to jitter and other factors (see figure below)

## Slide 5: Need for Polling/Announcement Frame (contd..)
TXOP sharing without a Poll/Ann. frame at the start of the TXOP :
TXOP sharing with a Poll/Ann. frame at the start of the TXOP:

## Slide 6: Need for Polling/Announcement Frame (contd..)
Furthermore, a candidate shared AP may be unavailable during the TXOP
  E.g., due to OBSS NAV, Co-Ex, AP power save, etc.
Possible that the traffic buffered at a candidate AP does not meet the traffic priority for the shared TXOP determined by the sharing AP
  And hence can’t use the shared portion of the TXOP
When an AP obtains a TXOP, how does it decide whether to share this TXOP and, if so, with whom?
  An AP doesn’t have to share every TXOP that it obtains
  And, if it decides to share a TXOP, it should share the TXOP with the neediest AP
  Blind TXOP sharing will lead to unnecessary overheads and poor performance
TGbn must provide a mechanism for sharing AP to:
  announce its intention to share the TXOP
  poll the candidate APs

## Slide 7: Additional Considerations
Some existing features require an ICF/ICR exchange at the start of a TXOP
  E.g., eMLSR
Some TGbn features propose to have ICF/ICR exchange at the start of a TXOP
  E.g., Co-Ex, AP PS, etc.
  The poll-response mechanism for C-TDMA fits this design
    Poll/response is yet another ICF/ICR
    Can be combined with an ICF/ICR exchange meant for another TGbn feature
    Such approach will improve the overall efficiency of the protocol
The BSRP Trigger frame can be considered as Poll/Announcement frame
  The poll can include candidate shared APs and optionally one or more its associated STAs
  Each responder is assigned a distinct resource unit (RU)
    Allowing the sharing AP to unambiguously identify who responded and who did not
Based on the responses, the sharing AP can decide its TXOP sharing plan
Note: Other forms of ICF for polling at the start of the TXOP can be considered.

## Slide 8: Response to the Polling/Ann. Frame
Polled shared AP(s) provide a response such as interest vs disinterest
  Interest: Nonzero values as the response indicate acceptance
    Exact format of the response is TBD
      BSR Control could be modified/extended for this purpose
      Alternatively, TGbn could define a new frame / A-Control
  Disinterest: All 0s in all BSR Control fields indicates that the polled AP is not interested in utilizing portion of the TXOP
    E.g., when the polled AP does not have any buffers for the indicated AC in the polling frame from the sharing AP

## Slide 9: Summary
To have efficient C-TDMA operation, the Polling/Announcement frame at the start of the TXOP is necessary
  Such a polling/announcement offers benefits over blind TXOP sharing and the TXOP sharing based on only long-term agreements
  Yet another ICF/ICR
  Improved efficiency of C-TDMA procedure
The BSRP Trigger can be used for polling/announcement
  This framework allows a sharing AP to efficiently poll candidate shared APs
  Responses from polled APs help the sharing AP make informed decision about TXOP sharing

## Slide 10: SP1
Do you agree that a TXOP owner AP announces its intention of sharing a portion of the time resource of its TXOP for C-TDMA operation, in an Initial Control frame (exact ICF and name TBD) sent at the beginning of the TXOP and that the frame polls AP(s) with whom it may share the TXOP to determine their interest?
  A TXOP owner AP that intends to share its TXOP is referred to as a sharing AP.
  A candidate AP identified (polled) in the Initial Control frame is referred to as a polled AP.
  The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS.
  Whether or not the sharing AP is mandated to send the Initial Control frame that announces that intention is TBD.

## Slide 11: SP2
Do you agree that, as part of the C-TDMA procedure, a sharing AP shall send a TXOP Allocation frame (exact name TBD) to a single polled AP to share a time portion of its TXOP and the frame is an MU-RTS TXS Trigger frame?
  The duration of the shared TXOP shall be indicated in the Allocation Duration field of the frame.
  The Duration field of the frame is set to the length of time required to transmit the solicited response frame plus one SIFS.

## Slide 12: SP3
Do you support that a sharing AP identifies a shared AP via the AID12 field carried in the User Info field of the sharing AP’s Trigger frame?

## Slide 13: References
[1] Abhishek Patil and et al. , “C-TDMA Frame Sequence,” 23/1895r1, Jan 2024.
[2] Yanjun Sun and et al., “Considerations on Coordinated TDMA (C-TDMA),” 23/0041r0, Jan 2023.
[3] Dibakar Das and et al. , “C-TDMA procedure in UHR,” 23/0261r0, Apr 2023.
[4] Yanjun Sun and et al., “Follow-up on Coordinated TDMA (C-TDMA),” 23/0739r1, Jul 2023.
[5] Si-Chan Noh and et al., “Considerations on Return TXOP between multiple APs,” 23/1327r0, Aug 2023.
[6] Liwen Chu and etc al., “Extended TXOP sharing,” 23/249r1, May 2023.
[7] George Cherian and et al., “Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be,” 19/1582r2, Nov 2019.
[8] Dibakar Das and et al., “C-TDMA Follow-up,” 23/93r2, Mar. 2024.
[9] Geonhwan Kim and et al., “TXOP Protection in C-TDMA,” 24/227r1, Apr. 2024.
[10] Geonhwan Kim and et al., “TXOP Return in C-TDMA,” 24/411r0, Apr. 2024.
[11] Geonhwan Kim and et al., “Coordinated TDMA (Follow up),” 23/1910r1, Nov. 2023.
[12] Si-Chan Noh and et al., “NAV protection for C-TDMA,” 24/375r0, Feb. 2024.
[13] Sanket Kalamkar and et al., “NAV Rule in C-TDMA,” 24/423r0, May 2024.