## Slide 1: TXOP Return in C-TDMA
Authors:
Date: 2024-04-12
Name | Affiliations | Address | Phone | email
Sanket Kalamkar | Qualcomm Technologies Inc. |  |  | sankal@qti.qualcomm.com
Abhishek Patil |  |  |  | 
Gaurang Naik |  |  |  | 
George Cherian |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Duncan Ho |  |  |  | 
Giovanni Chisci |  |  |  | 
Sherief Helwa |  |  |  | 

## Slide 2: C-TDMA Background
C-TDMA allows an AP that owns a TXOP to share a portion of the TXOP time with one or more APs
  The scheme is meant to improve latency and improve system efficiencies by reducing contention/collisions
C-TDMA Sequence:
  The sharing AP polls candidate shared APs via a polling/announcement frame
  The sharing AP triggers TXOP sharing via TXOP Allocation frame
  The shared AP returns unused TXOP (if any) via TXOP Return frame

## Slide 3: Mechanism for Returning the TXOP
CF-End seemed to be an obvious choice. However:
  CF-End resets the NAV for all the devices in the neighborhood
    Intra-BSS NAV is reset for STAs that are 11ax or beyond and belong to the same BSS as the shared AP
    Basic NAV for pre-11ax STAs or STAs that belong to other BSS
  Since the NAV is reset for these devices, they can contend to gain access to the medium during the sharing AP’s TXOP
    Can cause the sharing AP to lose control of the TXOP
      Esp., if the sharing AP is unable to access the medium in SIFS/PIFS after receiving the CF-End
TXOP return in TGbe’s TXS framework is achieved by means of an indication in the CAS Control field
  CAS Control field is carried in a QoS Null or a QoS Data frame transmitted by the shared STA to its associated (sharing) AP
  TGbn C-TDMA could follow the same scheme. However:
    QoS Null or QoS Data frames cannot be exchanged in unassociated state – i.e., between shared and sharing APs

## Slide 4: TXOP Return via a Management frame
Public Action frames are allowed between unassociated STAs
  And thus, permitted between sharing and shared APs
Carry CAS Control (indicating TXOP return) in a Public Action frame
  This could be a new frame defined by UHR
The proposed frame could also carry other information, such as:
  Information related to C-TDMA protocol (such as any updates to the C-TDMA parameters)
  If no additional information is to be carried in the frame body, then the frame can be a null action frame
    i.e., carries only the MAC header containing the CAS Control field
Benefit:
  Since the information is carried within CAS Control (i.e., header) of a mgmt. frame:
    It doesn’t reset the NAV for neighboring devices
    Sharing AP can react w/o having to process contents (i.e., the frame body) of the mgmt. frame
  Consistent with the scheme defined by TGbe TXS framework.

## Slide 5: Optionality of TXOP Return
TXOP return can be conditional and scenario-dependent
  For example, when the sharing AP wants to share the TXOP with more than one AP (after the current shared AP) and/or serve in-BSS clients after the shared portion of the TXOP
The polling and/or allocation frame could carry an indication of whether TXOP return is requested or not
Ability to receive a TXOP return frame could be based on capability of the sharing AP

## Slide 6: Summary
We identified challenges associated with CF-End as a TXOP return frame in C-TDMA
We proposed the use of CAS Control field (indicating TXOP return) in a Public Action frame for returning a shared TXOP
  Consistent with baseline TXOP return in TXS mechanism
  Enables sharing AP to maintain control of the TXOP
  Use of public action frame preserves baseline rules for communication between unassociated STAs.

## Slide 7: SP
Do you agree that, as part of the C-TDMA procedure, TGbn defines a mechanism for an AP, that receives a portion of the time resource from sharing AP, to return the remainder of the allocated time (if any) back to the sharing AP?
  Signaling details are TBD.

## Slide 8: References
[1] Abhishek Patil and et al. , “C-TDMA Frame Sequence,” 23/1895r1, Jan 2024.
[2] Yanjun Sun and et al., “Considerations on Coordinated TDMA (C-TDMA),” 23/0041r0, Jan 2023.
[3] Dibakar Das and et al. , “C-TDMA procedure in UHR,” 23/0261r0, Apr 2023.
[4] Yanjun Sun and et al., “Follow-up on Coordinated TDMA (C-TDMA),” 23/0739r1, Jul 2023.
[5] Si-Chan Noh and et al., “Considerations on Return TXOP between multiple APs,” 23/1327r0, Aug 2023.
[6] Liwen Chu and etc al., “Extended TXOP sharing,” 23/249r1, May 2023.
[7] George Cherian and et al., “Coordinated AP Time/Frequency Sharing in a Transmit Opportunity in 11be,” 19/1582r2, Nov 2019.
[8] Dibakar Das and et al., “C-TDMA Follow-up,” 23/93r2, Mar. 2024.
[9] Geonhwan Kim and et al., “TXOP Protection in C-TDMA,” 24/227r1, Apr. 2024.
[10] Geonhwan Kim and et al., “TXOP Return in C-TDMA,” 24/411r0, Apr. 2024.
[11] Geonhwan Kim and et al., “Coordinated TDMA (Follow up),” 23/1910r1, Nov. 2023.
[12] Si-Chan Noh and et al., “NAV protection for C-TDMA,” 24/375r0, Feb. 2024.
[13] Sanket Kalamkar and et al., “NAV Rule in C-TDMA,” 24/423r0, May 2024.