## Slide 1: Proposal for a TIG for Moving Vehicles Wireless LAN Access
Date: 2024-07-15
Authors:

## Slide 2: Abstract
The number of connected vehicles is growing rapidly
Infotainment is a major use case for connected vehicles with a significant amount of time-sensitive data demand
Current implementations rely solely on a cellular connection for time-sensitive data downlink and uplink for a moving connected vehicle
We propose creation of a TIG for supporting moving vehicles’ WLAN connection via a two-phased approach:
  Phase 1: Target speeds typical in downtown and busy suburban driving (typically ~ 40 km/h or less) and focus only on potential gaps in the MAC layer and above
  Phase 2: Investigate the feasibility of PHY modifications for better Doppler mitigations

## Slide 3: Piecing together the current remedies: Intra & Inter ESS Roaming
MAC issues under high mobility
    Fast and Scalable Scanning and AP Selection:
      Solicited/unsolicited Neighbor Report (802.11k/v/ai), BTM (802.11v), and FILS discovery (802.11ai) – Currently only intra-ESS
      Authentication before association: STA to try to associate with an AP it will succeed to authenticate with
        Fast BSS Transition (FT) allows authentication with target AP before breaking link with current AP– Currently only intra-ESS
        Passpoint (802.11u): STA can identify APs based on Network Address Identifier realms it has credentials for, stored preferences, prior associations, etc.
          ANQP/GAS helpful but not always fast enough
          Realm info (or their hash) included in beacon/probe response more helpful than ANQP-based
    Fast and Scalable Association to Next AP:
      FILS – Helps with resource request booking - Currently only intra-ESS
      802.11bn proposed solutions leveraging ML – Currently only intra-ESS
    Fast, secure, and scalable authentication/secure link establishment with next AP:
      Lighter authentication process: FILS authentication (using EAP-RP), FT, PMKSA Caching, Opportunistic Key Caching, … – Currently only intra-ESS
NOTE: Inter-ESS solutions less addressed and tougher to solve
Chart: Time-To-First-Byte
| Ping | Authentication and DHCP | Association | Scan
Time-To-First-Byte | 0.1 | 2.6 | 0.5 | 5
~ 9.7 secs TTFB
5 secs for scanning

## Slide 4: Piecing together the current remedies: Intra & Inter ESS Roaming – Cont’d
Higher layer issues under high mobility
  Intra-ESS solutions currently available:
    To fix DHCP latency/disruption due to reassigning an IP address:
      802.11ai/FILS IP address configuration
  For inter-ESS, potential solutions might include (but are not limited to):
    Mobile IP
    Potential expansion of the scope of FT (802.11r) and/or FILS (802.11ai)
      Expand Fast BSS Transition to allow IP address acquisition prior to breaking the current AP association
      Allow over-the-air exchange of APs from adjacent ESSs for handover coordination
      APs from adjacent ESS rely on a higher-layer protocol for handover coordination
Chart: Time-To-First-Byte
| Ping | Authentication and DHCP | Association | Scan
Time-To-First-Byte | 0.1 | 2.6 | 0.5 | 5
~ 9.7 secs TTFB
5 secs for scanning (without OCE)

## Slide 5: Tentative Objectives for Phase 1
Take steps toward seamless roaming both for Intra- and Inter- ESS including:
  Fast Target AP Discovery with helpful metrics advertised to help next AP selection
  Make Before Break Link Establishment
  Authentication Before Association
  No IP Address Reacquisition due to AP-AP handover
  Scalability of AP discovery and Authentication

## Slide 6: Proposed Text for the Scope of Automotive WLAN TIG
The Moving Vehicle WLAN Topic Interest Group will investigate a solution comprising current and new mechanisms which can enable non-AP STAs integrated with vehicles to connect to external 802.11 APs while in-motion and to seamlessly roam between APs intra and inter-ESS.

## Slide 7: Conclusion
Requesting support for creation of a TIG for Automotive WLAN Use Case
Phase 1: Lower mobility conditions (< 40 km/hour)
Phase 2: Higher speeds and contingent on the success of phase 1

## Slide 8: Motion
Do you approve the creation of a Topic Interest Group in the IEEE 802.11 Working Group aimed to seek a solution, potentially comprising current and new mechanisms, to enable non-AP STAs integrated with vehicles to connect to external 802.11 APs while in-motion and seamlessly roam between APs intra and inter-ESS?
  Y
  N
  A

## Slide 9: References
80211-2020
802.11-24/378r0
802.11-24/415r1
802.11-24/793r1