## Slide 1: Preemption TXOP
Date: 2024-07-03
Authors:

## Slide 2: Introduction
Latency reduction is one key objective as stated in UHR proposed PAR [1]
Several contributions [2]-[17] have made progress to support low latency medium access by constructing and furnishing the preemption mechanism
In this proposal, we focus on the TXOP level preemption branch, present concepts and essential actions covering the preemption transmission window for the in BSS preemption scenario

## Slide 3: Concept: Preemptor VS Preemptee
In BSS preemption
Preemptor:
  A STA who acquires the preempted transmission duration by initiating preemption
    The STA can be either AP or non-AP
  For traffic of AC2 that takes precedence over the current traffic of AC1, such as higher-priority traffic over lower-priority traffic
Preemptee:
  A non-AP STA who grants or accepts preemption by suspending the current traffic transmission or reception of AC1
    In the top view of traffic delivery, AP helps STAs forward traffic (either DL or UL), but does not generate traffic, only traffic intended for non-AP STA can be preempted
    The non-AP STA is either TXOP holder or TXOP responder
Exceptional scenario: Preempt DL/UL TXOP to transmit UL/DL higher-priority traffic
  Preemptor: EDCAF(AC2)
  Preemptee: EDCAF(AC1)

## Slide 4: Preemptee and Preemptor Identity
Non-AP STA1 is always the preemptee
Case Aa: AP’s DL LL preempts STA1’s UL TXOP
Case Ab: STA2’s UL LL preempts STA1’s UL TXOP
Case Ba: AP’s DL LL preempts STA1’s transmission
Case Bb: STA2’s UL LL preempts STA1’s transmission
Note:
Definition/description of “LL data” is under discussion
Whether to support all cases is TBD
For example, in case Ba, if AP would schedule LL data to STA2 together with data to STA1, we may or may not call this scenario “preemption”

## Slide 5: Hidden Node Preemption Issue and Solution
Hidden node issue: STA1 and STA2 are hidden from each other, collision happens while STA2 initiates preemption
Solution candidates:
either of the following two
  If non-AP STA1 is hidden from STA2, then STA2 shall not initiate preemption during the transmission between STA1 and AP
  If non-AP STA1 is hidden from STA2, then when STA2 initiates preemption and error occurs, STA2 shall not perform error recovery and shall stop initiating preemption
Hidden node issue example
Assumption:
STA1 or AP indicated preemption support in a signal that can be received by STA2

## Slide 6: Tx/Rx Mismatch Due to Tx/Rx Switch and Solution
Tx/Rx mismatch issue1: After Tx to STA1, AP needs to switch from Tx to Rx
Solution: STA2 shall transmit the first preemption frame to AP at least a t0 time after the last PPDU that AP transmits to STA1, no sooner than that
Tx/Rx mismatch issue2: After Rx from STA1, AP needs to switch from Rx to Tx
Solution: STA2 shall transmit the first preemption frame to AP at most a t0 time after the last PPDU that AP receives from STA1, no later than that
  t0: Tx/Rx switch duration

## Slide 7: How Long May Preemptor Preempt
TXOP limit (AC1): EDCA parameters to protect fairness within a BSS
  The longest duration in which a TXOP holder can maintain uninterrupted control of the medium and transmit its data
  The TXOP holder shall, subject to several exceptions, ensure that the duration of a TXOP does not exceed the TXOP limit, when nonzero
Preemption duration limit (AC2)
  For such longest duration, preemptor may preempt the current transmission
  For such longest duration, preemptee would suspend the current transmission
  Preemptor shall ensure preemption duration does not exceed such longest duration/limit
Preempt for transmission with third STA
Preempt DL/UL to transmit UL/DL

## Slide 8: Preemption Duration Limit
Option 1: Preemption duration is counted into the current TXOP
  Preemption duration longest: t2 = TXOP limit(AC1) - t1
  Continuing duration longest: t3 = TXOP limit(AC1) - t1 - t2
Option 2: Preemption duration is counted independently
  t2 = TXOP limit(AC2)
  t3 = TXOP limit(AC1) - t1
Option 3: Indicate new parameters termed such as “Preemption TXOP limits”
  t2 = Preemption TXOP limit(AC2)
  t3 = TXOP limit(AC1) - t1
  TXOP holder indicates Preemption TXOP Limit for the current TXOP, or advertised in the EDCA Parameter Set element in Beacon and Probe Response frames transmitted by the AP
(AC_VI) TXOP limit 3ms
(AC_VO) TXOP limit 1.5ms

## Slide 9: Preemption Duration Protection: Issue
Assumption: TXOP holder protected initial TXOP till time T1 via multiple protection
  Non-AP STA1 is TXOP holder in the figure
Issue: If preemption protected medium till a time < T1, the non-AP TXOP holder may fail to get remaining duration back
AP has no knowledge of how long STA1’s next frame would be, but AP knows T1

## Slide 10: Preemption Duration Protection: Solution
To ensure fairness for preemptee/TXOP holder after preemption ends, at the best effort, preemptor or AP shall
  Transmit at least one frame to indicate duration protection till time T1, or longer than T1
  Preferably till time T1+t2’, such that total transmission duration for AC1 remains T1, not shorted
After preemption ends (indication is TBD), preemptee/TXOP holder can continue transmission w/o contention/backoff
Related STAs may use a new timer to record the preemption duration causing medium busy, or re-use the existing NAV timer
  To be discussed

## Slide 11: Summary
Concept and identity of preemptor and preemptee in several cases
  Non-AP STA is always the preemptee
How to initiate preemption successfully
  Hidden node preemption issue and solution
  Tx/Rx mismatch issue and solution
How long may preemptor preempt
  Preemption duration limit
Preemption duration protection
  To ensure fairness for preemptee/TXOP holder after preemption ends
Notes: In this contribution, we focus on TXOP level preemption mechanism, present concepts and essential actions covering preemption transmission window

## Slide 12: Straw Poll 1
Do you agree that in 11bn the concept of preemptor and preemptee should be defined to facilitate the preemption mechanism?
NOTE – This can be defined along with the concept of preemption

## Slide 13: Straw Poll 2
Do you agree that in 11bn the preemption duration limit/parameter should be defined to facilitate the preemption mechanism?
NOTE – Preemptor or third STA shall ensure preemption duration does not exceed such limit
NOTE – How to defined it is TBD

## Slide 14: Straw Poll 3
Do you agree that in 11bn the non-AP preemption initiator (preemptor)
Shall transmit the first preemption frame to AP at least a some time after the last PPDU that AP transmits, no sooner than that
Shall transmit the first preemption frame to AP at most a some time after the last PPDU that AP receives, no later than that
NOTE – The “some time ” is TBD

## Slide 15: Straw Poll 4
Do you agree that in 11bn the preemption duration protection should at least cover the initial ending time that the TXOP holder protected?
NOTE – Whether the preemption duration protection can extend the initial TXOP ending time is TBD

## Slide 16: Straw Poll 5
Do you agree that in 11bn the preemption duration protection can extend the initial ending time that the TXOP holder protected?
NOTE – For how longer it can extend is TBD

## Slide 17: References
11-23/480r3, UHR Proposed PAR
11-23-0018-01-0uhr-low-latency-support-in-uhr
11-23-0092-00-0uhr-preemption
11-23-1886-03-00bn-preemption-techniques-to-meet-low-latency-ll-targets
11-23-2076-03-00bn-multiple-channel-access-in-preemption-sequence
11-24-0091-01-00bn-enhanced-scheduling-method-for-low-latency-traffic-follow-up
11-24-0103-01-00bn-txop-level-preemption-for-low-latency-application-in-802-11bn
11-24-0131-00-00bn-signaling-of-preemption
11-24-0168-00-00bn-txop-preemption-in-11bn
11-24-0247-00-00bn-considerations-on-ll-preemption
11-24-0390-00-00bn-a-uniform-procedure-for-preemption
11-24-0391-00-00bn-legacy-sta-and-obss-issues-for-preemption
11-24-0416-00-00bn-target-sta-prioritization-in-edca-based-preemption-mechanisms-during-a-dl-txop
11-24-0431-01-00bn-signal-for-preemption-request
11-24-0442-03-00bn-latency-reduction-for-immediate-real-time-application-traffic-transmission
11-24-0470-00-00bn-rethinking-preemption
11-24-0804-00-00bn-the-transmission-of-preemption-request-frame