## Slide 1: Considerations on NPCA
Date: 2024-06-18
Authors:

## Slide 2: Introduction
Non-Primary Channel Access (NPCA) has been widely discussed in TGbn group[1-9].
The motion for NPCA passed at the May 2024 meeting.
TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
  The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions

## Slide 3: Motivation
If the only one NPCA primary channel is also known to be busy due to OBSS traffic or other TBD conditions?
OBSS’s bandwidth or other ongoing/potential interferences (including various coexistence issues) may cover or interfere with the predefined NPCA primary channel.
Slide 3
AP
320MHz
160S
160P
STA
160 MHz
20P
OBSS
80 MHz
NPCA primary channel
within STA’s operating bandwidth

## Slide 4: Motivation
AP
320MHz
160P
20P
OBSS
80 MHz
NPCA primary channel
within STA’s operating bandwidth
We could set it away from the primary channel to reduce the probability of being interfered with at the same time.
STA
160 MHz

## Slide 5: Motivation
AP
320MHz
160P
20P
OBSS
80 MHz
NPCA primary channel
within STAs’ operating bandwidth
STA 2
80 MHz
We could set it away from the primary channel to reduce the probability of being interfered with at the same time.
The position may still need to be adjusted under certain conditions. For example, assuming that the NPCA primary channel is set within the STAs' operating bandwidth, then the position may be different when there are 80MHz STAs join in NPCA or only 160MHz STAs participating in NPCA.
STA
160 MHz

## Slide 6: Motivation
The position of the NPCA primary channel is critical.
Setting only one NPCA primary channel has low implementation complexity. However, the minimum operating bandwidth of all STAs participating in NPCA may change and the channel conditions change dynamically, a fixed position is not always the best choice.
AP
320MHz
160P
20P
OBSS
80 MHz
STA 2
80 MHz
STA
160 MHz
NPCA primary channel
within STAs’ operating bandwidth

## Slide 7: Proposal: NPCA primary channel update
During the NPCA capability negotiation or update phase, AP determines the NPCA primary channel to set or update based on OBSS bandwidth and other ongoing or potential interferences (including various coexistence issues). AP got related indications during or before NPCA capability negotiation or update phase. NPCA primary channel updates occur when necessary, the specific conditions for triggering updates are not limited.
AP announces the NPCA primary channel and the time it becomes effective to STAs. After it takes effect, the STA can switch to it when NPCA conditions are met.
STA reports switch delay information if necessary.
STA and AP use the switch delay information to perform subsequent operations, such as determining whether to participate in NPCA and whether to switch (e.g., the switch delay is less than a time threshold 𝑻_1; the NAVs minus switch delays required for round trip is greater than 𝑻_2).
AP announces the channel and the effective time
NPCA primary channel update
Subsequent operations
STA reports switch delay

## Slide 8: Summary
In this contribution, we propose to update NPCA primary channel. OBSS’s bandwidth or other ongoing/potential interferences (including various coexistence issues) may cover or interfere with the predefined NPCA primary channel.
AP announces the NPCA primary channel and the time it becomes effective. After it takes effect, the STA can switch to it when NPCA conditions are met.
The mechanism to update the NPCA primary channel to adapt to the channel conditions and NPCA STAs’ capability is conducive to realizing the original intention of non-primary channel access.

## Slide 9: References
[1] 11-23/34, Non-primary channel utilization
[2] 11-23/1414, Secondary channel usage follow up
[3] 11-23/961, UHR secondary channel access
[4] 11-23/797, Non-primary channel access
[5] 11-23/1891, Nonprimary channel access - follow up
[6] 11-23/2005, Non-primary channel access (NPCA)
[7] 11-24/427, Enabling Non-Primary Channel Access
[8] 11-24/486, Some considerations on non-primary channel access
[9] 11-24/70, Some details about non-primary channel access