## Slide 1: Mirror Symmetric 20 MHz DRU Tone Plan within 242 RRU Boundary
Date: 2024-07-14
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In [1], 20 MHz DRU tone plan which tone range is within 242 RRU boundary was proposed
In [2], mirror symmetric pilot tones were proposed based on the 20 MHz DRU tone plan in [1]
In [3], we proposed 20 MHz DRU tone plan which has mirror symmetric property for both data and pilot tones
  Some of the members raised a concern about the tone range which is not within 242 RRU boundary and can cause performance degradation when this tone plan is applied to a certain 20 MHz channel in a wider bandwidth
In this contribution, we propose a new 20 MHz DRU tone plan which is mirror symmetric for both data and pilot tones and guarantees 242 RRU boundary

## Slide 3: Proposed 20 MHz DRU Tone Plan
Proposed 20 MHz DRU tone plan
  [-120 ~ -4, +4 ~ +120] tones are allocated to DRUs and [-3, -2, +2, +3] tones are additionally allocated to 106 DRUs
    Tone range is within 242 RRU
  Tone spacing of 26 DRU is multiples of nine even around DC
    Low PAPR and better smoothing gain can be achieved
  The following pairs are mirror symmetric
    {26 DRU_a, 26 DRU_10-a}, {52 DRU_a, 52 DRU_5-a}, {106 DRU_1, 106 DRU_2}
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 

## Slide 4: PAPR Comparison
PAPR comparison
  Two tone plans have almost same PAPR
26 DRU
106 DRU
52 DRU
26 DRU
106 DRU
52 DRU
BPSK
QAM

## Slide 5: Comparison for 20 MHz DRU Tone Plans
Comparison
  Most of the previous Wi-Fi versions have symmetric tone plans
    If we make the DRU tone plan symmetric, we can use a similar approach for implementation used in the previous Wi-Fi.
  For PHY processing, we can only have information for some of the DRUs and we can use that information for their symmetric pair DRUs
  Further, 40 MHz tone plan proposed in [1] is almost symmetric, and thus, it would be better to make the 20 MHz tone plan symmetric as well
 | PAPR | Power Boosting Gain | Channel Smoothing | Within 242 RRU Boundary | Implementation
Proposed tone plan | Almost same | Same | Possible | Yes | Simpler w/ mirror symmetry
Tone plan in [1] |  |  |  |  | Not symmetric

## Slide 6: Proposed Pilot Tones for 20 MHz DRU Tone Plan (1/6)
Design for pilot tones
  We use two options for pilot tones proposed in [2] which are mirror symmetric
Option 1 for 26 DRUs
  26 DRUs are presented in the increasing order of first tone index to show how DRU indices are allocated
  Both pilot and data tones are mirror symmetric in the following pair
    {26 DRU_a, 26 DRU_10-a}  These are also the same DRU type*
*In forward or backward order of DRU, data and pilot tones are aligned with other DRUs
26 DRU_1
26 DRU_8
26 DRU_3
26 DRU_5
26 DRU_7
26 DRU_2
26 DRU_9
26 DRU_4
26 DRU_6

## Slide 7: Proposed Pilot Tones for 20 MHz DRU Tone Plan (2/6)
Option 1 for 52 DRUs
  Both pilot and data tones are mirror symmetric in the following pair
    {52 DRU_a, 52 DRU_5-a}  These are also the same DRU type
  Compared to option 2, pilot tone gap in each 52 DRU is rather narrow
52 DRU_1
52 DRU_4
52 DRU_2
52 DRU_3

## Slide 8: Proposed Pilot Tones for 20 MHz DRU Tone Plan (3/6)
Option 1 for 106 DRUs
  For a sufficient gap between pilot tones and mirror symmetry, we propose the following pilot tones (red tones)
    106 DRU_1: [-52, -19, 74, 107]
    106 DRU_2: [-107, -74, 19, 52]
  As a result, both pilot and data tones are mirror symmetric between two 106 DRUs and these are also the same DRU type
106 DRU_1
{-3, 2} tones are added
106 DRU_2
{-2, 3} tones are added

## Slide 9: Proposed Pilot Tones for 20 MHz DRU Tone Plan (4/6)
Option 2 for 26 DRUs
  26 DRUs are presented in the increasing order of first tone index to show how DRU indices are allocated
  Both pilot and data tones are mirror symmetric in the following pair
    {26 DRU_a, 26 DRU_10-a}  These are also the same DRU type
26 DRU_1
26 DRU_8
26 DRU_3
26 DRU_5
26 DRU_7
26 DRU_2
26 DRU_9
26 DRU_4
26 DRU_6

## Slide 10: Proposed Pilot Tones for 20 MHz DRU Tone Plan (5/6)
Option 2 for 52 DRUs
  Both pilot and data tones are mirror symmetric in the following pair
    {52 DRU_a, 52 DRU_5-a}  These are also the same DRU type
  Compared to option 1, pilot tones in each 52 DRU are sufficiently spaced
52 DRU_1
52 DRU_4
52 DRU_2
52 DRU_3

## Slide 11: Proposed Pilot Tones for 20 MHz DRU Tone Plan (6/6)
Option 2 for 106 DRUs
  For a sufficient gap between pilot tones and mirror symmetry, we propose the following pilot tones (red tones)
    106 DRU_1: [-73, -23, 53, 103]
    106 DRU_2: [-103, -53, 23, 73]
  As a result, both pilot and data tones are mirror symmetric between two 106 DRUs and these are also the same DRU type
106 DRU_1
{-3, 2} tones are added
106 DRU_2
{-2, 3} tones are added

## Slide 12: Conclusion
We have proposed 20 MHz DRU tone plan and have compared it with the tone plan proposed in [1]
  Two tone plans have the same power booting gain and similar performance in terms of PAPR and smoothing and guarantees 242 RRU boundary
  From the implementation point of view, our proposed tone plan may be more desirable based on the mirror symmetric property
We have also proposed pilot tones for our 20 MHz DRU tone plan by using two options in [2]
  Our complete tone plan is totally mirror symmetric
  The proposed pilot tones can significantly reduce DRU types
  We prefer option 2 since pilot tones are more sufficiently spaced than option 1

## Slide 13: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  For DRU tone plan in 20 MHz distribution bandwidth, the following DRUs are defined
    Nine 26 DRUs
    Four 52 DRUs
      Each 52 DRU is combined by two different 26 DRUs
    Two 106 DRUs
      Each 106 DRU is combined by two different 52 DRUs and two different tones which are not used in any 26 or 52 DRUs
Y/N/A: //

## Slide 14: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  Data and pilot subcarrier indices for DRUs in a 20 MHz UHR PPDU are defined in following table
Y/N/A: //
Data and pilot subcarrier indices for Distributed Tone RUs (DRUs) in a 20 MHz UHR PPDU |  |  |  |  | 
DRU type | DRU index and subcarrier range |  |  |  | 
26-tone DRU i=1:9 | DRU1 [-120:9:-12, 6:9:114] | DRU2 [-115:9:-7, 11:9:119] | DRU3 [-118:9:-10, 8:9:116] | DRU4 [-113:9:-5, 4:9:112] | DRU5 [-117:9:-9, 9:9:117]
 | DRU6 [-112:9:-4, 5:9:113] | DRU7 [-116:9:-8, 10:9:118] | DRU8 [-119:9:-11, 7:9:115] | DRU9 [-114:9:-6, 12:9:120] | 
52-tone DRU i=1:4 | DRU1 26-tone [DRU1, DRU2] |  | DRU2 26-tone [DRU3, DRU4] |  | 
 | DRU3 26-tone [DRU6, DRU7] |  | DRU4 26-tone [DRU8, DRU9] |  | 
106-tone DRU i=1:2 | DRU1 26-tone [DRU1~4], [-3, 2] |  | DRU2 26-tone [DRU6~9], [-2, 3] |  | 

## Slide 15: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  Pilot subcarrier indices for DRUs in a 20 MHz UHR PPDU are defined as follows
    26 DRU_1: [-93, 33]
    26 DRU_2: [-43, 83]
    26 DRU_3: [-73, 53]
    26 DRU_4: [-23, 103]
    26 DRU_5: [-63, 63]
    26 DRU_6: [-103, 23]
    26 DRU_7: [-53, 73]
    26 DRU_8: [-83, 43]
    26 DRU_9: [-33, 93]
    52 DRU_1: [-93, -43, 33, 83]
    52 DRU_2: [-73, -23, 53, 103]
    52 DRU_3: [-103, -53, 23, 73]
    52 DRU_4: [-83, -33, 43, 93]
    106 DRU_1: [-73, -23, 53, 103]
    106 DRU_2: [-103, -53, 23, 73]
Y/N/A: //

## Slide 16: References
[1] 11-24-0468-01-00bn-dru-tone-plan-for-11bn
[2] 11-24-0800-01-00bn-dsicussions-on-dru-pilot-design-principles
[3] 11-24-0767-00-00bn-20-mhz-tone-plan-and-pilot-design-for-dru-follow-up