## Slide 1: Thoughts on UHR-LTF for DRU
Date: 2024-07-14
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Abstract
In this contribution, we provide our thoughts on UHR-LTF design for DRU and discuss how to transmit UHR-LTF in a PPDU using DRUs

## Slide 3: Thoughts on UHR-LTF design for DRU (1/2)
For a DRU transmission, we suggest to design a new 4x UHR-LTF sequence in each distribution bandwidth
  4x UHR-LTF sequence means that it has coefficients on all of the tones overlapped with DRUs defined in each distribution bandwidth and its symbol length in the time domain is 12.8 us + GI
The reasons we need 4x UHR-LTF are
  We don’t have to conduct interpolation which may not be reliable for channel estimation since tone spacing of DRU is too large
  The same power boosting gain as the data part can be achieved
The reasons to design new UHR-LTF are
  Tone range may not match between the conventional LTF and the DRU tone plan
  The conventional LTF leads to high PAPR when DRU is used
    Please see Appendix for PAPR results of the conventional LTF when DRUs proposed in [1] are used

## Slide 4: Thoughts on UHR-LTF design for DRU (2/2)
The reasons we need UHR-LTF for each distribution bandwidth are
  DRU tone plans are designed based on the distribution bandwidth
  If we design UHR-LTF in each bandwidth not distribution bandwidth, it may be hard to optimize the PAPR given various distribution bandwidth modes and hybrid PPDUs
    Note that TGbn approved to allow 80 MHz and 20+20+40 MHz distribution bandwidth modes in 80 MHz PPDU
    We also discussed 20+40 MHz distribution bandwidth mode in 80 MHz with 20 MHz puncturing
    80 MHz, 160 MHz and 320 MHz hybrid PPDUs were discussed and DRU can be used in a specific 40 MHz, 80 MHz or 160 MHz channel with various distribution bandwidth modes in these PPDUs

## Slide 5: How to Transmit UHR-LTF for DRU (1/2)
In a PPDU using DRUs, UHR-LTF sequence corresponding to the distribution bandwidth of the DRUs is applied regardless of the PPDU bandwidth
  For example, when 20+20+40 MHz distribution bandwidth mode is used in 80 MHz PPDU, 20 MHz UHR-LTF, 20 MHz UHR-LTF and 40 MHz UHR-LTF are applied to 20 MHz, 20 MHz and 40 MHz channels, respectively
When a non-AP STA transmits TB PPDU using a certain DRU, UHR-LTF coefficients overlapped with the DRU are only used just as 11be
  I.e., UHR-LTF coefficients are set to zero for tones other than those overlapped with the DRU

## Slide 6: How to Transmit UHR-LTF for DRU (2/2)
The number of UHR-LTF symbols in a PPDU are determined by the same rule as 11be, i.e., it depends on NSS
  According to the allowed NSS for DRU, available sets of P-matrix and R-matrix we need to consider for PAPR optimization of UHR-LTF are different
    Note that data and pilot tones are multiplied by entries of P-matrix and R-matrix, respectively
    All of the entries of these two matrices are 1 or -1 except for 6 by 6 P-matrix which consists of exp(-j2πn/6)
  Thus, to design UHR-LTF by taking into account PAPR, we need to determine the maximum allowed NSS for DRU
    We simply suggest that the maximum allowed NSS for DRU is the same as that of RRU
    We need further discussion whether to support MU MIMO for DRU
    Note that 11be allows maximum 4 and 8 spatial streams for SU MIMO and MU MIMO, respectively, in a TB PPDU

## Slide 7: Summary
We have suggested to design a new 4x UHR-LTF sequence for a DRU transmission in each distribution bandwidth and have discussed reasons behind our suggestion
We have also discussed how to transmit UHR-LTF when DRU is used in a PPDU
  UHR-LTF corresponding to the distribution bandwidth is used
  UHR-LTF coefficients overlapped with an assigned DRU are only used
  The number of UHR-LTF symbols depends on NSS
    We have suggested that the maximum allowed NSS for DRU is the same as that of RRU
    Whether to support MU MIMO for DRU needs further study

## Slide 8: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  For a DRU transmission, a new 4x UHR-LTF sequence is defined in each distribution bandwidth
    4x UHR-LTF sequence means that it has coefficients on all tones overlapped with DRUs defined in each distribution bandwidth and its symbol length in the time domain is 12.8 us + GI
Y/N/A: //

## Slide 9: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  In a PPDU using DRUs, a UHR-LTF sequence corresponding to the distribution bandwidth of the DRUs is used regardless of the PPDU bandwidth
Y/N/A: //

## Slide 10: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  When a non-AP STA transmits TB PPDU using a certain DRU, UHR-LTF coefficients are set to zero for tones other than those overlapped with the DRU
Y/N/A: //

## Slide 11: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  The maximum allowed NSS for DRU is the same as that of RRU
    Whether to support MU MIMO for DRU is TBD
Y/N/A: //

## Slide 12: References
[1] 11-24-1096-00-00bn-mirror-symmetric-20-mhz-dru-tone-plan-within-242-rru-boundary

## Slide 13: Appendix
Maximum PAPR for 4x EHT-LTF sequence in 20 MHz for DRU and RRU transmission
  Tone plan proposed in [1] is used to calculate PAPR for DRU
  Maximum 8 spatial streams are considered
  Upper values are for DRU and lower values are for RRU
26 RU_1 | 26 RU_2 | 26 RU_3 | 26 RU_4 | 26 RU_5 | 26 RU_6 | 26 RU_7 | 26 RU_8 | 26 RU_9
4.89 3.78 | 5.84 3.67 | 6.59 3.67 | 5.54 3.78 | 3.91 3.82 | 4.05 3.78 | 5.10 3.67 | 4.24 3.67 | 6.29 3.78
52 RU_1 |  | 52 RU_2 |  |  | 52 RU_3 |  | 52 RU_4 | 
5.96 4.90 |  | 5.71 5.12 |  |  | 7.55 5.12 |  | 7.24 4.90 | 
106 RU_1 |  |  |  |  | 106 RU_2 |  |  | 
5.32 4.81 |  |  |  |  | 6.94 5.30 |  |  |