## Slide 1: Post-Quantum 802.11
Date: 2025-03-11
Authors:

## Slide 2: Abstract
This submission discusses current state of Post-Quantum algorithms and what their use in 802.11 might look like.
It is a justification for a call for the formation of a Post Quantum Study Group in 802.11

## Slide 3: Post-Quantum Cryptography
Today all of our public key crypto is based on two hard problems:
  Factoring large numbers
  Discrete logarithm problem
Our secure systems would become insecure if one (or both) of those were broken
A quantum computer, which does not exist yet, will be able to break both of these
Such a computer will exist in the (very near) future
We need to plan for a post-quantum future with 802.11

## Slide 4: Mosca Theorum
“There is a 1 in 7 chance that some fundamental public-key crypto will be broken by quantum by 2026, and a 1 in 2 chance of the same by 2031.” – Dr. Michele Mosca, (April 2015)
If encrypted data needs to be safe for X years; and,
If it takes Y years to deploy a post-quantum solution; and,
If a post-quantum computer will exist in Z years
Then if (X + Y) > Z you need to worry
Y
X
Z
Your secrets revealed!
time

## Slide 5: Current State of PQ Algorithms
NIST held a nearly decade long, multi-round competition for PQ algorithms
  Separate tracts for key exchange, and signature algorithms
  Characteristics considered included (not exclusively):
    Efficiency in hardware and software
    Memory requirements
    Ease of implementation
Finalists announced in 2023 (“ready for 2024”)
  CRYSTALS-Kyber (key establishment) covered in FIPS 203
  CRYSTALS-Dilithium (signature) covered in FIPS 204
  SPHINCS+ (signature) covered in FIPS 205
  FALCON (signature) FIPS TBD

## Slide 6: Module-Lattice-based (ML) Key-Encapsulation Mechanism (KEM)
A KEM is a set of algorithms constructed to allow for two parties to establish a shared secret over a public medium
ML-KEM (FIPS 203) defines such a construct using Kyber’s public key encryption algorithm and three hash functions
Three parameter sets defined with increasing security
  ML-KEM-512 providing security strength of 128bits
  ML-KEM-768 providing security strength of 192bits
  ML-KEM-1024 providing security strength of 256bits

## Slide 7: ML-KEM
KeyGen()
  Key generation function creates encapsulation key and decapsulation key
Encaps()
  Encapsulation function takes encapsulation key and produces ciphertext and a secret
Decaps()
  Decapsulation function takes decapsulation key and ciphertext and produces a secret
KeyGen
encapsulation key
decapsulation key
ciphertext
Encaps
Decaps
Bob
Alice
Bob’s copy of shared secret
Alice’s copy of shared secret
Three Functions

## Slide 8: ML-KEM
Key establishment, sort of like Diffie-Hellman
  Two message exchange:
    Alice generates her encapsulation key and sends it to Bob
    Bob sends Alice ciphertext
  Both sides generate a secret
  Exchange is unauthenticated!
ML-KEM does Implicit Rejection
  If Alice fails to properly decapsulate the ciphertext, Decaps() will return a bogus value, each side will then have different secrets
  Need to do a key-confirmation step to ensure success
ML-KEM is intended to be treated as a black box
  KYBER public key encryption algorithm cannot be used stand-alone
  Construct uses Fujisaki and Okamoto (FO) transform to obtain IND-CCA security from weaker IND-CPA PKE algorithm

## Slide 9: Using ML-KEM in 802.11
What 802.11 authentication protocols can use ML-KEM?
  EAP-TLS… let the IETF deal with that
  FILS does asymmetric key agreement today
    STA sends Diffie-Hellman exponential (802.11 auth request)
    AP sends Diffie-Hellman exponential (802.11 auth response)
ML-KEM-FILS!
  STA sends its encapsulation key (802.11 auth request)
  AP sends ciphertext (802.11 auth response)
Algorithm | Encaps key | Decaps key | ciphertext | shared secret
ML-KEM-512 | 800 | 1632 | 768 | 32
ML-KEM-768 | 1184 | 2400 | 1088 | 32
ML-KEM-1024 | 1568 | 3168 | 1568 | 32

## Slide 10: FILS Authentication
Signatures exchanged in assoc req/resp
DILITHIUM signatures are too big!
SPHINCS+ is bigger
FALCON signatures would fit in an MSDU!
FALCON uses floating point operations that must be performed in constant time though 
Algoritm | Public Key | Signature Size
FALCON-512 | 897 | 618
FALCON-1024 | 1793 | 1234
Algorithm | Public key | Signature Size
ML-DSA-44 | 1312 | 2420
ML-DSA-65 | 1952 | 3293
ML-DSA-87 | 2592 | 4595

## Slide 11: ML-KEM-FILS
Using ML-KEM in 802.11 authentication req/resp
Using FALCON in 802.11 association req/resp
But how to pass FALCON public key?
  Certificate has ASN.1 goo, identity, public key, extra attributes, issuer signature
  Certificate + signature in association frame might be too much
We could extend FILS to a 6 message exchange:
  ML-KEM in auth frames 1 and 2
  Certificate/pubkey exchange* in auth frames 3 and 4
  Signature authentication in association frames
Fragmentation/reassembly of 802.11 assoc frames? Maybe necessary anyway if FALCON is not realistic
* Could be privacy protected using a secret derived from ML-KEM exchange

## Slide 12: Authentication without Signatures
Assuming
  Alice and Bob have long-term encapsulation keys
  Alice and Bob can trust each others encapsulation keys somehow
Run ML-KEM twice: Alice uses Bob’s key in Encaps() to him, Bob uses Alice’s key in Encaps() to her
Both secrets are bound to the transmitted ciphertexts in a KDF to produce a single shared secret
This is analogous to the “encrypted nonce” method of authentication in IKEv1 (RFC 2409)
Completely deniable! Let’s call it The Bart Exchange
  “I didn’t do it. Nobody saw me do it. You can’t prove anything”
  -- Bart Simpson

## Slide 13: Bart: Authentication without Signatures
Alice KeyGen
Bob KeyGen
encapsulation key, E1
decapsulation key
ciphertext, C2
Encaps
Decaps
Alice’s copy of K1
Bob’s copy of K1
Encaps
Bob’s copy of K2
Decaps
Alice’s copy of K2
encapsulation key, E2
decapsulation key
ciphertext, C1
K = HKDF-Expand(K1 | K2, C1 | C2 | E1 | E2)
K = HKDF-Expand(K1 | K2, C1 | C2 | E1 | E2)
out of band
Bob
Alice

## Slide 14: Authentication without Signatures
Two-message exchange authenticates peer and key!
Resulting shared secret is bound to both ML-KEM invocations as well as the ciphertext transcript
Then a two-message proof-of-possession exchange
Simple auth+assoc exchange like current FILS
How to signal which key to use?
  AP advertises (a hash of) its encapsulation key in beacons
  STA sends (a hash of) its encapsulation key along with the ciphertext in first message protected with secret from ML-KEM?
But how to perform the out-of-band portion?
  Manual configuration?
  Certified encapsulation keys obtained somehow? QR code?
Could define a “what’s your KEM cert?” GAS exchange

## Slide 15: QR code of ML-KEM encaps keys
ML-KEM-512
ML-KEM-768
Note: they are base64-encoded

## Slide 16: What About Password/PSK Auth?
SAE uses the dragonfly exchange and that is not a simple Diffie-Hellman, it cannot use ML-KEM as a drop-in replacement for its public key cryptography
Is a PQ PAKE possible? Yes!
  CAKE by Beguinet et al describes a PQ PAKE but it, unfortunately, requires looping similar to SAE’s “hunting-and-pecking” to get a suitable string to encrypt– that is not desirable
  I-D draft-veitch-kemeleon specifies several encodings of ML-KEM encaps keys and ciphertexts into random bit strings, one of which produces a suitable output without looping
  Possible to use a variant of the Encrypted Key Exchange (by Bellovin and Merritt) with the random bitstring output of Kemeleon
  NoIC and CHIC are also PQ PAKEs we might be able to use in 802.11, there may be others

## Slide 17: Other Potential PQ Work in 802.11
There are other public key-based algorithms in 802.11, but are suitable for PQ
  OWE? ML-KEM could replace Diffie-Hellman
    STA sends encapsulation key in authentication frame seq=1
    AP sends ciphertext in authentication frame seq=2
  AP PeerKey? Same as OWE….
We also need to strengthen the 4-way Handshake by using SHA3 algorithms with PQ-enabled exchanges
But do we need a PQ OWE? To address security in 6GHz, probably yes. PQ PeerKey?
There is work to be done and times-a-wasting!

## Slide 18: Summary
A quantum computer would be able to break all the key agreement and signatures we do today– FILS, SAE, OWE, all EAP methods including EAP-TLS.
What protocols do we need to modify?
802.11 is a transient medium but how long do we want to protect our messages from exposure?
How long will it take to deploy a solution?!?
Remember Mosca Theorum: If (X+Y)>Z then Trouble!
We need to think about what to do to be ready for a post-quantum world
It’s 2025 so the “ready for 2024” algorithms are ready
Time to form a Post Quantum Study Group in 802.11. Please vote “Yes” in the plenary!

## Slide 19: References
FIPS 203-- https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.203.ipd.pdf
Cake– https://eprint.iacr.org/2023/470
KEMeleon– https://www.ietf.org/archive/id/draft-veitch-kemeleon-00.html
EKE-– https://www.cs.columbia.edu/~smb/papers/neke.pdf
CHIC– https://eprint.iacr.org/2024/308.pdf
NoIC– https://eprint.iacr.org/2025/231.pdf