## Slide 1: Vendor Specific PHY Options With Minimal PHY Changes – Follow-Up
Jun 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: Motivation for Standardized PHY-level Vendor Specific Signaling Mostly a repeat from [1]
Goals:
  Signal the presence of proprietary PHY-layer features in PPDUs to devices in the transmitter’s eco-system
  Avoid confusing devices outside their eco-system by conforming to the 802.11 standard
Stakes are raised with U-SIG
  This needs to support many generations of 802.11 MAC/PHY amendments and many vendors/eco-systems
  Any misuse of reserved fields or VS-redefinition of standardized fields runs the risk that the misuse/redefinition will be exposed in future amendments
The MAC has rich and mature mechanisms for safe feature experimentation, prototyping and deployment
  Vendor Specific (sub)elements, and (Public) Action frames
  Some of these proprietary features didn’t work out, and did not burden the 802.11 standard
  Some of these proprietary features created high value and were returned to 802.11 and have been proposed/accepted as standardized features
    i.e., vendor specific extensions support a rich and healthy 802.11 eco-system
Let’s create a safe environment for PHY experimentation, prototyping and deployment too
  And can we do this with minimal PHY changes?  i.e., also some MAC changes

## Slide 3: UHR (SU)/MU PPDU Perfect Identification of Vendor-Specific PPDUs is Not Required
Axiom:
  If a) a STA attempts to receive a PPDU not intended for the STA, and the STA fails to successfully receive the PSDU due to vendor specific PHY functionality and b) the PHY still sets CCA as usual, then there is near-zero cost and this situation does not need to be avoided by design.

## Slide 4: Vendor Specific Signaling Requirements when seeking minimization of PHY changes – Top Level
A STA may negotiate vendor specific behavior as a recipient with a peer using upper layer signaling (e.g., MAC-level vendor-specific negotiation)
The vendor specific behavior must not affect information for third party STAs:
    PPDUs containing RTS, CTS, CF-End (and likely MU-RTS, Ack, BA) must be unchanged
    LSTF + LLTF + LSIG + RLSIG + version independent fields of the USIG must be unchanged
    Yet-to-be-defined fields intended for third party STAs must also be unchanged (i.e., U-SIG)
Thus, for static VS behavior negotiated with a subset of the peers, the agreement must include a way for transmitting peers in the subset to identify PPDUs intended for the STA uniquely wrt PPDUs sent by peers not in the subset*
  See next slide
If the VS behavior is dynamic (i.e., can change per PPDU)
  The “static” requirements are still needed
  As well, there needs to be a way to signal the dynamic parameters (i.e., via per-PPDU signaling)

## Slide 5: The Problem Applies Equally to Clients and APs
VS
VS
No PPDU identificatn required after second peer negotiates same VS behavior*
VS
Ditto
VS1
No PPDU identificatn required
VS
VS2
VS
A: 1 Peer
B: 1++ peer uses VS signaling, 1++ peer does not
VS
No PPDU identificatn required after second peer negotiates same VS behavior*
VS
VS
C: All peers use the same VS signaling
Ditto
VS1
VS2
D: 1++ peer uses VS1 signaling, 1++ peer uses VS2 signaling
No PPDU identificatn required
Client Scenarios
AP Scenarios
PPDU identificatn required
PPDU identificatn required
PPDU identificatn required
PPDU identificatn required
Notes: *PPDU identification beforehand is required else limiting the VS behavior to certain (e.g., modern) PHY formats and using certain (e.g., legacy such as NON-HT) PHY formats on a link until the VS negotiation completes is an alternative solution to this, but adds new and complicated (e..g, time-varying) format selection rules that can extend past association.

## Slide 6: Options to identify received PPDUs with different VS behavior, while minimizing PHY changes: STA-ID is most promising
Option | Position* in PPDU | Analysis (see next slides for more detail)
BSS Color | Very early |  Not unambiguous, not adequate (see [2]); useless for APs
Reserved USIG bit(s) | Very early |  U-SIG bits need to support multiple future PHY generations; allocating some of these bits for VS purposes was discussed multiple times in TGbe but never accepted.
New VS SIG field (see 24/0461) | Very early |  Greater PHY changes; some test complexity concerns (see [2])
STA-ID | Early | () Reliable, unless device has virtual APs/STAs in different BSSs, and there is an STA-ID collision or there is the broadcast RU
Pad bits in UHRSIG | Middling | (~) Lighter PHY changes
Waveform, such as transmitting information in the UHTLTF null subcarriers | Middling-Late |  Greater PHY changes
Service field | Late | (~)
PHY Pad bits in the Data field | Very late |  Too late to be useful
 | *The earlier in the PPDU the better | 

## Slide 7: AID is most promising …
AID Rule: A device wishing to negotiate VS behavior as a recipient with a peer shall ensure that the AID in use with the peer is different from the AID in use with other peers not using that VS behavior
  Easy for an AP (it is an AID maker); hard for a non-AP STA (it is an AID taker)
Don’t use PHY VS features before association – tolerable limitation
Don’t use PHY VS features with the Broadcast RU – tolerable limitation
Enable non-SP STA to veto AIDs that break the AID Rule – new protocol
With 802.11bi, to help non-AP STAs hide in the crowd, clients can change all their parameters (including AIDs) at the same time, at epoch boundaries, then AID could change regularly (coordinated by the AP).
  Since future AID(s) are determined well before their upcoming epoch boundaries so, in the rare case of planned AID(s) violating the AID Rule, the non-AP STA can veto such AIDs and solicit updated AID(s)
Requirements summary:
  By association, the non-AP STA can preemptively veto certain AIDs (e.g., its in-use AIDs), and
  Post-association, and only needed if 802.11bi is in use, the non-AP STA can veto upcoming AID assignment(s) before the applicable epoch(s) (when and if needed)

## Slide 8: Protocols to Achieve AID Vetoing by and after association
By assoc option | Description |  | Analysis
A | Define a new “AID List Veto element”, sent in Assoc Req, with an “AID List Veto field” that lists the lists AIDs that the STA wishes not to be assigned. |  |  Completely precludes AIDs violating the AID Rule at association
S/T/U/V | Vetoing protocol performed very quickly after association, before any (EHT)/UHR PPDUs are be sent |  The peer does not understand the need to avoid (EHT)/UHR PPDUs initially, so this fails; a fix requires extra complexity (i.e., A is cleaner). | 
Post-assoc option | 802.11bi optimi-zed? | Description |  | Analysis | Analysis | Analysis
S | N | Define a protected request frame to carry the AID List Veto element post-assoc + a response frame to carry the new AID. |  |  If exchanged before the problematic AID’s 11ai epoch, completely precludes AIDs after association | ~ When exchanged before the problematic AID’s 11bi epoch, completely precludes AID collisions after assoc | ~ When exchanged before the problematic AID’s 11bi epoch, completely precludes AID collisions after association
T | N | Add AID change fields to Link Reconfig (see 23/1898) | ? 23/1898 is a different use case (it would be a Link Reconfig “back to self” with many spurious fields). The request does not indicate vetoed AIDs, so could require many iterations; this can be improved by adding an AID List Veto field in the request. |  |  | 
U | N | AID Switch Req frame(AID Req element) + AID Switch Resp frame(AID Resp element) (from 11ah) |  | ? The request does not indicate vetoed AIDs, so could require many iterations. Also these elements contain other spurious fields. |  | 
V | Y | Define a protected request frame to carry a list of AID vetoes for a (typically sparse) list of upcoming epochs; then reuse the being-defined 802.11bi response frame |  | XXXX |  |  Completely precludes AIDs violating the AID Rule after assoc, with efficiency

## Slide 9: Options A+S (and relevant to T/U): AID List Veto element (and field)
AID Veto List field lists the AIDs that the STA does not wish to have assigned as the STA’s AID, and could be:
  N * 2 octets, where each 2 octets contains the AID
  N * 1.5 octets + 0/0.5 octets of Pad bits, where each 1.5 octets contains a 12-bit or 11-bit AID
For TIM compactness, the AP wishes to allocate low AIDs, so the AP might be disinclined to accept requests from a STA that requests to veto too many low AIDs
For option V, there are several signaling options, which can be evaluated as the 11bi protocol component matures.
Element ID | Length | Element ID Extension | AID Veto List field
1 octet | 1 octet | 1 octet | variable

## Slide 10: Options to include per-PPDU signaling for dynamic VS behavior, while minimizing PHY changes: several reasonable choices
Option | Position* in PPDU | Common / Per-User | Analysis (see next slides for more detail)
Reserved USIG bit(s) | Very early | Common |  U-SIG bits need to support multiple future PHY generations; allocating some of these bits for VS purposes was discussed multiple times in TGbe but never accepted.
New VS SIG field (see 24/0461) | Very early | Common |  Greater PHY changes; some test complexity concerns
Redefined bit(s) or redefined values in the User field | Early | Per-User | () Need 11bn draft to allow this for negotiated exceptions (and no change in number of bits)
Pad bits in UHRSIG | Middling | Common & Per-User |  These bits are already uncontrolled; format can be entirely VS once connected STA-IDs are unique
Waveform | Middling-Late |  |  PHY changes; receivers might depend on unexpected features of the waveform.
Service field | Late | (Common &) Per-User | () Need 11bn draft to allow this for negotiated exceptions
PHY Pad bits in the Data field | Very late | (Common &) Per-User |  Too late to be useful
 | *The earlier in the PPDU the better |  | 

## Slide 11: Summary
802.11 has certain PHY resources (U-SIG fields, User fields, UHTSIG pad field, Service field etc)
Each time a vendor uses one of these PHY resources without proper guardrails, practically the PHY resources become unavailable to future amendments
Proper guardrails for PHY VS signaling include:
  All PHY VS behaviors shall be first negotiated with a peer using upper layer signaling (e.g., MAC-level vendor-specific negotiation)
  A STA shall not negotiate, and shall tear down any successful negotiations for, VS behaviors whenever the STA as a recipient cannot distinguish between intended PPDUs with a VS behavior different to other intended PPDUs
    For instance, for UHR (SU)/MU PPDUs, the recipient device of VS behavior with a peer shall ensure that the AID in use with the peer is different from the AID in use with other peers not using that VS behavior
    Via AID allocation (if AP) and/or Options A + S/T/U/V (AID vetoing) (if non-AP STA)
  For UHR TB PPDUs, VS dynamic signaling may occur in the Service field (see backup)
  For UHR (SU)/MU PPDUs, VS dynamic signaling may occur in the User field and UHTSIG field
    No acceptance of VS use of U-SIG bits; yet high temptation – need to provide a safety valve
  All such vendor specific signaling shall operate so that it never precludes standardized use of the same signaling resources.

## Slide 12: References
[1] 23/1099, “Vendor Specific SIG field”, Brian Hart (Cisco Systems)
[2] 24/0461, “Vendor Specific Signaling”, Brian Hart (Cisco Systems)

## Slide 13: Strawpoll 1
Do you agree to add the following text to the 11bn SFD:
  11bn shall define guardrails to enable PHY-level vendor specific extensions that are safe:
    Not ambiguous to an intended recipient
    Use of any other PHY signaling resources shall not introduce interoperability issues if they were to be unreserved / redefined in a future amendment
Y / N / A