## Slide 1: Client Experience Reporting
Jul 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Jerome Henry | Cisco Systems |  | 
Vishal Desai | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 

## Slide 2: Executive Summary
Situation
APs have many control knobs that affect the client experience
APs optimize the setting of those knobs to maximize the client experience
  … Using measures made by or offered to the APs
Problem
These measures may not capture all the dimensions that matter to clients
Clients have no easy, standardized way to express their satisfaction / dissatisfaction with the 802.11 deployment
  …. They don’t have a seat at the table
Solution
Enable clients to be able to report their recent Client Experience to the network

## Slide 3: Situation – AP has many control knobs at different time scales that affect the client experience
Very long
AP positions (dense, sparse, coverage holes)
Major feature support (11n/ ac/ ax/ be/.., 11r, …)
Backhaul throughput / latency to intranet
Backhaul throughput / latency to Internet
Long
Number of SSIDs
Choice and change frequency of Primary channel / Channel width
Choice and change frequency of AP TX power / Local TPC/TPE
Coverage overlap between adjacent APs
EDCA and MU EDCA parameters
Medium feature support and enablement (FILS, TWT, R-TWT, P2P TWT)
BSS Coloring
Short
Network contribution to time to associate
Network contribution to time to roam
BA/TWT/SCS/ … agreements accepted / countered / rejected
Use of BSS-wide mgmt. features like AP Add/Delete, Advertised TTLM as APs juggle tasks
Use of per-STA mgmt. features like BTM to another AP, BTM+TTLM, BTM+Link Add+Delete to steer clients to clearer air
Use of legacy features like Probe Response suppression, Association Rejection, ML Setup with fewer links offered, etc
Very Short
How often to trigger each client (&/or solicit BSR)
How DL traffic is scheduled to clients
How often to sound each client
MCS/NSS/RU selection for DL and for UL
Use of OFDMA / MU-MIMO / SU (and level of padding)

## Slide 4: Situation – AP has many measures for an excellent client experience
Brief onboarding time
Reliable DHCP, DNS, walled garden, application performance
  Ongoing assurance testing, Thousand Eyes
Comprehensive wireless coverage throughout the deployment
Channel utilization not too high
  Few co-channel APs, high throughput for offered load
Low proportion of retries wrt tries
  Low latency, high power efficiency
Especially for QoS TIDs, transmit buffers are shallow almost always
  Low latency
High MCSs / NSSs / data rate with individual clients
High system throughput / efficiency
  High degree of spatial reuse via AP/client power control
SLAs expressed by SCS(QC) met (with margin)
Brief outages during roaming
  Solid coverage overlap between adjacent APs

## Slide 5: Problem – but these measures are incomplete: they don’t include the client’s own perspective of their experience
What matters to the client:
Connectivity (to intranet, Internet)
Coverage, Throughput, Latency & Jitter
  Determined in turn by RSSI, interference level, contending Wi-Fi devices, deferring due to non-Wi-Fi emissions, etc
Power efficiency
Roaming experience
In-device coexistence mitigation
Privacy
Other …
But the AP is not directly aware of many of these parameters:
E.g., AP might aim for a minimum DL RSSI and UL RSSI everywhere, but only has intermittent access to DL RSSIs via 11k Beacon Report. And AP2AP RSSIs are an inferior substitute for these.
Example: stadium antennas (configured to 10deg beamwidth) have much weaker AP2AP RSSIs than AP2client RSSIs

## Slide 6: Solution – Overarching Concept
Enable clients to be able to report their recent Client Experience to the network
Thereby provide the system of APs (+compute) and clients with the information needed to improve the collective client experience
Enable the network’s ongoing trialing of alternatives to discover how to maximize the client experience
  Akin to Minstrel for rate selection, but with a much larger scope (i.e., revisit slide 3)
The trialing can be:
  Manual, or
  Automatic, via closed loop optimization (using AI/ML etc), likely with guardrails

## Slide 7: Solution – Option A: One Client Experience Score, plus areas for improvement
Client can report a Client Experience Score (“Health Score”): e.g., 1 (all but unusable) to 255 (faultless)
  To accommodate the range of clients and how much effort they can allocate to determining a Client Experience Score, exactly how a client populates the value may be implementation dependent
  The overarching requirement is for the client to pick a way to calculate their Client Experience Score such that the client would be happier with a network that it describes by a higher score than by a lower score
Client can also report area(s) for improvement by the network:
  E.g., 802.11 coverage/throughput, 802.11 latency/jitter, scanning and roaming, reliability, power efficiency, in-device coexistence, security/upper layers, backhaul, …
  The union of areas defined should provide complete coverage of the network characteristics; and each area should be specific enough that the network can reasonably identify what kind of actions would mitigate the concern

## Slide 8: Solution – Option B: Multiple Client Experience Scores, one per topic
Example Client Experience Scores | Example circumstances where client reports a worse metric | Example circumstances where client reports a better metric
802.11 Coverage / Throughput | Weak DL RSSI at strongest AP; low MCSs; traffic arrival rate from client’s upper layers is higher than the Wi-Fi transmission rate; the client’s TX buffers are overflowing; many retries; long contention time; MSDU expiry reached (aka packet loss) | Strong DL RSSI at strongest AP; high MCSs; TX buffers are mostly empty; and/or the client is operating at max PHY speed with high channel access duty cycle; no/minimal packet loss
802.11 Latency/Jitter | VO/VI packet loss; high VO/VI buffer depth (and/or MSDUs are dwelling a long time there) and/or VO/VI buffers are overflowing (any buffers, if mis-marked traffic?); codec in upper layers has downshifted to (much) lower than the highest quality; SCS(QC) SLA not met; bad ping time | No/minimal VO/VI packet loss, low VO/VI buffer depth (and/or MSDUs are spending little time dwelling there; VO/VI buffers (almost) never overflow; codec in upper layers is operating at its highest quality
Scanning and Roaming | Roaming often; panic roams required; roaming recommendations (e.g., in Neighbor Report or ?BTM) not good, long dead times; often serving AP’s RSSI is low; (often) not seeing two APs with RSSIs > -67 dBm | Serving AP’s RSSI is high so roaming not a consideration; or roaming occurs with minimal scanning and little downtime especially when QoS flows are active; no panic roams; client always sees two APs at > -67 dBm
Reliability | Periods of no frame transmission or no association;, missing multiple beacons in a row; multiple MSDUs in a row being expired out; received MPDUs being released to upper layers despite SN holes | Continuous connectivity with no extended dropouts
Power efficiency | On battery and low MCS on TX/RX; long periods of idle RX or backoff; many retries | Wall powered or transmit/active receive at high MCS; with few retries
In-Device Coexistence | Taking a long time to change PM bit, data rates drop markedly after each IDC absence, heightened retries, etc | Client leaves and returns with minimal Wi-Fi downtime
Security/upper layers | Auth failure; EAP failure; no IP address; can’t reach gateway; DNS not working; stuck at captive portal; no Internet connectivity to the usual places | Full connectivity
Backhaul | IP/TCP/peer throughput much lower than wireless throughput | IP/TCP/peer throughput similar to wireless throughput

## Slide 9: Solution – Options A+B: Extra Details
To calibrate/compare the information over time as the client mix evolves, it is preferred that:
  The Client Experience Score(s) be subject to quantitative guidelines, and/or
  The sender identifies itself via one or more of: device type/make/model/SW versions/chipset ID [1]
The client feedback could be sent as:
  a response to an AP request or an unsolicited response or
  a conditional response to a conditional AP request (“send an unsolicited response whenever a Client Experience Score is above/below a threshold or changes by an amount above/below a threshold”)
To help compare the client experience before-and-after a network behavioral change, the AP might request the Client Experience Score(s) calculation be reset
For clients that cannot connect, the network may infer a CES of 0

## Slide 10: Summary
Benefit of Client Experience:
Enable clients to be able to report their recent Client Experience (“health”) to the network
  … such that the system of APs (+compute) and clients has the information needed to improve the collective client experience of the system
Ongoing trialing of alternatives can occur, to discover how to maximize the client experience
This provides clients with a seat at the table when decisions are being made on their behalf
The goal of this process is for clients to collectively see a higher Client Experience score
The proposal is very flexible for clients:
  What the client puts in is what the client gets out

## Slide 11: References
[1] 24/0518, “Troubleshooting Metric Follow Up”, Jerome Henry et al, Cisco Systems

## Slide 12: Strawpoll 1
Do you prefer option 1 (1 Client Experience Score + list of areas for improvement) versus option 2 (multiple Client Experience Scores, one per area)
Option 1
Option 2
Abstain

## Slide 13: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn amendment will define an exchange that allows non-AP STAs to rate their Client Experience of the current network
Y / N / A

## Slide 14: Backup