## Slide 1: Client Experience Reporting
Oct 2024
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Jerome Henry | Cisco Systems |  | 
Vishal Desai | Cisco Systems |  | 
Javier Contreras | Cisco Systems |  | 
Binita Gupta | Cisco Systems |  | 
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 

## Slide 2: The infrastructure seeks an excellent client experience, but doesn’t always have adequate visibility
Brief onboarding time
  When did the client’s onboarding effort first start?
Comprehensive wireless coverage throughout the deployment
  But a client that cannot be heard does not register
Channel utilization not too high
  Interference at client ≠ interference at AP
Low proportion of retries wrt tries
  Collided client transmissions are not received; cannot be counted
High MCSs / NSSs / data rate with individual clients
High system throughput / efficiency
Especially for QoS TIDs, transmit buffers are shallow almost always
  AP could use fast BSR polling but cost is too high
SLAs expressed by SCS(QC) met (with margin)
  AP might not receive SST; does not see expired traffic (ditto R-TWT: was the underlying SLA met?)
Brief outages during roaming
  AP does not know when a client’s upper layer UL traffic reached its MAC-SAP

## Slide 3: Even so, the infrastructure applies its best experience and augments it with client-provided metrics where available
APs have many control knobs that affect the client experience
  AP locations, RRM (AP power, channel and channel width), AP scheduler, (MU)EDCA parameters … see backup
APs do have many measures for an excellent client experience
  Throughput, DL latency histogram for QoS traffic, channel utilization at AP, …
  11k client reports such as Beacon Report
But, from the previous slide, these measures are inevitably incomplete: even with all the specific 11k-defined metrics, the AP doesn’t capture the client’s full perspective of its experience
  Impact
  Issue#
1
2
3
3
3
3
  1: Critical  Reason Codes 
  2: Important + known + readily quantifiable  11k 
  3: Impactful but not readily quantifiable or not previously known  this presentation

## Slide 4: Overarching Concept
Client Experience score goes up
Client Experience score goes down
Network performs correlation with environmental & network events; seeks more of them
Network performs correlation with environmental & network events; seeks less
of them
Client puts more effort into Client Experience
Infrastructure puts more weight on Client Experience
The client must calculate their Client Experience Score such that the client would be happier with a network that it describes by a higher score than by a lower score
The infrastructure must incorporate this feedback and make increased client satisfaction an explicit component of its overall goal
… then, what the client puts in strongly affects how much consideration the infrastructure gives it, and so what the client gets out (virtuous circle to spur more effort)
Enable clients to be able to report their recent Client Experience Score (CES) to the network
Consumed manually:
  Client experience score drops broadly after roll-out of new infrastructure SW release  pull the release and root cause
  Client experience score is low (or drops) for a few client SKUs  contact vendor and clarify their concern
  Other issues  e.g., add more APs / move APs / upgrade APs / implement feature X / enable feature Y
Consumed automatically:
  Expectation is for a future with more automated network management (AI/ML; e.g., AI RRM)
  Network correlates scores against events; performs ongoing trialing of alternatives (using its control knobs) to discover how to maximize the CES
     Tweak RRM behavior / tweak scheduler behavior
  AI/ML carries risks: e.g., RL can overfit; always desirable to have CES for a reality-check in the training + validation + test data-sets

## Slide 5: Option A: One Client Experience Score, plus areas for improvement
Client can report a Client Experience Score (“Health Score”): e.g., 1 (all but unusable) to 255 (faultless)
  To accommodate the range of clients and how much effort they can allocate to determining a Client Experience Score, exactly how a client populates the value may be implementation dependent
  But there should be a quantified “Effort” score: e.g., 1 (no effort) to 5 (max effort)
  The overarching requirement is for the client to pick a way to calculate their Client Experience Score such that the client would be happier with a network that it describes by a higher score than by a lower score
Client can also report area(s) for improvement by the network:
  E.g., 802.11 coverage/throughput, 802.11 latency/jitter, scanning and roaming, reliability, power efficiency, in-device coexistence, security/upper layers, backhaul, …
  The union of areas defined should provide complete coverage of the network characteristics; and each area should be specific enough that the network can reasonably identify / correlate what kind of actions would mitigate the concern

## Slide 6: Option B: Multiple Client Experience Scores, one per topic (+Effort)
Example Client Experience Scores | Example circumstances where client reports a worse metric | Example circumstances where client reports a better metric
802.11 Coverage / Throughput | Weak DL RSSI at strongest AP; low MCSs; traffic arrival rate from client’s upper layers is higher than the Wi-Fi transmission rate; the client’s TX buffers are overflowing; many retries; long contention time; MSDU expiry reached (aka packet loss) | Strong DL RSSI at strongest AP; high MCSs; TX buffers are mostly empty; and/or the client is operating at max PHY speed with high channel access duty cycle; no/minimal packet loss
802.11 Latency/Jitter | VO/VI packet loss; high VO/VI buffer depth (and/or MSDUs are dwelling a long time there) and/or VO/VI buffers are overflowing (any buffers, if mis-marked traffic?); codec in upper layers has downshifted to (much) lower than the highest quality; SCS(QC) SLA not met; bad ping time | No/minimal VO/VI packet loss, low VO/VI buffer depth (and/or MSDUs are spending little time dwelling there; VO/VI buffers (almost) never overflow; codec in upper layers is operating at its highest quality
Scanning and Roaming | Roaming often; panic roams required; roaming recommendations (e.g., in Neighbor Report or ?BTM) not good, long dead times; often serving AP’s RSSI is low; (often) not seeing two APs with RSSIs > -67 dBm | Serving AP’s RSSI is high so roaming not a consideration; or roaming occurs with minimal scanning and little downtime especially when QoS flows are active; no panic roams; client always sees two APs at > -67 dBm
Reliability | Periods of no frame transmission or no association;, missing multiple beacons in a row; multiple MSDUs in a row being expired out; received MPDUs being released to upper layers despite SN holes | Continuous connectivity with no extended dropouts
Power efficiency | On battery and low MCS on TX/RX; long periods of idle RX or backoff; many retries | Wall powered or transmit/active receive at high MCS; with few retries
In-Device Coexistence | Taking a long time to change PM bit, data rates drop markedly after each IDC absence, heightened retries, etc | Client leaves and returns with minimal Wi-Fi downtime
Security/upper layers | Auth failure; EAP failure; no IP address; can’t reach gateway; DNS not working; stuck at captive portal; no Internet connectivity to the usual places | Full connectivity
Backhaul | IP/TCP/peer throughput much lower than wireless throughput | IP/TCP/peer throughput similar to wireless throughput

## Slide 7: Protocol Details
To calibrate/compare the information over time as the client mix evolves, it is preferred that:
  The Client Experience Score(s) (CES(s)) be subject to quantitative guidelines (FFS), and/or
  The sender identifies itself via one or more of: device type/make/model/SW versions/chipset ID [via 11v]
Protocol expectations:
  AP sends Measurement Request indicating:
    Reset any pre-existing CES-related state and begin calculating CES(s), to be reported:
      At a defined single-shot or periodic schedule (e.g., once per xx minutes) and/or
      At a defined trigger condition (e.g., CES(s) have markedly increased or decreased)
    Or a request for the latest (cumulating) CES(s)
    Or a request to stop calculating CES(s) (e.g., a request with no periodic reporting or trigger conditions)
  Upon request (2) or periodically (1.1) or after the triggering condition (1.2), the client sends a Measurement Report containing the Client Experience score(s)
Item 1 helps the Client Experience Score(s) to be compared before-and-after a network behavioral change
Measurement Request of type Client Experience(mode=reset+start, periodicParams, conditonalParams)
Measurement Report of type Client Experience
… period elapses
Client Experience drops by 10%
Measurement Request of type Client Experience(mode=updateRequest)
Measurement Report of type Client Experience
Measurement Report of type Client Experience
Measurement Request of type Client Experience(mode=stop)
Measurement Report(Accept)

## Slide 8: Summary
Benefit of Client Experience:
Enable clients to be able to report their recent Client Experience (“health”) to the network
  … such that the system of APs (+compute) and clients has the information needed to improve the collective client experience of the system
Ongoing trialing of alternatives can occur, to discover how to maximize the client experience
This provides clients with a seat at the table when decisions are being made on their behalf
The goal of this process is for clients to collectively see a higher Client Experience score
The proposal is very flexible for clients:
  What the client puts in is what the client gets out

## Slide 9: References
[1] 24/0518, “Troubleshooting Metric Follow Up”, Jerome Henry et al, Cisco Systems

## Slide 10: Strawpoll 1
If Client Experience Score were to be added to the SFD, do you most prefer:
Option A (1 Client Experience Score + list of areas for improvement)
Option B (Multiple Client Experience Scores, one per area)
Abstain

## Slide 11: Strawpoll 2
Do you agree to add the following text to the 11bn SFD:
  The 802.11bn amendment will define an exchange that allows non-AP STAs to rate their Client Experience of the current network
Y / N / A

## Slide 12: Backup

## Slide 13: AP has many control knobs, at different time scales, that affect the client experience
Very long
AP positions (dense, sparse, coverage holes)
Major feature support (11n/ ac/ ax/ be/.., 11r, …)
Backhaul throughput / latency to intranet
Backhaul throughput / latency to Internet
Long
Number of SSIDs
Choice and change frequency of Primary channel / Channel width
Choice and change frequency of AP TX power / Local TPC/TPE
Coverage overlap between adjacent APs
EDCA and MU EDCA parameters
Medium feature support and enablement (FILS, TWT, R-TWT, P2P TWT)
BSS Coloring
Short
Network contribution to time to associate
Network contribution to time to roam
BA/TWT/SCS/ … agreements accepted / countered / rejected
Use of BSS-wide mgmt. features like AP Add/Delete, Advertised TTLM as APs juggle tasks
Use of per-STA mgmt. features like BTM to another AP, BTM+TTLM, BTM+Link Add+Delete to steer clients to clearer air
Use of legacy features like Probe Response suppression, Association Rejection, ML Setup with fewer links offered, etc
Very Short
How often to trigger each client (&/or solicit BSR)
How DL traffic is scheduled to clients
How often to sound each client
MCS/NSS/RU selection for DL and for UL
Use of OFDMA / MU-MIMO / SU (and level of padding)