## Slide 1: Distribution Bandwidth of DRU - Follow up
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | email
Mengshi Hu | Huawei |  |  | humengshi@huawei.com
Ross Jian Yu |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Background
11bn supports a distributed tone RU (DRU) for a TB PPDU transmission, where the DRU means an RU consisting of subcarriers spreading across a certain bandwidth [1]. According to the DRU discussions, to determine an allocated DRU, the following information is needed:
  The corresponding Regular RU (RRU) of the DRU.
  The distribution bandwidth (DBW) of the DRU.
  In this contribution, we further discuss the following topics related to DBW:
  Suggested types of DBW
  Signaling of DBW
After knowing the DBW, the indicated RRU is mapped to a specific DRU.
Figure 1 DRU Indication

## Slide 3: Types of DBW
As discussed in [2], the power gain of a DRU compared to the RRU case is shown below:
  According to the above analysis, all of the above DBWs (20, 40, 80, and 160 MHz) should be supported to adapt to different scenarios:
  The smaller size DBWs can provide enough power gains for smaller size DRUs.
  The larger size DBWs can further enhance the power gain performance of the larger size DRUs, such as 242-, 484-, and 996-tone DRUs.
  To achieve UHR goals, it is important to enhance the performance of large size DRUs.
NRU | DRU |  |  | 
 | DBW = 20 MHz | DBW = 40 MHz | DBW = 80 MHz | DBW = 160 MHz
26 | 8.06 | 11.07 | 11.07 | 11.07
52 | 6.3 | 8.06 | 11.07 | 11.07
106 | 3.29 | 6.3 | 8.06 | 11.07
242 | N/A | 2.62 | 5.05 | 8.06
484 | N/A | N/A | 2.62 | 5.05
996 | N/A | N/A | N/A | 2.62
Table 1 Power Gain Compared to RRU Case (dB)

## Slide 4: Indication of DBW
After knowing the corresponding RRU and DBW of a DRU, the accurate position of a DRU can be determined.
  The corresponding RRU could be indicated by the conventional method.
  To indicate the DBW to further determine the DRU, two directions are discussed here:
  Per-User Indication
  Common Indication
In the subsequent slides, we further discuss the above two directions.

## Slide 5: Per-User Indication of DBW
  To indicate the DBW of a DRU, one direct and natural thought is to convey the DBW related information in the User Info field of each user.
  The following green block is an example:
Figure 2 Per User Indication of DBW

## Slide 6: Example of Per-User Indication
Regarding the details of the DBW related information, an example is further shown below:
  Each User Info field may use 3 additional bits to indicate the DBW related information.
Note that according to the existing User Info field design, it may be hard to get so many additional bits for the DBW related indication.
  UEQM and CSD may also need some bits.
  Reserved bits may be needed for some other usages.
Value | Meaning
000 | RRU
001 | DRU (20 MHz DBW)
010 | DRU (40 MHz DBW)
011 | DRU (80 MHz DBW)
100 | DRU (160 MHz DBW)
101 - 111 | Reserved
Table 2 DBW Related Information

## Slide 7: Common Indication of DBW
Different from the per-user indication, the common indication can also be used to notify the DBW, saving the overhead in User Info fields:
  According to the DBW discussions, a 20 MHz sub-channel may only correspond to one type of DBW. Thus, although the per-user indication provides more flexibility for indication, there is no need to use different indications for the DRUs in the same frequency range.
  What is really needed for signaling is to show the DBW of each 20 MHz sub-channel.
Figure 3 Common Indication of DBW
Containing sixteen 20 MHz sub-channels (320 MHz)
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?
DBW?

## Slide 8: Example of Common Indication
An example of common indication is shown below:
  Since the DBW pattern in each 80 MHz is limited to only several types, a table with 80 MHz granularity could be used to indicate the DBW of RUs related to that 80 MHz.
Figure 4 An example of common Indication
Containing sixteen 20 MHz sub-channels (320 MHz)
Value | Meaning
x | RRU
y | DRU (80 MHz DBW)
z | DRU (160 MHz DBW)
… | …
Table for each 80 MHz
The same table
The same table
The same table
More entries can be used to indicate different DBW patterns, such as 20+20+40, 40+20+20, etc.

## Slide 9: Summary
In this contribution, we further share some thoughts on the DRU DBW:
  DBWs (20, 40, 80, and 160 MHz) should be supported to adapt to different scenarios.
  Suggest using the common indication for DBW signaling.

## Slide 10
[1] Alfred Asterjadhi, TGbn Motions List - Part 1, 802.11 DCN 2024/171r6
[2] Mengshi Hu, et al. Discussion on Distribution Bandwidth of DRU, 802.11 DCN 2024/801r1
References

## Slide 11: Straw Poll #1
Do you agree to include the following into the 11bn SFD?
  11bn defines distribution bandwidth of 20 MHz, 40 MHz, 80 MHz and 160 MHz.
    The distribution bandwidth is the bandwidth that a DRU spans over.
    The distribution bandwidth is smaller or equal to the PPDU bandwidth.
    Y
    N
    A

## Slide 12: Straw Poll #2
Do you agree to include the following into the 11bn SFD?
  The distribution bandwidth information is notified in the Common Info field of a trigger frame.
    Y
    N
    A