## Slide 1: New MCSs for 11bn-Follow Up
Date: 2024-09-11
Authors:
Name | Affiliations | Address | Phone | Email
Shengquan Hu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | shengquan.hu@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | 

## Slide 2: Introduction
We have proposed adding new MCSs for 11bn in [1]:
  The four new MCSs are based on the combinations of existing modulation and coding rate:
    {QPSK, 16QAM, 256QAM} with coding rate R=2/3
    16QAM with coding rate R=5/6
Same as in [1], other studies in contributions [2~5] also verified and confirmed the benefit of adding new MCSs for 11bn :
    Close the large sensitivity SNR gap between the adjacent existing MCSs
    Improve the throughput gains up to 30%
    Better reliability and more accurate link adaptation
    Increase the throughput of UEQM
    Low complexity
The new MCSs was proposed in March, we think it is time to make progress on this topic

## Slide 3: Reference
Shengquan Hu, Mediatek Inc.
Slide 3
[1] 11-24-0469-00-00bn-New MCSs for 11bn
[2] 11-24-0474-00-00bn-UHR unequal modulation pattern and new MCS
[3] 11-24-0498-00-00bn-Unequal Modulation in MIMO TxBF and New MCS for 11bn
[4] 11-24-0507-01 UEQM Further Details
[5] 11-24-0753-01-00bn-new-mcs-simulation-results

## Slide 4: Straw Poll #1
Shengquan Hu, Mediatek Inc.
Slide 4
Do you agree to include the following text to the 11bn SFD?
Introduce new MCSs which are applicable to single spatial stream transmissions, as well as to equal modulation and unequal modulation cases in multiple spatial stream transmissions

## Slide 5: Straw Poll #2
Shengquan Hu, Mediatek Inc.
Slide 5
Do you agree to include the following text to the 11bn SFD?
Add the following modulation and code rate combinations as the new MCSs for 11bn:
    Modulations of {QPSK, 16QAM, 256QAM} with code rate R=2/3
    Modulation of 16QAM with code rate R=5/6

## Slide 6: Straw Poll #3
Shengquan Hu, Mediatek Inc.
Slide 6
Do you agree to include the following text to the 11bn SFD?
Use total 5 bits to indicate UHR MCSs in User field in UHR-SIG and in User Info field in UHR Trigger Frame
    Details of 5 bits position for UHR MCSs indication TBD