## Slide 1: EDCA+ for High Priority Access
Date: 2024-09-06
Authors:

## Slide 2: Background
EDCA based techniques to reduce tail access delay of Low Latency (LL) traffic in multi-BSS dense scenarios has been discussed [1-3]
The techniques support the LL traffic by giving higher priority than legacy STAs which are using EDCA
Among them, (Hi)gh (P)riority EDCA is proposed in [1]
  Separate STA(s) with traffic streams that require bounded latency/stringent ETE bounds from the rest of the contention crowd
  Allow LL STA(s) to send special signal or MAC frame to announce (Hi)gh (P)riority EDCA contention PRIOR to regular contention start
This document proposes a method to
  Provide a scalable method using HiP EDCA parametrized by AP
  Further reduce delays due to EDCA collisions.

## Slide 3: HiP EDCA Illustration [1]
EDCA contention period
Previous TXOP
TxOP gained by STA3
STA4
STA3
STA2
Legacy
STA1
Legacy
Last frame of TXOP
SIFS
DIFS
DS
or
frame
AIFSN
AIFSN
Idle
Busy
EIFS mode/NAV
Idle
Busy
Idle
Idle
BO: rand(0,7)=4
BO: rand(0,7)=5
PPDU transmission
Idle
Idle
Busy
Busy
Busy
Busy
Busy
Busy
EIFS mode/NAV
DS
or
frame
PIFS

## Slide 4: Motivation
Some observations are provided in [1]
  If AP send DS for DL LL streams, it has additional gain
  If DS transmissions are randomized, it would help to increase gain
Some aspects requires additional enhancements
  Fully distributed way is vulnerable to DS congestion in dense environment
  . For reducing congestion, additional conditions (e.g., # of retransmissions, etc.) might be required
  . Adding randomness to DS transmission is limited because the time resource is not enough
  . It is not easy to add/control the conditions in a distributed feature
  . It is hard to block the operations of STAs if there are unexpected problems
  In addition to AC_VO, AC_VI may need to be support with higher priority than best effort traffic.
  . We may not have AC_VO in the network while AC_VI is delayed
  . In the future, we may have a traffic which is higher priority than AC_VO
  AP may further prioritize the urgent traffic

## Slide 5: EDCA+
AP can provide some parameters to decide whether STA sends DS or not
  Traffic Type (Access Class, TID, etc.)
    For example, AP selects the lowest access class (LAC) allowed for prioritized access
    If AC_VI is selected as LAC, AC_VO and AC_VI are allowed to be transmitted
STA3
(AC_VO)
STA2
(AC_VI)
STA1
(Legacy)
AP
…
Beacon w/
LAC = AC_VO
STA3
(AC_VO)
STA2
(AC_VI)
STA1
(Legacy)
AP
…
Beacon w/
LAC = AC_VI
EDCA
EDCA
EDCA+
EDCA
EDCA+
EDCA+

## Slide 6: EDCA+
AP can provide some parameters to decide whether STA sends DS or not (Cont.)
  Priority Value (PV)
    AP selects a proper value within [PVmin, PVmax] for access control
  Range of PV : [PVmin, PVmax]
    Could be fixed in advance.
STA decide DS transmission by using the received parameters from AP
  STA selects a Access PV(APV) within [PVmin, PVmax]
  If APV < PV and traffic type is higher than LAC, STA is eligible to send DS
STA3
(AC_VO)
STA2
(AC_VI)
AP
…
APV = 2 < PV = 3
Beacon w/
PV = 3, Range = [0, 10]
LAC = AC_VO
EDCA
STA3
(AC_VO)
STA2
(AC_VI)
AP
…
APV = 10 > PV = 3
Beacon w/
PV = 3, Range = [0, 10]
LAC = AC_VO
EDCA
EDCA
EDCA+

## Slide 7: Example 1 of EDCA+
Allow the access of STA (AC_VO, PV = 3)
EDCA contention period
Previous TXOP
STA4
(AC_VO)
STA3
(AC_VO)
STA2
(AC_VI)
STA1
(Legacy)
SIFS
DIFS
Idle
Idle
PIFS
Idle
AP
…
APV = 2 < PV = 3
APV = 4 > PV = 3
AIFSN
Idle
Busy
Busy
Busy
Backoff (BO)
rand(0,7) = 3
Beacon w/
PV = 3, Range = [0, 10]
LAC = AC_VO
AIFSN
EIFS /NAV
EIFS /NAV
EIFS /NAV
Busy
Busy
Busy
Idle
Busy
N/A
Last frame of TXOP
PPDU transmission
DS or
A Frame
ACK
Busy
Busy
Busy
AIFSN
EIFS /NAV
Busy

## Slide 8: Example 2 of EDCA+
Allow the access of STA (AC_VO, PV = 3), but STA 3 is prioritized by AP
EDCA contention period
Previous TXOP
STA4
(AC_VO)
STA3
(AC_VO)
STA2
(AC_VI)
STA1
(Legacy)
SIFS
DIFS
Idle
Idle
PIFS
Idle
AP
…
APV = 2 < PV = 3
APV = 4 > PV = 3
Idle
Busy
Busy
Busy
Busy
Busy
Busy
Beacon w/
PV = 3, Range = [0, 10]
LAC = AC_VO
EIFS /NAV
EIFS /NAV
EIFS /NAV
Busy
Busy
Busy
Idle
Busy
N/A
Last frame of TXOP
DS or
A Frame
Busy
PPDU transmission
ACK
AIFSN
AIFSN
AIFSN

## Slide 9: Example 3 of EDCA+
Allow the access of AP only (not for STA)
Plus, PV=0 block the operation of HiP EDCA if there is unexpected problem
EDCA contention period
Previous TXOP
STA4
(AC_VO)
STA3
(AC_VO)
STA2
(AC_VI)
STA1
(Legacy)
SIFS
DIFS
Idle
Idle
PIFS
Idle
AP
…
N/A
N/A
Idle
Busy
Busy
Busy
Busy
Busy
Busy
Beacon w/
PV = 0
EIFS /NAV
EIFS /NAV
EIFS /NAV
Busy
Busy
Busy
Idle
N/A
DS or
A Frame
Last frame of TXOP
PPDU transmission
AIFSN
AIFSN
AIFSN
AIFSN
EIFS /NAV
Busy
ACK

## Slide 10: Additional Considerations on EDCA+
AP may provide additional parameters
  Number of Retransmission
    If AP wants to provide additional priority according to the number of retransmissions, it can be provided
    If the value is 1, STA shall be failed at least once before participating in EDCA+
  Contention window size for EDCA +
    Could be smaller than EIFS (e.g., AC_VI uses this value instead of EDCA value)
AP may send TF for UORA, MU-RTS, etc.
  Compared to general TXOP operation, AP transmission can be prioritized because MAC frame (e.g., TF instead of DS) can be transmitted right after PIFS/DIFS

## Slide 11: Summary
EDCA+ is proposed to further reduce delay
  Provide additional access control method
  . To reduce the EDCA collisions in dense environment by using PV based decision
  . To control the congestions by using the EDCA+ parameters in addition to PV
  Enhance the scalability by using AP control
  . To extend the target traffic, e.g, AC_VI in addition to AC_VO
  . To open for future enhancement of AP control by introducing new EDCA+ parameters

## Slide 12: Reference
[1] 11-24-840-00-00bn-hip-edca-proposal
[2] 11-23/1886, Preemption-techniques-to-meet-low-latency-ll-targets
[3] 11-24/0416, Target STA Prioritization in EDCA-based Preemption Mechanisms during a DL TXOP

## Slide 13: Straw poll 1
Do you agree to improve EDCA to reduce tail access delay of low latency traffic?
Note : The solution can operate under the guidance/supervision of the AP to limit impact to legacy use cases.