## Slide 1
Indication Techniques for Urgent Traffic
Date: 2024-07-11
Name | Affiliations | Address | Phone | email
Jinho Choi | Samsung Electronics | 56, Seongchon-gil, Seocho-gu, Seoul, Republic of Korea |  | dominic.choi@samsung.com
Jack Jonghyo Lee |  |  |  | 
Jaheon Gu |  |  |  | 
Jonghoe Koo |  |  |  | 
Jungjun Kim |  |  |  | 
Mingyu Lee |  |  |  | 
Seongho Byeon |  |  |  | 
Suhwook Kim |  |  |  | 
Taeyoung Ha |  |  |  | 
Youngwan So |  |  |  | 

## Slide 2: Introduction
In order to improve tail of the latency distribution and jitter, which is one of the objectives of 802.11bn [1], it has been actively discussed how to support aperiodic low latency (LL) traffic, mainly including preemption [2-5]
In order to support timely transmission of LL traffic with stringent latency requirement, it is important to efficiently identify its presence because it needs to be frequently checked
In this submission, we discuss how to effectively identify urgent traffic in consideration of the relative importance of traffic

## Slide 3: Overview of UL LL Traffic Support
TXOP holder checks the existence of LL traffic and may also collect additional information such as buffer status
  The soliciting frame may be delivered explicitly (e.g., BSRP or NFRP) or implicitly (e.g., included in a data frame)
LL STAs notify the presence of LL traffic and may provide solicited additional information
LL traffic is transmitted using the resources allocated according to the exchanged information as described above

## Slide 4: A Scenario to Consider
Since all STAs can access RA-RUs as per current spec., multiple LL STAs (even non-LL STAs) may select the same RA-RU to send their BSRs
Due to the collision, transmission of more urgent traffic may fail due to the transmission attempt of traffic that can afford delay
Similar problem always exist in any cases where randomness exists

## Slide 5: Thoughts on Traffic/STA Identification
An efficient use of resources to identify urgent traffic is essential
  Since TX holder doesn’t know who has LL traffic, the use of RA-RU(s) can be helpful to efficiently discover the presence
  Due to the nature of LL traffic, its presence needs to be identified by a concise procedure repeated at short intervals
An effective method of giving priority to appropriate traffic (e.g., highly likely to violate its QoS requirements) is also required
  It is desirable that the priority of traffic is determined according to the situation at the time of transmission
  At a given opportunity, for example, more urgent traffic should be sent in a timely manner to meet their requirements so as not to degrade user experience
Therefore, identifying eligible STA(s) in an efficient and effective way is an important design criterion
  An eligible STA in this context is regarded as a STA having traffic satisfying a specified condition(s) (e.g., remaining delay budget, traffic category)

## Slide 6: Proposal
Enabling TXOP holder (or AP) to specify condition(s) for resources used for sending traffic information
  To effectively consider the priority of traffic while filtering out ineligible traffic
  Ex) Condition 1 (C1): remaining delay is less than 3ms, Condition 2 (C2): remaining delay is not less than 3ms but less than 10ms
STA(s) shall transmit the response according to the conditions
  Any STA with traffic that satisfies the condition can send a response

## Slide 7: Setting and Utilizing Conditions
The conditions may be set based on various criteria as needed
  Ex) residual delay, buffered data size, AC, TID, AID, etc., and their combination
TXOP holder can differentiate the competition rate (priority) by allocating different amounts of resources for each condition
  Ex) X RA-RUs for condition 1 & Y RA-RUs for condition 2, where X ≠ Y
TXOP holder can adjust the conditions and resources depending on the BSS environment (number of STAs, number of streams, etc.)
  TXOP holder may manage the conditions dynamically by including them in some frames, or may manage them (semi-)statically by announcing via beacon or the like
  Although the possibility of collision is not completely eliminated, it seems to be a more scalable approach
    TXOP holder doesn’t need to manage additional context for LL STA or LL stream

## Slide 8: Application of the Proposal
The proposed scheme is applicable to various procedures to support LL traffic, including preemption mechanisms that have been discussed
  If the probability of collision can be reduced enough by further specifying the conditions, it can also be considered to skip the STA identification step and transmit LL traffic immediately by using Basic TF with UORA
  In the EDCA-based preemption mechanism [2], the conditions can be used to apply different contention parameters or to control the traffic to participate in the contention
  When the Zadoff-Chu sequence is used as a PR signal [6], it can be used to adjust competition rate by allowing STAs to select an index in different ranges depending on the conditions

## Slide 9: Conclusion
In order to support LL traffic well, it is important to identify LL STA(s) efficiently and effectively
In this contribution, we discussed how to indicate the eligibility to use resources to inform the presence of urgent traffic, which consequently differentiates transmission opportunities according to the relative importance of traffic
The proposed scheme is applicable to various procedures to support LL traffic

## Slide 10: References
[1] 23/0480r3, UHR proposed PAR
[2] 23/1886r3, Preemption techniques to meet low-latency (LL) targets
[3] 24/0131r0, Signaling of preemption
[4] 24/0168r0, TXOP preemption in 11bn
[5] 24/0390r0, A uniform procedure for preemption
[6] 24/0431r2, Signal for preemption request

## Slide 11: SP #1
Do you agree to define a mechanism in 11bn for a TXOP holder to allow a STA to indicate the presence of traffic for low latency traffic delivery within its TXOP?
Note: TXOP holder can be an AP or a non-AP STA
Note: Policy for TXOP holder allowing indication is TBD

## Slide 12: SP #2
Do you agree to define a mechanism for an AP to restrict STA(s) to conditionally[Note] indicate the presence of traffic for urgent traffic delivery?
Note: Conditions are TBD (e.g., remaining delay, TID, etc.)