## Slide 1: UL Data Rate for AMP
Date: 2024-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 2: Abstract
In this contribution, we analyse the signalling overhead of both legacy and AMP devices and discuss the reasonable UL data rate for AMP devices.
Doc.: IEEE 802.11-24/1198r0

## Slide 3
Background
  Legacy WiFi devices
    Multiple rates are supported depending on modulation and coding, e.g., MSC
      802.11a 6 Mbps to 54 Mbps
      802.11n 6.5 Mbps to 600 Mbps
  Two DL data rates are supported in 802.11ba
    LDR - 62.5 kbps, mandatory with similar coverage as MR of legacy WiFi devices
    HDR – 250 kbps data rate with shrinking coverage
  For AMP devices, we consider two deployment scenarios
    Hybrid deployment: AMP devices are deployed with legacy WiFi devices
      Minimal impacts on the legacy devices
    Standalone deployment: AMP devices only
      Efficiency is still needed.
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 4
Preamble of 802.11n
The preamble in 802.11n (Wi-Fi 4) can vary in length depending on whether the frame is using a legacy (non-802.11n) format or a high-throughput (HT) format.
Preamble Components
  Legacy Preamble: Compatible with 802.11a/g devices, this ensures backward compatibility.
    Legacy Preamble is composed of:
      Short Training Field (STF): 8 µs
      Long Training Field (LTF): 8 µs
      Signal Field (SIG): 4 µs
      Total length: 20 µs
  HT Preamble: Specific to 802.11n, providing additional information for high-throughput operations.
    When operating in HT mode, the preamble includes both the legacy components and additional HT-specific components:
      HT Short Training Field (HT-STF): 4 µs
      HT Long Training Field (HT-LTF):The length of HT-LTF can vary depending on the number of spatial streams. Each spatial stream adds 4 µs.
  Total length: 36 µs for a single spatial stream configuration.
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 5
MAC Header of 802.11n
Basic MAC Header Structure
  Frame Control: 2 bytes
  Duration/ID: 2 bytes
  Address 1 (Receiver Address): 6 bytes
  Address 2 (Transmitter Address): 6 bytes
  Address 3 (Destination Address): 6 bytes
  Sequence Control: 2 bytes
  Total for basic MAC header: 24 bytes
Additional Fields in 802.11n
  QoS Control Field: 2 bytes (used in QoS Data frames)
  HT Control Field: 4 bytes (used in HT Data frames)
Up to 30 bytes
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 6
Signalling Overhead of 802.11n
Transmission rate of MAC header
  Channel Width:20 MHz
  MCS Index 0
    BPSK (Binary Phase Shift Keying) modulation
    1/2 coding rate
    Single spatial stream
    Transmission Rates: 6.5 Mbps
    30 bytes takes around 37 µs
Total duration of overall signalling overhead (PHY preamble + MAC header)
  36+37=73 µs
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 7
Frame Duration of 802.11n
Typical payload size
  VoIP: VoIP packets might have payload sizes around 100 bytes (small packet size due to the nature of audio data).
  Web Browsing: Typical web browsing might see payload sizes between 500 and 1500 bytes.
  File Transfers: Larger payloads are common, especially if aggregation is used, often reaching several thousand bytes.
  Standard Definition (480p) video streaming: Typical payload size is around 1000-2000 bytes per frame.
Range in 100 to several thousand bytes
Total duration of one frame
  100 bytes: up to 73+123 = 196 µs
  2000 bytes: up to 73+2461 = 2.53 ms
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 8
Preamble of AMP
Preamble Components
  Legacy Preamble [1]: Compatible with 802.11a/g devices, this ensures backward compatibility.
    Legacy Preamble is composed of:
      Short Training Field (STF): 8 µs
      Long Training Field (LTF): 8 µs
      Signal Field (SIG): 4 µs
      Total length: 20 µs
  2 BPSK mark symbols: 8 µs
  AMP sync: 64 µs (HDR)
  Total length: 92 µs
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 9
MAC Header of AMP
Basic MAC Header Structure
  Frame Control: 2 bytes
  Duration/ID: 1 bytes
  Address 1 (Receiver Address): 2 bytes
  Address 2 (Transmitter Address): 2 bytes
  Address 3 (Destination Address): 6 bytes
  Sequence Control: 1 bytes
  Total for basic MAC header: 8 bytes
Up to 8 bytes
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 10
Reasonable UL Data Rate of AMP
Transmission rate
  250kbps
Typical payload size
  256bits
Total duration per device
  92+1280 = 1.37 ms
FDM channel
  Total duration per device: 1.37/FDM
Higher data rate is needed for UL to reduce the length of the PPDU, i.e., channel occupation time, with less impacts on legacy devices.
  At least 250kbps, 62.5kbps may not be applicable
  Higher rate, e.g., 1 Mbps, can be considered.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 11
Link Budget
84.5 dB link budget can be achieved for 62.5 kbps
Link budget for enhanced date rates can be estimated as follows,
  250 kbps, 78.5 dB
  500 kbps, 75.5 dB
  1 Mbps, 72.5 dB
1 Mbps can be supported with reasonable link budget.
Yinan Qi (OPPO)
Slide 11
Doc.: IEEE 802.11-24/1198r0
July 2024
Parameter | Value
TX Power | -15 dBm
Thermal Noise Floor | -101 dBm
Noise Figure | 9 dB
Noise Power Level | -92 dBm
Required SNR (LDR) | -7.5 dB
Receiver Sensitivity | -99.5
Link Budget | 84.5 dB

## Slide 12
Summary
  In this submission, we discuss the UL data rate for AMP:
    Efficient UL transmission is needed for both hybrid and standalone deployments;
    AMP frame should not be too long thus very low data rate may not be desirable in certain scenarios;
    Up to 1 Mbps UL rate can be supported with reasonable link budget.
Yinan Qi (OPPO)
Slide 12
Doc.: IEEE 802.11-24/1198r0
July 2024

## Slide 13: Reference
[1] Steve Shellhammer, et. al., “Ultra-Low Power Wake-up Radio Standard,” Wiley, 2023
Doc.: IEEE 802.11-24/1198r0
July 2024