## Slide 1: PHY Design for AMP
Date: 2024-07-15
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | 
Chuanfeng He |  |  |  | 
Ke Wang |  |  |  | 
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 2: Abstract
In this contribution, we discuss the PHY design for AMP covering the following aspects
  PPDU design
  Asymmetric UL/DL design
  Coding
Doc.: IEEE 802.11-24/1199r1

## Slide 3
Background
  Different generations of 802.11 PPDU structures are shown in below.
  Two OFDM symbols BPSK-Mark1 and BPSK-Mark2 are inserted after L-SIG for misclassification issues [1].
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 4
PPDU Design for AMP – Legacy Preamble
  Main design aspects
    Preamble with wider BW
    AMP part with narrow BW
  The AMP PPDU should also starts with legacy preamble including L-STF, L-LTF and L-SIG.
  The MCS should be signalled in L-SIG and for AMP PPDU, MCS should be set as MCS0 so that if MCS is not configured as MCS0, the STA knows the received PPDU is non-HT legacy PPDU.
  Q: Whether or not there is a need to differentiate AMP PPDU from other PPDU structures including HT, VHT, HE and WUR?
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 5
PPDU Design for AMP – AMP Preamble
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-24/1199r1
July 2024
WUR-sync =
WUR Data
802.11ba HDR-Sync
WUR-sync = [W, W]
WUR Data
802.11ba LDR-Sync
AMP-sync = [W, ] or [, W]
AMP Data
AMP : Different sync format with the same length
AMP-sync = G
AMP Data
AMP: Different sync sequence with the same/different length
  AMP Sync design
    New sync sequence: same/different length, correlation property, balance of 1 and 0, etc.
    Legacy sync sequence: no commercial deployment of WUR devices yet, thus no need to differentiation, potential new combination

## Slide 6
PPDU Design for AMP – AMP SIG
  A SIG part can be inserted between AMP-Sync and AMP Data to explicitly indicate AMP payload configuration [2].
  The following parameters can be included in SIG,
    Rate: explicit indication of data rate
      E.g., 62.5kbps, 250kbps, 500kbps, 1Mbps, 2 bits
    UL/DL indication (1 bit):
      Asymmetric UL/DL format
      Non-AP AMP STAs don’t detect UL PPDU
    Length
      96-256 bits, up to 64 bytes, 6 bits
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 7
PPDU Design for AMP – AMP SIG (Cont.)
  The following parameters can be included in SIG,
    Backscatter indication (1 bit)
      Indicate if the UL transmission is active transmission or backscattering
      If backscattering, the AMP payload part can be CW only
    Parity check (1 bit)
      Error detection
    Coding (1 bit)
      Indicate if FEC coding is applied
    Reserved (2 bit)
      For future enhancements
  Total number of bits and overall duration
    14 bits
    Length: 224 µs @62.5 kbps, 14 µs @1 Mbps
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 8
Asymmetric UL/DL Design
Different supported rates for UL and DL
  Low rate can be supported for DL since one DL frame can address multiple AMP devices and thus is transmitted less frequently
  High rate is preferred for UL to enhance the transmission efficiency, especially when many AMP devices are deployed
Different PPDU formats
  Legacy preamble can be used in DL but may be too complicated for UL
  DL is only active transmission but for UL both active Tx and backscattering should be considered, which may not have the same PPDU format as DL
Different waveform/modulation
  OOK can be baseline for DL
  UL: OOK, FSK, etc., but may converge to one
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 9
Coding for AMP
Line Coding for DL, e.g. Manchester code
  AMP can easily decode
  No significant complexity, thus power consumption is negligible
Line coding for UL
  Consider FEC code for UL
  Convolutional code
    Low coding complexity
    Coding gain with enhanced UL link budget
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 10
Summary
  In this submission, we discuss the PHY design aspects for AMP including:
    Overall PPDU format including legacy preamble part and AMP part;
    AMP part design including sync, SIG and payload;
    Asymmetric UL/DL design
    FEC Coding
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-24/1199r1
July 2024

## Slide 11: Reference
[1] Steve Shellhammer, et. al., “PHY Misclassification Issue,” IEEE 802.11-19/0423r1, March 2019
[2] Bin Qian, et. al., “Initial Thought on 2.4 GHz DL AMP PPDU Design,” IEEE 802.11-24/0847r0, May 2024
Doc.: IEEE 802.11-24/1199r1
July 2024