## Slide 1: 2.4 GHz Downlink AMP PPDU Follow Up
Date: 2024-07-18
Authors:
Name | Affiliations | Address | Phone | Email
Bin Qian | Huawei | Shenzhen, China |  | qianbin14@huawei.com
Lei Huang |  | Singapore |  | 
Panpan Li |  | Singapore |  | 
Wei Lin |  | Shenzhen, China |  | 
David, Xun Yang |  | Shenzhen, China |  | 
July 2024
Notes: September 2012

## Slide 2: Abstract
This contribution continues the discussion on the AMP DL PPDU format in the 2.4 GHz frequency band
July 2024

## Slide 3: Recap: Structure of AMP DL PPDU
In [1], we propose some initial thoughts on the AMP DL PPDU format in the 2.4 GHz frequency band
The AMP DL PPDU consists of the OFDM based wideband portion and the On-Off Keying (OOK) based narrowband portion
The NB portion of AMP DL PPDU consists of AMP-Sync field, AMP-SIG field, and AMP-Data field
July 2024

## Slide 4: Consideration on AMP-Data field
The AMP DL may support a wider range of data rates than that of WUR
  There are different types of AMP STAs [2]
    Some AMP STAs have clock accuracy of less than 1k ppm, others have clock accuracy of 10k – 100k ppm
    Different types of AMP STAs may have different sensitivity
  The higher data rate leads to shorter PPDU duration to provide better coexistence
  The lower data rate is helpful to improve the DL reliability of the low-capability AMP STAs
  The lower data rate could be used to compensate the DL-UL imbalance shown in [3]
July 2024

## Slide 5: Consideration on AMP-Sync field
The detection performance of the Sync field should match the performance of the data field
  The Sync field of length 64 us is used for WUR high data rate (HDR)
    For the HDR, the Sync field is specified as the bit sequence
  The Sync field of length 128 us is used for WUR low data rate (LDR)
    For the LDR, the Sync field is specified as the concatenation of two copies of
A dedicated AMP-Sync field allows for more flexibility in optimizing each type of AMP STA
  If lower data rate is introduced, the Sync field needs to be enhanced to avoid becoming a bottleneck
  If higher data rate is introduced, the Sync field needs to be shortened to avoid overdesign
July 2024

## Slide 6: Consideration on AMP-SIG field
In WUR PPDU, the WUR-Sync field carries the data rate information. However, adding more data rates could exhaust the available unique patterns of Sync field, degrading the reliability of the Sync field
A specific AMP-SIG field could easily support a wider range of data rates and additional parameters such as AMP data length, PHY version identifier, UL/DL, BSS color
  These parameters are critical for the receiver to correctly interpret and decode the payload
  Ensuring a more reliable SIG field is beneficial for the overall DL performance
July 2024

## Slide 7: Summary
We further discuss the necessity to include specific AMP-Sync field and AMP-SIG field in the AMP DL PPDU format in the 2.4 GHz frequency band
July 2024

## Slide 8: References
[1] 11-24-0847-00-00bp-initial-thought-on-2.4-ghz-dl-amp-ppdu-design
[2] 11-24-0853-00-00bp-design-target-and-device-capabilities-for-amp-iot
[3] 11-24-0075-00-0amp-follow-up-on-amp-link-budgets
July 2024

## Slide 9: SP 1
Do you support that the AMP DL PPDU in 2.4 GHz frequency band consists of the OFDM based wideband portion and the On-Off Keying (OOK) based narrowband portion?
  The bandwidth of the wideband portion is 20 MHz while the bandwidth of the narrowband portion is TBD.
  Yes:
  No:
  Abstain:
July 2024

## Slide 10: SP 2
Do you support to include an AMP-Sync field in the narrowband portion of the AMP DL PPDU in 2.4 GHz frequency band?
  The AMP-Sync field format is TBD
  Yes:
  No:
  Abstain:
July 2024

## Slide 11: SP 3
Do you support to include an AMP-SIG field in the narrowband portion of the AMP DL PPDU in 2.4 GHz frequency band?
  The AMP-SIG field format is TBD
  Yes:
  No:
  Abstain:
July 2024