## Slide 1: NPCA – Next level discussions
Date: 2024-09-07
Authors:

## Slide 2: Recap
Non-Primary Channel Access (NPCA) feature in UHR enables an AP and a non-AP STA to communicate on a nonprimary channel when the primary channel is busy due to OBSS traffic
TGbn has agreed to the following:
  TGbn defines a mode of operation that enables a STA to access the secondary channel while the primary channel is known to be busy due to OBSS traffic or other TBD conditions.
    The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
    A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is known to be busy due to OBSS traffic or other TBD conditions.

## Slide 3: Introduction
When an OBSS transmission is detected on the BSS primary, NPCA STAs will switch to the NPCA Primary channel and will contend to initiate a TXOP
To ensure coordinated operation on the NPCA Primary, the following details must be specified:
  When can an NPCA transmitter initiate a TXOP after switching?
  How does the transmitter contend on the NPCA Primary channel?
  Which subchannels can the transmitter use after gaining access?
  Are there ways to improve coordination between two peer NPCA STAs?
In this contribution, we provide the details on the above aspects of NPCA

## Slide 4: Switching delay
A switch from the Primary channel to the NPCA Primary channel will incur a delay
  Refer to this as the NPCA Switching delay
Similarly, a switch from the NPCA Primary channel to the BSS Primary channel will also incur a delay
  Refer to this as the NPCA Switch back delay
The spec must allow the NPCA STAs to signal these delays to its peer
  As an example, AP advertises its switching delays in Management frame(s) that it transmits, and a non-AP STA provides its switching/switch back delays when it exchanges frames for enabling NPCA mode
Each NPCA STA must honor the switching and switch back delay of its peer when initiating a TXOP on the NPCA Primary channel
  Which implies that after switching, the NPCA transmitter shall not transmit a frame to the NPCA receiver until the receiver’s NPCA Switching delay has elapsed
    Note: the delay time must be applied after a reference switch time which is TBD and needs to be defined

## Slide 5: Contention on NPCA Primary channel
Two successive switches to the NPCA Primary channel may be separated by large gaps
During this time, NPCA STAs
  Will not contend on the NPCA Primary channel
  Are not required to be aware of OBSS activity (if any) on the NPCA Primary channel
Therefore, an NPCA STA doesn’t have to maintain the contention parameters for the NPCA primary in the same manner as the BSS’s primary channel (which it will be accessing more often).
For simplicity, we propose:
  NPCA STAs do not need to maintain the backoff state for the NPCA Primary channel after switching back to the primary channel
  Instead, every time the NPCA STA switches to the NPCA Primary channel, it sets the CW to a certain value and picks a new backoff counter value

## Slide 6: Subchannels used for NPCA transmissions
After gaining the right to initiate a TXOP on the NPCA Primary channel, the NPCA STA can combine additional idle 20 MHz subchannels
However, these 20 MHz subchannels must satisfy the following conditions:
  Include the NPCA Primary channel
  Be within the AP’s BSS bandwidth
  Must not occupy the channels within the bandwidth of the OBSS transmission on the BSS Primary channel
  Must not include any channel that the AP has punctured using the Disabled Subchannel Bitmap
To utilize the entire remaining bandwidth, puncturing may be required
  E.g., if OBSS BW is 40 MHz in a 160 MHz BSS, utilizing the remaining 120 MHz requires puncturing
  However, if an immediate response is required, per 11be rules, this can be achieved only by soliciting TB PPDUs
  Further discussion is needed on whether a frame that does not solicit TB PPDUs can puncture subchannels beyond those that are indicated in the Disabled Subchannel Bitmap

## Slide 7: Trigger frames signaling in NPCA (1/2)
When NPCA STA switches to NPCA Primary channel,
  It performs ED, PD, and contends for access on NPCA Primary channel
  Monitors for incoming PPDUs from peer NPCA STA on the NPCA Primary channel
  Thus, during an NPCA opportunity, the NPCA Primary channel serves as a temporary primary channel for the NPCA STA
In a triggered UL OFDMA transmissions, the RU assigned to the STA is with respective to the primary channel.
  For example, B1-B7 of RU Allocation indicate the RU assigned to the non-AP STA within an 80 MHz block of the BSS bandwidth, wherein the 80 MHz block is identified by B0 and PS160 fields
  However, when operating on the NPCA primary channel there is an ambiguity as to which is the reference primary channel.
Since the NPCA primary channel acts as a temporary primary channel, we propose to use the NPCA Primary channel as the reference primary for triggered UL OFDMA operation

## Slide 8: Trigger frames signaling in NPCA (2/2)
There may be instances where an OBSS transmissions is detected by the non-AP STA but not detected by the AP
  In such a scenario, the AP might transmit a Trigger frame spanning the entire BSS bandwidth, which includes the NPCA Primary channel
  The non-AP STA that has switched to the NPCA Primary channel, upon decoding the Trigger frame, might infer the wrong RU and respond in the wrong RU
Can be resolved by including an explicit indication when Trigger frame is transmitted via the NPCA Primary channel
  The non-AP STA can combine the explicit indication with the RU Allocation and respond in the correct RU

## Slide 9: Improving coordination in NPCA (1/2)
There can be loss of coordination between the NPCA AP & NPCA non-AP STA if both AP and non-AP STA contend and transmit
  For example, due to hidden node or the asymmetric view problem among other issues
  Hidden node problem: When one peer observes OBSS but other does not
    If AP does not observe OBSS, client’s EDCA transmission would be wasted
    If client does not observe OBSS, TXOP is still successful as long as one NPCA STA responds to the AP
  Asymmetric view: When NPCA AP and non-AP STA observe different OBSS PPDU/TXOP
    The duration for which BSS Primary channel is Busy is different at the two NPCA peers (see adjoining figure)
    Client’s EDCA transmission might initiate TXOP for a duration longer than what is Busy at the AP
      Causing AP to become unavailable on the BSS Primary channel for a portion of time

## Slide 10: Improving coordination in NPCA (2/2)
Proposal: Define a mode under NPCA where NPCA non-AP STAs do not use untriggered UL transmissions
In both problems discussed in the previous slide, it is the AP’s view that matters
  If AP is performing frame exchanges on NPCA Primary channel beyond how long its BSS Primary channel is Busy, legacy non-AP STA can have a performance impact
  Therefore, it is more efficient for the AP to initiate TXOP as per what it observes on the BSS Primary channel
Enabling a mode where NPCA non-AP STAs do not use untriggered UL transmissions may lower cases of coordination loss between NPCA peers

## Slide 11: Summary
NPCA can improve spectral utilization by utilizing unused secondary channels when the primary channel is Busy
However, switching and transmissions on the NPCA Primary channel must be coordinated to maximize these gains
In this contribution we presented details on the following aspects:
  When is the earliest that an NPCA transmitter can initiate a TXOP after switching
  How the transmitter contends on the NPCA Primary channel
  Which channels can be used by the NPCA transmitter after it gains access
  How a trigger-only mode under NPCA improves coordination between peer NPCA STAs

## Slide 12: Straw Polls
Do you agree that an NPCA STA shall indicate the following to its peer NPCA STA?
  NPCA switching delay
    time it needs to switch from the BSS Primary channel to the NPCA Primary channel
  NPCA switch back delay
    time it needs to switch from the NPCA Primary channel to the BSS Primary channel

## Slide 13: Straw Polls
Do you agree with the following:
  An NPCA STA shall initiate frame exchange on the NPCA Primary channel with an NPCA Initial Control Frame in the non-HT PPDU or non-HT duplicate PPDU format using a rate of 6 Mb/s, 12 Mb/s, or 24 Mb/s
  Details on NPCA ICF are TBD

## Slide 14: Straw Polls
Do you agree that an NPCA STA shall initiate a TXOP on the NPCA Primary channel following the rules defined in 10.23.2.2 (EDCA backoff procedure) and 10.23.2.4 (Obtaining an EDCA TXOP) with the following exception:
  Every time the STA switches to the NPCA Primary channel, it shall initialize CW_NPCA[AC] to TBD value and pick a new backoff counter (BO_NPCA) randomly between 0 and CW_NPCA[AC]. QSRC_NPCA[AC] shall be set to 0.
  NOTE – Baseline EDCA procedure is followed on the BSS Primary channel. The values of CW_NPCA and BO_NPCA are discarded by the NPCA STA when it switches back to the BSS Primary channel.

## Slide 15: Straw Polls
Do you support that after an NPCA STA has gained the right to initiate a TXOP on the NPCA Primary channel, it can transmit on a set of channels that:
  Includes the NPCA Primary channel, and
  are within the AP’s BSS bandwidth, and
  do not include the channels in the bandwidth occupied by the OBSS traffic that caused the NPCA STA to switch from the BSS primary channel to the NPCA primary channel, and
  do not include the channels that are indicated as punctured in the Disabled Subchannel Bitmap subfield in the EHT Operation element,
  It is TBD whether a frame that does not solicit TB PPDUs can puncture 20 MHz subchannels not indicated as punctured in the Disabled Subchannel Bitmap subfield of the EHT Operation element

## Slide 16: Straw Polls
Do you agree to the following:
  When soliciting an UL TB PPDU on the NPCA Primary channel, the NPCA AP shall signal the RU index considering the NPCA Primary channel as the reference primary channel
    The Trigger frame soliciting the TB PPDU shall explicitly indicate that it is transmitted via the NPCA Primary channel (details TBD)

## Slide 17: Straw Polls
Do you agree to define a mode of operation in NPCA where the NPCA non-AP does not use untriggered UL transmissions on the NPCA primary channel
  This mode can be enabled/disabled by the AP
  Whether the mode is for all associated non-APs or per non-AP is TBD
  TBD whether MU EDCA parameters mechanism is used for this or not

## Slide 18: References
[1] M. Park, et al., “11-24/0495r0: Non-Primary Channel Access (NPCA) – Follow Up”