## Slide 1: ICF ICR Follow Up
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: ICF/ICR and Baseline BSRP
ICF can be transmitted by an AP for the following dynamic initial control information:
  Soliciting non-AP STA’s available time and future unavailable time for in-device co-existence.
  Soliciting non-AP STA’s low capability sate to high capability state switch.
  Reporting AP’s future unavailable time for in-device co-existence.
  Announcing Tx/Rx parameter restriction (maximal BA, NSS) of the TXOP responders, i.e., addressed STAs of BSRP Trigger.
ICF can be transmitted by a non-AP STA for the following dynamic initial control information:
  Soliciting AP’s available time and future unavailable time for in-device co-existence.
  Reporting STA’s future unavailable time for in-device co-existence.
  Announcing Tx/Rx parameter restriction (maximal BA, NSS) of the TXOP responders, i.e., addressed AP of BSRP Trigger.
A non-AP STA solicited by BSRP Trigger can do the following things:
  Reporting buffer status for AP’s resource allocation in TB PPDU.
  Reporting resource request for STA’s P2P frame exchanges.

## Slide 3: Open Questions of BSRP Trigger ICF and ICR
The ICF/ICR frame format to carry initial control information needs to be further clarified.
  In 11-24/494, special User Info field (s) of ICF before Padding field is proposed to carry the initial control information.
  In 11-24/494, Per AID TID Info field (s) of ICR with special AID value is proposed to carry the initial control information.
  In 11-24/857, Multi-STA BA as ISR is proposed.
Can both the non-AP STA’s responding with resource request and the non-AP STA’s responding with ICR be solicited in one Trigger frame?
If the answer is yes, can an AP explicitly or implicitly indicate whether a BSRP Trigger solicit both resource request and dynamic initial control information?

## Slide 4: Common Initial Control Info in ICF Trigger
The Common Initial Control Info field with 0 (when no common initial control info exists), one or multiple Type + Length + Content tuples are carried after 16-bit all 1s in the Padding field of the Trigger frame.
The Common Initial Control Info Length field indicate the length of the Common Initial Control Info field, e.g. in octets.
  Another variant is that the Special User Info field indicates whether the Common Initial Control Info exists, and if the Common Initial Control Info exists, the Common Initial Control Info Length is not needed.
    An addressed STA that needs to check pre-FCS does the following:
      An addressed STA that doesn’t support initial control information but supports control frame protection figures out PN + MIC by decoding the length of each Type + Length + Content.
      An addressed STA that doesn’t support initial control information and control frame protection figures out pre-padding FCS by decoding the length of each Type + Length + Content and then skipping 14-octet PN + MIC.
PN
1111111111111111
Sixteen 1s
MIC
6 Octets or 0
8 Octets or 0:
Pre-Padding FCS
4 octets or 0
Additional Padding
variable
Common Initial Control Info Length
2 Octets or 0
Variable:
Common Initial Control Info
Protected ICF Trigger

## Slide 5: Common Initial Control Info in ICF Trigger
The Common Initial Control Info field with 0 (when no common initial control info exists), one or multiple Type + Length + Content tuples are carried after 16-bit all 1s in the Padding field of the Trigger frame.
The Common Initial Control Info Length field indicate the length of the Common Initial Control Info field, e.g. in octets.
  Another variant is that the Special User Info field indicates whether the Common Initial Control Info exists, and if the Common Initial Control Info exists, the Common Initial Control Info Length is not needed.
    An addressed STA that needs to check pre-FCS does the following:
      An addressed STA that doesn’t support initial control information but supports control frame protection figures out PN + MIC by decoding the length of each Type + Length + Content.
      An addressed STA that doesn’t support initial control information and control frame protection figures out pre-padding FCS by decoding the length of each Type + Length + Content and then skipping 14-octet PN + MIC.
PN
1111111111111111
Sixteen 1s
MIC
6 Octets or 0
8 Octets or 0:
Pre-Padding FCS
4 octets or 0
Additional Padding
variable
Common Initial Control Info Length
2 Octets or 0
Variable:
Common Initial Control Info
Protected ICF Trigger

## Slide 6: Per User Initial Control Info in ICF Trigger
One option for the user initial control info is that the User Initial Control Info List field is carried after Common Initial Control Info field.
  The User Initial Control Info List field includes 0, 1 or multiple Per User Initial Control Info field.
The User Initial Control Info List Length field indicate the length of the User Initial Control Info List field, e.g. in octets.
  Another variant is that the Special User Info field indicates whether the User Initial Control Info List field exists, and if the User Initial Control Info List field exists, the User Initial Control Info List Length is not needed.
    An addressed STA that needs to check pre-FCS does the following:
      An addressed STA that doesn’t support initial control information but supports control frame protection figures out PN + MIC by decoding the length of each Type + Length + Content of Common User Info, and Per User Initial Control Info fields.
      An addressed STA that doesn’t support initial control information and control frame protection figures out pre-padding FCS by decoding the length of each Type + Length + Content, skipping Per User Initial Control Info fields, and then skipping 14-octet PN + MIC.
PN
1111111111111111
Sixteen 1s
MIC
6 Octets:
8 Octets:
Pre-Padding FCS
4 octets
Additional Padding
variable
Common Initial Control Info Length
2 Octets:
Variable:
Common Initial Control Info
Protected ICF Trigger
Variable:
User Initial Control Info List
User Initial Control Info List Length
2 Octets:

## Slide 7: Mixing Resource Request and ICR or Not
Option 1:
  A BSRP Trigger frame can be used to solicit the responding frames from the following non-AP STAs:
    Non-AP STA supporting low capability listening and in-device coexistence,
    Non-AP STA supporting low capability listening,
    Non-AP STA supporting in-device coexistence, and
    Non-AP STA not supporting any of the following low capability listening, in-device coexistence.
Option 2:
  A BSRP Trigger frame can be used to solicit the responding frames from the following Non-AP STAs:
    Either
      Non-AP STAs supporting low capability listening,
      Non-AP STAs supporting in-device coexistence, and
    Or
      Non-AP STAs not supporting any of the following low capability listening, in-device coexistence.
Option 1 is preferable

## Slide 8: Mixed ICR Information and Resource Request or Not
Option 1:
  A non-AP STA that supports ICR and is solicited by the first ICF frame will respond with all the following information if supported by the non-AP STA:
    Available time, and unavailable time (start time and duration) if known,
    Resource request information.
  A non-AP STA that supports ICR and is solicited by a Trigger other than the first ICF frame will respond with resource request information.
  The AP needs to allocate enough resource in the solicited TB PPDU for each addressed STA to transmit all the responding information supported by the AP
    Available time, and unavailable time (start time and duration) if known,
    Resource request information.
Option 2:
  In BSRP Trigger frame, the solicited information is explicitly indicated.
Option 2 is preferable.
  Otherwise, a non-AP STA needs to provide the different feedback based on whether it is first polled by the AP.
  Additionally, the AP and non-AP STA may have the different view about whether AP already correctly receive the ICR feedback.

## Slide 9: SP 1
Do you support that if the intermediate FCS and the PN/MIC fields are both present in a Trigger frame then the intermediate FCS shall appear immediately after the PN/MIC field?