## Slide 1: ICF ICR Follow Up
Date: 2024-07-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: ICF Consideration
BSRP as ICF can be transmitted by an AP for the following dynamic initial control information:
  Soliciting non-AP STA’s available time and unavailable time for in-device co-existence (IDC).
BSRP as ICF can be transmitted by a non-AP STA for the following dynamic initial control information:
  Reporting STA’s available time and unavailable time for in-device co-existence.
MU-RTS, BSRP Trigger can be used in EMLSR, low-capability mode to high-capability mode switch, DSO where no initial control information is carried in responding frame.

## Slide 3: Protected ICF Trigger with Intermediate FCS
If required by the enabled feature solicited by the ICF or Trigger frame, the recipient may need to stop the decoding of the soliciting Trigger frame that is protected before the padding.
  Both intermediate FCS and PN + MIC exist in the soliciting Trigger frame.
The intermediate FCS is after PN and MIC for control frame protection.
  This can guarantee the received Trigger frame successfully pass the CRC checking for the usage of the Trigger frame content.
PN
1111111111111111
Sixteen 1s
MIC
6 Octets or 0
8 Octets or 0:
Intermediate FCS
4 octets or 0
Additional Padding
variable
Protected ICF Trigger

## Slide 4: ICR
When multiple TXOP responders are solicited by BSRP Trigger as ICF, the responding frames need to be carried in TB PPDU.
  (Multi-STA BA as ICR when carrying feedback (available/unavailable time),
  QoS Null when no feedback is reported

## Slide 5: Mixing Resource Request and ICR or Not
A BSRP Trigger frame can be used to solicit the responding frames from the following non-AP STAs:
  Non-AP STA supporting low capability mode (LCM) and in-device coexistence,
  Non-AP STA supporting DSO,
  Non-AP STA supporting in-device coexistence (IDC),
  Non-AP STA not supporting any of the LCM, DSO, IDC.
Some features, e.g. LCM, DSO, need to early stop the decoding of the Trigger frame.

## Slide 6: Mixed ICR Information and Resource Request or Not
A non-AP STA that supports ICR and is solicited by the ICF frame will respond with all the following information if supported by the non-AP STA:
  Available time, and unavailable time (start time and duration) if known,
  Resource request information.
The AP needs to allocate enough resource in the solicited TB PPDU for each addressed STA to transmit all the responding information supported by the AP
  Available time, and unavailable time (start time and duration) if known,
  Resource request information.

## Slide 7: Summary
This presentation discusses the following:
  ICF, ICR frame
  The responding PPDU when multiple STAs are solicited by an ICF.
  The PN + MIC and intermediated FCS in ICF

## Slide 8: SP 1
Do you support to use BSRP Trigger frame as a UHR Initial Control frame (ICF) sent:
  From an AP for soliciting response in TB PPDU format from one or more scheduled STAs, and to allow an M-BA frame to be included in the TB PPDU sent by the UHR scheduled STAs in response, when carrying feedback (i.e. unavailability) information
    BSRP Trigger frame follows baseline rules for the format of the solicited TB-PPDU

## Slide 9: SP 2
Do you support that if the intermediate FCS and the PN/MIC fields are both present in a Trigger frame then the intermediate FCS shall appear immediately after the PN/MIC field?