## Slide 1: Initial control frames and initial control response design
Date: 2024-07-12
Authors:

## Slide 2: Summary of proposals
ICF-ICR exchange will be a key component of many new features in 11bn
  STA Dynamic power save (transition from low capability to high capability mode)
  eMLSR enhanced power save (thanks to intermediate FCS)
  Container for dynamic feedbacks (i.e. unavailability periods)
  DSO, NPCA
And it is a key component for eMLSR both for EHT and UHR STAs
Design goal:
  Have an ICF-ICR sequence for SU, where the response is carried in non-HT Dup format (for UL and to ensure better NAV protection in presence of pre-HE STAs)
  Have an ICF-ICR sequence for MU, where the response is carried in TB PPDU format
  Enable all new features, and ensure compatibility with legacy features and STAs

## Slide 3: ICR design: Multi-STA BA
Multi-STA BA seems like a good and flexible container for carrying the dynamic feedbacks (unavailability), security fields, and padding
Define 1st Special per AID TID info fields that are designed to contain feedbacks (can be called Feedback Per AID TID Info field or Feedback field)
Define 2nd Special per AID TID info fields that are designed to contain Security fields (can be called Security Per AID TID Info field or Security field)
Define 3rd Special per AID TID info fields that are designed to contain feedbacks (can be called padding field)
Frame Control
Duration
RA
TA
BA Control
BA Info
FCS
Per AID TID Info
Per AID TID Info
Security Per AID TID Info
Feedback Per AID TID Info
padding Per AID TID Info
…
New field

## Slide 4: ICR design: Multi-STA BA
Feedback Per AID TID Info fields
Use Special per AID TID info fields that are designed to contain feedbacks (can be called Feedback Per AID TID Info fields)
  Identification of a Feedback Per AID TID Info field compared to a regular Per AID TID Info field is proposed to be done thanks to the TID and Ack Type fields. Example TID=13, Ack Type=0
  This allows to keep BA SSC (Starting Sequence Control field) to modify the size of the BA Bitmap (0,4,8,16,32,64,128) to better match the contained feedback size or in case there are multiple feedbacks, and to be backward compatible
AID11 field setting:
  If the ICR is unicast: AID value set to special value or destination STA (doesn’t matter)
  If the ICR is broadcast: AID value set to special value (for common feedback) or destination STA (for per STA feedback)

## Slide 5: ICF design
Needs a frame that solicits TB Response for M-user
Needs a frame that solicits non-HT Dup Response for single user, for UL, and to get NAV protection from pre-HE STAs.
Needs to be backward compatible
  ICF able to open a TxOP for legacy STAs (especially EHT eMLSR STAs) and UHR STAs
Needs to be able to:
  Have an ICF that can solicit an ICR that can include feedbacks (unavailability) in an unsolicited manner
In this presentation, we focus only on the scope of DL MU operation
  i.e. ICF trigger frame sent by an AP and that solicits ICR response in TB PPDU format
We’ll have a follow-up presentation

## Slide 6: ICF proposal for soliciting TB PPDU: BSRP trigger frame
Looking at all the requirements that we listed in previous slides, the choice of the BSRP Trigger Frame seems very logical
One of the biggest advantage is that it is already an ICF for eMLSR in 11be, and therefore allows to schedule legacy STAs and UHR STAs with a single frame
  Inclusion of Intermediate FCS, security fields, padding is either native or can be done easily in a backward-compatible way

## Slide 7: ICF proposal for soliciting TB PPDU: BSRP trigger frame
BSRP TF design as ICF
  Define ways to include Intermediate FCS (several good proposals have already been proposed) for some mechanisms (eMLSR, DPS, …)
  Define ways to include security fields if we allow control frame protection
  Modify the BSRP rules so that the intended receiver can include a Multi-STA BA frame in the PPDU sent in response, at least when it wants to carry unavailability indications or if it enables control frame protection

## Slide 8: Straw poll #1
Do you support to include the following in the 11bn SFD:
11bn uses BSRP Trigger frame as a UHR Initial Control frame (ICF) sent from an AP for soliciting response in TB PPDU format from one or more scheduled STAs, and to allow an M-BA frame to be included in the TB PPDU sent by the UHR scheduled STAs in response, when carrying feedback (i.e. unavailability) information or when the response is protected
NOTE: What frame to use as a UHR Initial Control frame (ICF) soliciting a response from a single STA in non-HT (Dup) PPDU that carries feedback (i.e. unavailability) information or that is protected is TBD