## Slide 1: Considerations on Client Power Save for 11bn
Date: 2024-09-10
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com

## Slide 2: Introduction
IEEE 802.11bn task group has agreed to define Dynamic Power Save（DPS） mode for a STA that is a UHR Mobile AP or a UHR non-AP STA wherein the STA may transition from a lower capability mode to a higher capability mode upon reception of an initial control frame
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, e)
  Initial Control frame is TBD
  NSS and MCSs, with at least one higher capability than that in the lower power capability modWhether that applies for a non-mobile AP is TBD
This contribution proposes a mechanism for the flexible management of DPS mode.

## Slide 3: DPS as a mode of operation
The benefit from Dynamic Power Save（DPS） mode depends on the requirements of the traffic to be delivered and power save for the UHR non-AP STA in DPS mode .
DPS-capable non-AP STAs can enable or disable the DPS mode when it is associated with the DPS-capable AP
Enabling the DPS mode, the STA can
operate in its lower capability mode when no DPS initial control frame (ICF) addressed to it is received
do frame exchanges in a higher capability mode followed by an DPS ICF addressed to it from its associated AP.
Disabling the DPS mode, the STA always
operate in its full capability mode when the STA stay in the active mode.

## Slide 4: DPS as a mode of operation (Cont.)
Signaling for DPS mode
Enabling DPS mode:
An DPS-capable non-AP STA can enable dynamically DPS mode by notifying the DPS-capable AP or by negotiating with the DPS-capable AP.
DPS operation parameters, such as DPS mode indication（enabling DPS mode）, DPS padding delay, optional operating parameters for the lower capability mode and higher capability mode are carried in the DPS mode management frames (such as DPS mode notification frame).
Frame exchanges in DPS mode:
The DPS-capable non-AP STA operates in its lower capability mode when no DPS initial control frame (ICF) addressed to it is received
The DPS-capable non-AP STA does frame exchanges in a higher capability mode followed by an DPS ICF addressed to it from its associated AP.
Updating parameter(s) in DPS mode.
An DPS-capable non-AP STA in DPS mode can update dynamically DPS parameters by sending a DPS mode notification frame with DPS mode indication (enabling DPS mode) and DPS parameters to be updated to the DPS-capable AP. AP optionally responds to the DPS mode notification frame.

## Slide 5: DPS as a mode of operation (Cont.)
Signaling for DPS mode
Disabling DPS mode:
An DPS-capable non-AP STA can disable dynamically DPS mode by notifying the DPS-capable AP or by negotiating with the DPS-capable AP.
DPS mode indication（disabling DPS mode）is carried in the DPS mode exchange frames (such as DPS mode notification frame).
AP optionally responds to the DPS mode notification frame sent by the STA.
Behavior of the DPS-capable non-AP STA when disabling DPS mode:
the STA always operate in its full capability mode when the STA stays in the active mode.

## Slide 6: Summary
The benefit from DPS depends on the requirements of the traffic to be delivered and power save for the UHR non-AP STA in DPS mode .
DPS as a mode of operation is suggested to be considered for the flexible management of DPS:
Enabling/disabling the DPS mode based on the requirements of the traffic to be delivered and/or power save for DPS-capable non-AP STAs.
updating the operating parameters in DPS mode depending on the requirements of the traffic to be delivered and/or power save for DPS-capable non-AP STAs.

## Slide 7: References
[1] UHR proposed PAR, https://mentor.ieee.org/802.11/dcn/23/11-23-0480-01-0uhr-uhr-proposed-par.pdf
[2] Power Save Protocols for UHR - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0544-01-00bn-power-save-protocols-for-uhr-follow-up.pptx
[3] Client power save, https://mentor.ieee.org/802.11/dcn/23/11-23-2003-00-00bn-client-power-save.pptx
Liuming Lu (OPPO)

## Slide 8: SP
SP : Do you support to specify a mechanism for enabling or disabling Dynamic Power Save（DPS） mode in UHR?
The mechanism is TBD.
Liuming Lu (OPPO)