## Slide 1: Considerations on Client Power Save for 11bn
Date: 2024-09-10
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Chaoming Luo |  |  |  | 
Ning Gao |  |  |  | 
Yapu Li |  |  |  | 
Liangxiao Xin |  |  |  | 

## Slide 2: Introduction
Power save is very important especially for client devices such as mobile phones. Currently 802.11bn task group has agreed to define Dynamic Power Save（DPS） mode.
the STA that uses DPS mode may transition from a lower capability (LC) mode to a higher capability (HC) mode upon reception of an initial control frame
  Lower capability mode (e.g., 20 MHz BW, one SS, limited data rates, PPDU format)
  Higher capability mode (e.g., operating BW, NSS and MCSs, with at least one higher capability than that in the lower power capability mode)
  Initial Control frame is TBD
  Whether that applies for a non-mobile AP is TBD
This contribution proposes a mechanism for the flexible management of DPS mode.
More parameters to be signaled for DPS mode can be considered
  Enabling/disabling DPS mode
  DPS padding delay and DPS switch back delay
  the TX/RX parameters in lower capability (LC) mode
  the TX/RX parameters in higher capability (HC) mode

## Slide 3: Signaling for DPS mode
  DPS mode indication (name TBD): Enabling/disabling DPS mode
  DPS mode indication can be used to indicate the DPS mode of a STA in active mode, for example, it is set to 1 to indicate that the STA will enable DPS mode, and set to 0 to indicate that the STA will disable DPS mode.
  DPS padding delay & DPS switch back delay
  DPS padding delay: time the STA needs to switch from the lower capability (LC) mode to higher capability (HC) mode
  DPS switch back delay :time it needs to switch from the higher capability (HC) mode to the lower capability (LC) mode
  The two parameters may change after the STA is associated with the AP, for example, the TX/RX parameters of HC mode may be updated due to the operating mode (OM) change of the STA so that the delay parameters may be required to be updated accordingly.

## Slide 4: Signaling for DPS mode (Cont.)
  TX/RX parameters in LC/HC mode
  By default
  Lower capability mode: 20 MHz BW, one SS, limited data rates, PPDU format
  Higher capability mode: full capability mode
  the TX/RX parameters for lower capability (LC) mode and/or higher capability mode can be optionally indicated
  Pro: finer or more flexible DPS; Con: overhead for signaling
  Lower capability mode: 20(+) MHz BW, one(+) SS, limited data rates, PPDU format
  an intermediate capability between the lower capability mode and full capability may act as another higher capability mode.

## Slide 5: DPS as a mode of operation
DPS-capable non-AP STAs can enable or disable the DPS mode when it is associated with the DPS-capable AP
Enabling DPS mode:
An DPS-capable non-AP STA can enable dynamically DPS mode by notifying the DPS-capable AP or by negotiating with the DPS-capable AP.
DPS operation parameters, such as DPS mode indication（enabling DPS mode）, DPS padding delay, DPS switch back delay, optional operating parameters for the lower capability mode and higher capability mode are carried in the DPS mode management frames (such as DPS mode notification frames).
Frame exchanges in DPS mode:
The DPS-capable non-AP STA operates in its lower capability mode when no DPS initial control frame (ICF) addressed to it is received
The DPS-capable non-AP STA transitions from a lower capability (LC) mode to a higher capability (HC) mode upon reception of an initial control frame and do frame exchanges in a higher capability mode if the transition is required.
Updating parameter(s) in DPS mode.
An DPS-capable non-AP STA in DPS mode can update dynamically DPS parameters by sending a DPS mode notification frame with DPS mode indication (enabling DPS mode) and DPS parameters to be updated to the DPS-capable AP. AP optionally responds to the DPS mode notification frame.

## Slide 6: DPS as a mode of operation (Cont.)
DPS-capable non-AP STAs can enable or disable the DPS mode when it is associated with the DPS-capable AP
Disabling DPS mode:
An DPS-capable non-AP STA can disable dynamically DPS mode by notifying the DPS-capable AP or by negotiating with the DPS-capable AP.
DPS mode indication（disabling DPS mode）is carried in the DPS mode exchange frames (such as DPS mode notification frame).
AP optionally responds to the DPS mode notification frame sent by the STA.
Behavior of the DPS-capable non-AP STA when disabling DPS mode:
the STA always operate in its full capability mode when the STA stays in the active mode.

## Slide 7: Summary
The benefit from DPS mode depends on the environments where the STA is located, the requirements of the traffic to be delivered for the STAs, the TX/RX parameters in lower capability (LC) mode and/or higher capability (HC) mode.
An mechanism for the flexible management of DPS mode is suggested to be considered:
Enabling/disabling the DPS mode
updating the operating parameters in DPS mode,
the operating parameters to be indicated for DPS mode may include:
DPS mode indication
DPS padding delay
DPS switch back delay
optional operating parameters in the lower capability mode
optional operating parameters in higher capability mode

## Slide 8: References
[1] UHR proposed PAR, https://mentor.ieee.org/802.11/dcn/23/11-23-0480-01-0uhr-uhr-proposed-par.pdf
[2] Power Save Protocols for UHR - follow up, https://mentor.ieee.org/802.11/dcn/24/11-24-0544-01-00bn-power-save-protocols-for-uhr-follow-up.pptx
[3] Client power save, https://mentor.ieee.org/802.11/dcn/23/11-23-2003-00-00bn-client-power-save.pptx
Liuming Lu (OPPO)

## Slide 9: SP
SP : Do you support to specify a mechanism for enabling or disabling Dynamic Power Save（DPS） mode in UHR?
The mechanism is TBD.
Liuming Lu (OPPO)