## Slide 1: Triggered Beamforming in TGbn - More Insights
Date: 2024-07-04
Authors:

## Slide 2: Introduction
Support for beamforming in TB PPDUs has been discussed in 11be [1] as well as during the UHR SG [2-4]
In [5] we summarized the benefits of supporting BF for TB PPDUs, and then ran a SP for ‘defining a protocol for supporting triggered UL beamformed data transmission in TGbn’
  The results were 105Y, 71N
Here we share some more results and insights based on offline discussions; in particular, we discuss non-triggered per-STA precoding, its performance compared with triggered (joint) precoding and the reason for the performance gap.

## Slide 3: Recap - Benefits of Beamforming with TB PPDUs
There are several, non-negligible benefits associated with applying beamforming (precoding) to TB PPDUs:
  Huge gain (e.g. 8dB) in the UL MU-MIMO case, as shown in [2] and [3]
  More modest, but still substantial, gains in the UL SU-MIMO case, as shown in [1]
  Applying orthogonal (e.g. SVD-based) precoders in the SU-MIMO case means linear detection is optimal, so this can lead to lower complexity and lower power consumption for the AP’s receiver
  There are many non-AP STA devices today that support beamforming, but cannot support it in the TB PPDU case due to protocol/standard limitations, so we can remove that restriction

## Slide 4: Issues with non-triggered Per-STA Precoding
For both SU-MIMO and MU-MIMO, can non-triggered per-STA UL sounding work?
  In the case of SU-MIMO, precoders computed separately per-STA are generally good
  Issue #1 relates to the individual non-AP STA that initiates the UL sounding procedure with the AP at its own discretion, rather than triggered by the associated AP.
    When triggered by the AP for UL beamformed data transmission:
      Since each non-AP STA transmits its sounding NDP at a different time, one precoder (corresponding to one specific non-AP STA) may be much ‘older’ than another STA’s precoder - and the former may not be relevant anymore – therefore degrading the performance at the AP (receiver) side
      The AP might expect accuracy variation between the non-AP STAs with valid precoder data (since the precoder is measured at different times by each non-AP STA).
    Adding individual request from each non-AP STA to start UL sounding procedure seems inefficient (compared to a unified, AP managed and efficient protocol).
  Issue #2 relates to the MU-MIMO case, in particular the usage of per-STA precoding rather than ‘Joint precoding’ which is computed by the AP for all the solicited non-AP STAs
    Using the “per-STA precoding” gives little to no gain over open-loop transmissions (doesn’t decrease the MUI), as opposed to using a ‘joint precoder’ computed at the AP which yields a huge gap
    This is demonstrated in the next slides

## Slide 5: Precoded UL MU-MIMO: Goodput Results
In order to make a fair evaluation of the performance, we look at 2x2 and 4x4 cases, with several payload sizes
We assume the following:
  2x2 and 4x4, in each case 2 or 4 STAs transmit a single stream to the AP; STAs are equipped with 2 Tx antennas
  LDPC, TGn-D NLOS, Smoothing CHEST (for both the sounding NDP and the data PPDU), MMSE detection
  Precoder provided to STAs using MCS 3
  25KB/100KB of payload
  At each SNR we find the MCS which maximizes the goodput
  All frame durations (e.g. NDP, NDP-A, precoder, BA) are considered for goodput
We compare between 3 different schemes:
  Open-Loop MU-MIMO (no precoding)
  UL MU-MIMO with per-STA precoding (ignoring protocol issues described earlier)
  UL MU-MIMO with joint precoding

## Slide 6: Precoded UL MU-MIMO: Goodput Results
For 25KB payload in the 2x2 case we get the following results
There is a large gain for most of the SNR range
Per-STA precoding performs poorly; why?
Per stream precoder tries to maximize the SNR regardless of the MIMO matrix correlation, whereas the joint-precoder does take the correlation into account!
5dB gain

## Slide 7: Precoded UL MU-MIMO: Goodput Results
For 25KB payload in the 4x4 case we get the following results
There is a large gain for most of the SNR range
Again, per-STA precoding performs poorly
6dB gain

## Slide 8: Precoded UL MU-MIMO: Goodput Results
For 100KB payload in the 2x2 case we get the following results
There is a large gain for all of the SNR range
Again, per-STA precoding performs poorly
~5dB gain

## Slide 9: Precoded UL MU-MIMO: Goodput Results
For 100KB payload in the 4x4 case we get the following results
There is a large gain for all of the SNR range
Again, per-STA precoding performs poorly
7dB gain

## Slide 10: Conclusions
Beamforming is an important feature of 802.11, and is widely used in products, in both DL & UL
Since 11ax, triggered transmissions (TB PPDUs) are commonly used in the UL
However, beamforming is not supported for TB PPDUs (both OFDMA/SU-MIMO and MU-MIMO)
  Adding support is expected to improve the throughput & reliability across the entire SNR range, aligning with the scope of TGbn
  This is especially true given the multiple benefits associated with precoded TB transmissions
  The corresponding complexity is quite limited
Precoded TB PPDUs should be supported within TGbn

## Slide 11: References
[1] 11-20-1672r2: UL Beamforming for TB PPDUs (Shimi Shilo et al)
[2] 11-23-27r1: Uplink MU-MIMO Improvements (Sigurd Schelstraete et al)
[3] 11-23-725r0: Uplink MU-MIMO Precoding – Follow Up (Sigurd Schelstraete et al)
[4] 11-23-263r0: Triggered Beamforming in UHR (Shimi Shilo et al)
[5] 11-24-108r0: Triggered Beamforming in UHR – Follow Up (Shimi Shilo et al)