## Slide 1: Further considerations for UHR preamble
Date: 2024-07-11
Authors:

## Slide 2: Introduction
Preamble design requires careful consideration
  Should be able to accommodate all expected functionality (and associated signaling) for UHR
  Signaling bits in preamble are limited
Previous submissions [1, 2] suggested an approach to avoid duplication between EHT and UHR functionality
  Modes already supported in EHT don’t need to be supported in UHR
  Duplication might lead to extra testing time and confusion in deployment
Other submissions [3] prioritize simplicity over avoidance of duplication
  New PHY Version ID for all UHR transmissions

## Slide 3: Purpose of submission
Have we identified all the requirements for UHR preamble?
Invite further discussion on required functionalities before locking down preamble design
  Ways to avoid duplication (if desired) is not the only factor
This submission looks at possible requirements that could impact preamble design
  Specifically: OFDMA support for 11be and 11bn
  Invite others to formulate additional requirements (if any – e.g. LR, …) to allow for well-informed decision on preamble design

## Slide 4: 11be/11bn mixed mode OFDMA
One issue that would impact preamble design is whether we envision mixed use of 11be and 11bn in OFDMA
  I.e., a mode where a single (DL or UL) OFDMA transmission addresses a mix of 11be and 11bn capable STAs simultaneously
There is an interest in combined use of different 802.11 generations
  See: A-PPDU proposals [4]
    Proposed for 11bn/11ax mix
    “Native” support for 11bn/11be mix would be simpler
      No dependence on SST, DSO, …
“Existing” UL OFDMA does not appear to prohibit a mix of 11ax and 11be user info fields
  Trigger frame sent in legacy format
  No support for mixed DL OFDMA

## Slide 5: 11be/11bn mixed mode OFDMA (2)
Being able to address both 11be and 11bn offers advantages:
  Increased efficiency (as opposed to having to partition 11be and 11bn STAs in separate groups)
  More seamless introduction of 11bn (AP) in legacy-11be (STA) deployment

## Slide 6: Impact on preamble design
Such a (DL) OFDMA transmission would have to meet a number of constraints:
  Be fully processed by both 11be and 11bn STAs
    Can not cause early termination for either type of STA
  Preamble changes after U-SIG (if any) should be transparent to 11be devices
    11be devices should be able to parse preamble – or at least the parts relevant for the 11be device
    In particular, 11be devices should see compatible EHT-SIG
  User Info fields could be identical for 11be and 11bn devices, or a new 11bn format could be defined for the User Info field
Clearly, support of mixed 11be/11bn OFDMA mode would require careful consideration of preamble design

## Slide 7: Conclusion
We presented additional considerations that could impact preamble design
One such issue is the support of mixed 11be/11bn OFDMA transmissions
This and other requirements need to be decided before making fundamental choices in preamble design

## Slide 8: Straw Poll
SP1:
Do you agree to include the following text to the 11bn SFD?
  UHR shall have the ability to address a mix of EHT and UHR STAs in a single OFDMA transmission (UL or DL)

## Slide 9: References
[1] UHR preamble design options , IEEE 802.11-24/0428
[2] UHR preamble design follow-up , IEEE 802.11-24/0774
[3] UHR PPDU PHY Version, IEEE 802.11-24/0876
[4] Discussion on A-PPDU follow-up, IEEE 802.11-24/0224