## Slide 1
Long LDPC Designs Based on 11n LDPC Codes
Date: 2024-07-16
Authors:
Name | Affiliations | Address | Phone | Email
Wei Lin | Huawei |  |  | lin.linwei@huawei.com
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 
Yan Xin |  |  |  | 
Chenchen Liu |  |  |  | 
David Xun Yang |  |  |  | 

## Slide 2: Discussion on Current WLAN LDPC Codes
The current 11n LDPC codes were designed and introduced for 802.11n in around 2004.
  There are 4 code rates (1/2, 2/3, 3/4, 5/6) and 3 code lengths (648, 1296, 1944) supported in Wi-Fi systems since then  Highest Rate = 5/6, Longest Length = 1944
  The 12 different LDPC matrices were designed individually for each rate and length, i.e., they don’t share the same base matrix or set of permutation coefficients.
Since the introduction of 11n LDPC codes, multiple LDPC codes were introduced for various industrial scenarios, e.g., 5G NR, 11ad/ay, DVB, ATSC 3.0, PON, etc.
  Among the various industrial LDPC codes, 5G NR LDPC codes can support very large range of rates and lengths with 2 base matrices and 2 set of permutation coefficients.
  BG1 of size 46 x 68 can support rates of 1/3 ≤ R ≤ 8/9, and information lengths of 308 ≤ K ≤ 8448
  BG2 of size 42×52 can support rates of 1/5 ≤ R ≤ 2/3, and information lengths of 40 ≤ K ≤ 3840
The 11n LDPC length of 1944 were designed for BW ≤ 40M, Streams ≤ 4, and Mod ≤ 64QAM
  In 802.11bn, the highest throughput can be achieved with largest BW >= 320M, 8 spatial streams, 4096QAM, thus the number of LDPC codewords can be very large with current length-1944 LDPC

## Slide 3: Potential Enhancements on WLAN LDPC
In [1], we surveyed the two major LDPC structures widely employed in industry currently.
  Classic QC-LDPC (11n/11ad/DVB)  Quasi Cyclic + Repeat Accumulate
  Raptor-Like QC-LDPC (5G)  Protograph + Multi-Edge Type + Accumulate Repeat Accumulate
  It can be seen from [1], the NR LDPC outperforms 11n 1944 LDPC codes with same length and rates
  Moreover, with the increase of codeword lengths, the NR LDPC outperforms the longest 11n LDPC at various code rates  over 1 dB at rate-1/2
In [2], authors also discussed the requirements for enhanced coding performance
  Considering the performance vs complexity trade off, [2] suggested the block-length of 2x1944 bits as a sweet spot
  Code constructions based on lifting on current 11n 1944 LDPC matrices were proposed, and fine tuning is achieved by modifying graphs to improve decoding threshold and error floor, while retaining the lifting framework
  The proposed 2x-LDPC codes can reuse the existing hardware blocks of 11n 1944 LDPC codes
In this contribution, 2x-LDPC codes based on lifting on current 11n 1944 LDPC matrices are also provided, with the same structure as the 2x-LDPC codes in [2]
  Further fine tuning is achieved by adjusting the connections to improve both decoding thresholds and error floors

## Slide 4: Lifting on 11n 1944 LDPC Codes
There are two ways of lifting that can somehow reuse the current 11n LDPC hardware
  CPM Diagonal Lifting (Better Reusing) vs. CPM Size Lifting (NR LDPC, Better Throughput)
Row #1
#2
#3
#4
Row #1
#2
#3
#4
#5
#6
#7
#8
2x-LDPC (N = 3888, R = 5/6)  Each Layer can reuse the current 11n LDPC Layers
11n LDPC (N = 1944, R = 5/6)
2x-LDPC Lifting Indication matrix
  Further fine tuning is achieved by adjusting the connections to improve both decoding thresholds and error floors

## Slide 5: Performance of 2x-LDPC Codes: R = 1/2
Our 2x-LDPC-A and 2x-LDPC-B in [2]: FER performance comparisons for a frame including a single/10/100 codewords  At least 100 Error Blocks collected at each SNR point
The performance of Num codewords is obtained by scaling the performance of single codeword: FER_Num = 1 – (1 – FER_1)Num

## Slide 6: Performance of 2x-LDPC Codes: R = 2/3
Our 2x-LDPC-A and 2x-LDPC-B in [2]: FER performance comparisons for a frame including a single/10/100 codewords  At least 100 Error Blocks collected at each SNR point
The performance of Num codewords is obtained by scaling the performance of single codeword: FER_Num = 1 – (1 – FER_1)Num

## Slide 7: Performance of 2x-LDPC Codes: R = 3/4
Our 2x-LDPC-A and 2x-LDPC-B in [2]: FER performance comparisons for a frame including a single/10/100 codewords  At least 100 Error Blocks collected at each SNR point
The performance of Num codewords is obtained by scaling the performance of single codeword: FER_Num = 1 – (1 – FER_1)Num

## Slide 8: Performance of 2x-LDPC Codes: R = 5/6
Our 2x-LDPC-A and 2x-LDPC-B in [2]: FER performance comparisons for a frame including a single/10/100 codewords  At least 100 Error Blocks collected at each SNR point
The performance of Num codewords is obtained by scaling the performance of single codeword: FER_Num = 1 – (1 – FER_1)Num

## Slide 9: Summary
In this contribution, we provided a set of 2x-LDPC (N = 3888 bits) codes based on lifting on current 11n 1944 LDPC matrices
With further fine tuning to improve both decoding thresholds and error floors, the proposed set of 2x-LDPC perform better or equivalent to the 2x-LDPC in [2].

## Slide 10: References
11-24-0924-00-00bn-initial-discussion-on-possible-ldpc-improvements-in-wlan, Wei Lin, et al.
11-23-1985-03-00bn-longer-ldpc-codeword, Rethna Pulikkoonattu, Tom Richardson, et al.
T. J. Richardson, “Error floors of LDPC codes,” in Proc. Allerton Conf. Communications, Control and Computing, Monticello, IL, Oct. 2003, pp. 1426–1435.
Jeremy Thorpe, “Low Density Parity Check (LDPC) Codes Constructed from Protographs,” JPL INP Progress Report 42-154, August 15, 2003.
T. Richardson, R. Urbanke, “Multi-edge type LDPC codes,” in Workshop Honoring Prof. Bob McEliece, Pasadena, CA, May 24–25, 2002.
A. Abbasfar, D. Divsalar and K. Yao, "Accumulate repeat accumulate codes," ISIT 2004. Proceedings., Chicago, IL, USA, 2004, pp. 505.

## Slide 11
Thank You

## Slide 12: Appendix: 2x-LDPC Matrix for R = 1/2
57 -1 -1 -1 -1 -1 -1 -1 50 -1 -1 -1 -1 11 -1 -1 -1 50 -1 -1 -1 79 -1 -1 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 57 -1 -1 -1 -1 -1 -1 -1 50 -1 -1 11 -1 -1 -1 50 -1 -1 -1 79 -1 -1 -1 -1 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 3 -1 -1 -1 28 -1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 55 -1 7 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
3 -1 -1 -1 28 -1 -1 -1 -1 0 -1 -1 -1 -1 -1 -1 55 -1 7 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
30 -1 -1 -1 -1 -1 -1 -1 -1 24 37 -1 -1 -1 -1 -1 -1 56 14 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 30 -1 -1 -1 -1 -1 -1 24 -1 -1 37 -1 -1 -1 -1 56 -1 -1 14 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 62 53 -1 -1 -1 -1 -1 -1 53 -1 -1 -1 -1 3 -1 -1 35 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
62 -1 -1 53 -1 -1 -1 -1 53 -1 -1 -1 -1 -1 -1 3 35 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 40 -1 -1 -1 -1 20 -1 -1 66 -1 -1 -1 -1 22 -1 28 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
40 -1 -1 -1 -1 -1 -1 20 66 -1 -1 -1 -1 -1 -1 22 -1 28 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
0 -1 -1 -1 -1 -1 -1 -1 -1 8 -1 -1 42 -1 -1 -1 50 -1 -1 -1 -1 -1 -1 8 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 0 -1 -1 -1 -1 -1 -1 8 -1 -1 -1 -1 42 -1 -1 -1 50 -1 -1 -1 -1 8 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 69 -1 79 79 -1 -1 -1 -1 -1 -1 -1 56 -1 -1 -1 -1 52 -1 -1 -1 -1 -1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1
69 -1 79 -1 -1 79 -1 -1 -1 -1 -1 -1 -1 56 -1 -1 52 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1
-1 65 -1 -1 -1 -1 -1 -1 -1 38 -1 57 -1 -1 -1 -1 72 -1 -1 -1 27 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1
65 -1 -1 -1 -1 -1 -1 -1 38 -1 57 -1 -1 -1 -1 -1 -1 72 -1 -1 -1 27 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1
-1 64 -1 -1 -1 -1 -1 -1 14 -1 52 -1 -1 -1 -1 -1 30 -1 -1 -1 -1 -1 32 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1
64 -1 -1 -1 -1 -1 -1 -1 -1 14 -1 52 -1 -1 -1 -1 -1 30 -1 -1 -1 -1 -1 32 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1
-1 -1 -1 45 -1 -1 -1 70 -1 0 -1 -1 -1 -1 -1 -1 -1 77 9 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1
-1 -1 45 -1 -1 -1 70 -1 0 -1 -1 -1 -1 -1 -1 -1 77 -1 -1 9 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1
-1 2 -1 56 -1 -1 -1 57 35 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 12 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1
2 -1 56 -1 -1 -1 57 -1 -1 35 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 12 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0
-1 24 -1 -1 61 -1 -1 -1 -1 60 -1 -1 -1 -1 27 -1 -1 51 -1 -1 -1 -1 -1 16 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1
24 -1 -1 -1 -1 61 -1 -1 60 -1 -1 -1 -1 -1 -1 27 51 -1 -1 -1 -1 -1 16 -1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0

## Slide 13: Appendix: 2x-LDPC Matrix for R = 2/3
-1 61 75 -1 -1 4 -1 63 -1 56 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 8 -1 -1 2 -1 -1 17 -1 25 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
61 -1 -1 75 4 -1 63 -1 56 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 8 -1 -1 -1 -1 2 17 -1 25 -1 -1 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
56 -1 74 -1 -1 77 20 -1 -1 -1 -1 -1 -1 -1 64 -1 -1 24 4 -1 -1 67 -1 -1 -1 7 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 56 -1 74 77 -1 -1 20 -1 -1 -1 -1 -1 -1 -1 64 24 -1 -1 4 67 -1 -1 -1 7 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 28 21 -1 -1 68 10 -1 7 -1 -1 14 -1 65 -1 -1 -1 -1 -1 -1 23 -1 -1 -1 -1 -1 -1 -1 -1 75 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1
28 -1 -1 21 68 -1 -1 10 -1 7 14 -1 65 -1 -1 -1 -1 -1 -1 -1 -1 23 -1 -1 -1 -1 -1 -1 75 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1 -1
48 -1 38 -1 -1 43 78 -1 -1 76 -1 -1 -1 -1 -1 -1 -1 -1 5 -1 36 -1 -1 -1 15 -1 -1 72 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1
-1 48 -1 38 43 -1 -1 78 76 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 5 -1 36 -1 -1 -1 15 72 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1
40 -1 -1 2 -1 53 25 -1 -1 -1 52 -1 62 -1 -1 -1 -1 20 -1 -1 -1 -1 44 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1
-1 40 2 -1 53 -1 -1 25 -1 -1 -1 52 -1 62 -1 -1 20 -1 -1 -1 -1 -1 -1 44 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1
-1 69 -1 23 -1 64 10 -1 22 -1 -1 -1 -1 21 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 68 -1 -1 23 -1 29 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1
69 -1 23 -1 64 -1 -1 10 -1 22 -1 -1 21 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 68 23 -1 29 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1
12 -1 0 -1 68 -1 20 -1 55 -1 61 -1 -1 -1 -1 40 -1 -1 -1 -1 -1 -1 -1 52 -1 -1 -1 -1 -1 -1 -1 44 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1
-1 12 -1 0 -1 68 -1 20 -1 55 -1 61 -1 -1 40 -1 -1 -1 -1 -1 -1 -1 52 -1 -1 -1 -1 -1 -1 -1 44 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0
-1 58 -1 8 -1 34 -1 64 -1 78 -1 -1 -1 -1 -1 11 -1 78 -1 24 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 58 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1
58 -1 8 -1 34 -1 64 -1 78 -1 -1 -1 -1 -1 11 -1 78 -1 24 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 58 -1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0

## Slide 14: Appendix: 2x-LDPC Matrix for R = 3/4
48 -1 -1 29 28 -1 -1 39 9 -1 61 -1 -1 -1 -1 -1 -1 -1 63 -1 45 -1 80 -1 -1 -1 -1 -1 -1 -1 37 -1 -1 32 22 -1 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1 -1
-1 48 29 -1 -1 28 39 -1 -1 9 -1 61 -1 -1 -1 -1 -1 -1 -1 63 -1 45 -1 80 -1 -1 -1 -1 -1 -1 -1 37 32 -1 -1 22 -1 1 -1 0 -1 -1 -1 -1 -1 -1 -1 -1
-1 4 49 -1 42 -1 48 -1 11 -1 30 -1 -1 -1 -1 -1 -1 -1 49 -1 -1 17 41 -1 37 -1 -1 15 -1 -1 -1 54 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1 -1
4 -1 -1 49 -1 42 -1 48 -1 11 -1 30 -1 -1 -1 -1 -1 -1 -1 49 17 -1 -1 41 -1 37 15 -1 -1 -1 54 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1 -1
35 -1 -1 76 -1 78 -1 51 -1 37 -1 35 21 -1 -1 -1 17 -1 64 -1 -1 -1 -1 -1 -1 -1 59 -1 7 -1 -1 -1 -1 -1 32 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1 -1
-1 35 76 -1 78 -1 51 -1 37 -1 35 -1 -1 21 -1 -1 -1 17 -1 64 -1 -1 -1 -1 -1 -1 -1 59 -1 7 -1 -1 -1 -1 -1 32 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1 -1
-1 9 -1 65 44 -1 9 -1 54 -1 -1 56 73 -1 -1 34 -1 42 -1 -1 -1 -1 -1 -1 35 -1 -1 -1 -1 -1 -1 -1 -1 46 39 -1 0 -1 -1 -1 -1 -1 0 -1 0 -1 -1 -1
9 -1 65 -1 -1 44 -1 9 -1 54 56 -1 -1 73 34 -1 42 -1 -1 -1 -1 -1 -1 -1 -1 35 -1 -1 -1 -1 -1 -1 46 -1 -1 39 -1 0 -1 -1 -1 -1 -1 0 -1 0 -1 -1
-1 3 62 -1 -1 7 80 -1 -1 68 26 -1 -1 -1 -1 80 55 -1 -1 -1 36 -1 -1 -1 -1 26 -1 -1 -1 9 -1 -1 -1 72 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0 -1
3 -1 -1 62 7 -1 -1 80 68 -1 -1 26 -1 -1 80 -1 -1 55 -1 -1 -1 36 -1 -1 26 -1 -1 -1 9 -1 -1 -1 72 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1 0
-1 26 -1 75 33 -1 21 -1 69 -1 -1 59 -1 3 -1 38 -1 -1 -1 -1 -1 -1 -1 35 -1 -1 62 -1 36 -1 26 -1 -1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0 -1
26 -1 75 -1 -1 33 -1 21 -1 69 59 -1 3 -1 38 -1 -1 -1 -1 -1 -1 -1 35 -1 -1 -1 -1 62 -1 36 -1 26 -1 -1 -1 -1 -1 1 -1 -1 -1 -1 -1 -1 -1 -1 -1 0

## Slide 15: Appendix: 2x-LDPC Matrix for R = 5/6
-1 13 -1 48 -1 80 66 -1 -1 4 -1 74 -1 7 30 -1 76 -1 -1 52 37 -1 60 -1 -1 -1 -1 49 73 -1 -1 31 -1 74 73 -1 23 -1 -1 -1 1 -1 0 -1 -1 -1 -1 -1
13 -1 48 -1 80 -1 -1 66 4 -1 74 -1 7 -1 -1 30 -1 76 52 -1 -1 37 -1 60 -1 -1 49 -1 -1 73 31 -1 74 -1 -1 73 -1 23 -1 -1 -1 1 -1 0 -1 -1 -1 -1
-1 69 63 -1 -1 74 56 -1 64 -1 -1 77 57 -1 65 -1 -1 6 -1 16 51 -1 -1 -1 64 -1 -1 -1 68 -1 9 -1 -1 48 62 -1 54 -1 27 -1 -1 -1 0 -1 0 -1 -1 -1
69 -1 -1 63 74 -1 -1 56 -1 64 77 -1 -1 57 -1 65 6 -1 16 -1 -1 51 -1 -1 -1 64 -1 -1 -1 68 -1 9 48 -1 -1 62 -1 54 -1 27 -1 -1 -1 0 -1 0 -1 -1
51 -1 15 -1 0 -1 -1 80 -1 24 25 -1 42 -1 54 -1 -1 44 -1 71 -1 71 9 -1 67 -1 -1 35 -1 -1 58 -1 -1 -1 29 -1 -1 -1 -1 53 0 -1 -1 -1 0 -1 0 -1
-1 51 -1 15 -1 0 80 -1 24 -1 -1 25 -1 42 -1 54 44 -1 71 -1 71 -1 -1 9 -1 67 35 -1 -1 -1 -1 58 -1 -1 -1 29 -1 -1 53 -1 -1 0 -1 -1 -1 0 -1 0
16 -1 -1 29 36 -1 -1 41 44 -1 56 -1 -1 59 37 -1 50 -1 24 -1 -1 -1 -1 65 4 -1 65 -1 52 -1 -1 -1 -1 4 -1 -1 73 -1 -1 52 1 -1 -1 -1 -1 -1 0 -1
-1 16 29 -1 -1 36 41 -1 -1 44 -1 56 59 -1 -1 37 -1 50 -1 24 -1 -1 65 -1 -1 4 -1 65 -1 52 -1 -1 4 -1 -1 -1 -1 73 52 -1 -1 1 -1 -1 -1 -1 -1 0