## Slide 1: Considerations for Multi-AP SP Coordination
Date: 2024-11-07
Authors:

## Slide 2
Abstract
In this contribution we share some thoughts on the multi-AP coordination of service periods.

## Slide 3: Introduction
Multi-AP coordination of service periods have been discussed in 802.11bn [1][2]
  Coordinated TDMA
  Coordinated rTWT/TWT
  Combination of coordinated TDMA and coordinated rTWT/TWT
Some of the features have already passed motions:
  Coordinated TDMA
  Coordinated rTWT
In this contribution, we want to share our thoughts on designing coordinated TDMA and Coordinated rTWT/TWT

## Slide 4: Coordinated rTWT/TWT (1)
TGbn has passed Motion 48 regarding coordinated rTWT [3]:
  Move to add to the TGbn SFD the following:
  Define mechanisms that enable APs to coordinate their rTWT schedule(s) and/or to ensure that one AP provides the protection of the rTWT schedule(s) of the other AP.
  NOTE – TBD mechanisms including negotiation between 2 APs and advertisement.
Coordinated rTWT is a useful tool to ensure delivery of periodic low latency traffic
Motion text does not make it clear whether there is consensus on protection of OBSS’ rTWT schedule
  rTWT is meant to carry low latency traffic which must be successfully transmitted within a short interval
  Coordination of rTWT alone provides some protection, but may not be sufficient
Protection of OBSS’ rTWT is needed in addition to coordination

## Slide 5: Coordinated rTWT/TWT (2)
TWT is a useful tool for 802.11 networks
  TWT was originally designed to be a power saving feature
  But it is also a tool to reduce contention and allow UL scheduling
    E.g. triggered TWT
Benefits of TWTs may be lost if they are not coordinated among OBSS
  Increased contention from OBSS
  Unable to transmit when triggered
  STAs need to stay awake outside of TWT since they were not able to complete their transmission/reception
TWTs should be coordinated as well among OBSS
  Whether it needs protection needs more discussion

## Slide 6: Coordinated rTWT/TWT (3)
A few things to consider when designing coordinated TWT/rTWT
  OBSS rTWT should be protected
  Prevent abuse
    APs know the priority of rTWT traffic from their own BSS through SCS, but OBSS APs have no access to that information, leading to opportunities of abuse by greedy neighbors

## Slide 7: Coordinated TDMA (1)
TGbn has passed Motion 46 on C-TDMA [3]:
  Move to add to the TGbn SFD the following:
  TGbn shall define a Coordinated TDMA (C-TDMA) procedure for an AP to share its time resources of an obtained TXOP with a set of APs.
    Set of APs is TBD.
    The set can consist of one AP.
C-TDMA would be beneficial to support unpredictable low latency traffic
  Proposals to allow one AP to poll other APs for intention and traffic priority before sharing the AP’s obtained TXOP [4]

## Slide 8: Coordinated TDMA (2)
A few things that need to be considered when designing C-TDMA
  Reduce overhead:
    There is a lot of overhead in C-TDMA:
      Obtaining TXOP
      Polling of OBSS AP
      Response of OBSS AP
      TXOP sharing frame exchanges
    Benefits should be weighted considering the amount of overhead
  Over-provisioning of TXOP:
    Sharing APs likely want to operate in a quid pro quo manner
    Easy way to have sufficient time for an AP’s own BSS and share enough time for OBSS is to obtain a TXOP that is longer than needed by an AP’s own BSS
    Such a practice may not be beneficial for low latency traffic delivery
    Is there a way to prevent this?

## Slide 9: Coordinated TDMA (3)
A few things that need to be considered when designing C-TDMA (cont’d)
  Prevent abuse:
    APs know the priority of the traffic in its own BSS through SCS
    A sharing AP has no such information about OBSS traffic, leaving room for abuse by greedy APs
  Security:
    Security is an important consideration in designing TGbn features
    How can we ensure security among OBSS APs, e.g.:
      How is trust established
      Security context exchange

## Slide 10: Conclusions
  We discussed the Coordinated SPs feature in TGbn
    Coordinated rTWT/TWT
    Coordinated TDMA
  We discussed a number of considerations when designing the coordinated SPs feature
    For Coordinated rTWT/TWT:
      OBSS rTWT should be protected in addition to coordination
      OBSS TWT should be coordinated
      Design should consider features to prevent abuse by OBSS APs
    For Coordinated TDMA:
      Weight benefits considering the overhead
      Prevent over-provisioning of TXOP
      Prevent abuse by greedy OBSS APs
      Ensure security among OBSS APs

## Slide 11
References
[1] 11-24/462r0, MAPC Coordinated service periods (MAPC SPs), Brian Hart
[2] 11-23/1962r0, Gain analysis for coordinated AP transmissions, Abhishek Patil
[3] 11-24/171r16, TGbn Motions List – Part 1, Alfred Asterjadhi
[4] 11-24/1016r2, C-TDMA Follow up: Additional details on framing sequence, Sanket Kalamkar