## Slide 1: Considerations on SCS enhancement
Date: 2024-10-31
Authors:

## Slide 2: Introduction
In applications indicated in the PAR [1]:
Virtual reality (VR), robotics, industrial automation for industrial IoT, etc.
In a scenario where a single AP manages the entire room within a house under a single BSS, the AP must control all devices handling multiple applications, such as VR apps and other applications, while meeting the application requirements.
Audio-Video synchronization is one of the minimum requirements for immersive experience.
STA groups [2]
Example
Virtual meetings with avatars
At DL

## Slide 3: Existing procedure in 11be
Restricted Target Wake Time (R-TWT)
Stream Classification Service (SCS)
  One or more SCS streams can be established between one or multiple non-AP STAs and an AP
    Each SCS stream is managed by an SCSID
    For MLD, SCSID is managed at the MLD level
  QoS requirements for each SCS stream are set parametrically using the QoS Characteristics Element from the STA side
    Delay bound, etc.

## Slide 4: Issue
For example, in VR applications, the specific application requirements necessary to achieve an immersive experience can not be fully addressed within the SCS.
Minimum requirement: Video and audio synchronization (e.g., lip-sync)
In addition, while QoS is configured using parametric settings (e.g., the QoS Characteristics element), it is managed through TID values ranging from 0 to 7. This limits the ability to differentiate and prioritize traffic flows [3].
When multiple SCS streams are assigned the same TID, before the traffic from the VR application (e.g., SCSID#1 and SCSID#2) is fully transmitted, traffic from other applications (e.g., SCSID#N) may intervene. This can lead to issues such as out-of-sync video and audio (e.g., lip-sync).
VR App with application requirements

## Slide 5: Grouping Multiple SCS Streams
The Application ID (App ID) is included in the SCS Request frame and notified to the AP alongside the SCSID, enabling the AP to group multiple SCSIDs based on the App ID.
Non-AP STA: Sends an SCS Request frame that includes both the SCSID and the Application ID.
AP: Sends an SCS Response frame to establish the SCS stream with the Non-AP STA and performs scheduling using the Application ID, which groups multiple SCSIDs.

## Slide 6: Scheduling across Multiple SCS Streams by Application ID
The Application ID facilitates the transmission of traffic associated with SCSIDs tied to the same application.
For instance, in VR applications, requirements like video and audio synchronization (e.g., lip-sync) can be effectively managed through the Application ID.
with application requirements

## Slide 7: Summary
This contribution proposes using the Application ID to group multiple SCSIDs.
The Application ID can group multiple SCSIDs, facilitating the transmission of traffic associated with SCSIDs tied to the same application.
  In scenarios where a single AP manages the entire room in a house under a single BSS, the Application ID helps meet specific application requirements, such as video and audio synchronization (e.g., lip-sync) in VR applications.

## Slide 8: Straw Poll 1
Define a high-level ID that groups multiple SCS streams, each identified by SCSIDs, from the perspective of the application layer, in the SFD.
  The high-level ID may be used to assist an AP MLD or Non-AP MLD in scheduling radio resources to meet relative QoS requirements among the multiple SCS streams (e.g., allowable delay time for one type of SCS stream relative to another)

## Slide 9: References
[1] IEEE 802.11-23/480r3, UHR proposed PAR
[2] IEEE 802.11-24/0625r0, Thoughts on low latency traffic transmission
[3] IEEE 802.11-22/0041r0, Some Issues on SCS Operation

## Slide 10: Appendix: Possible Use-case
In a scenario where a single AP manages an entire factory within a single BSS, the AP must control all devices handling multiple applications (Group #1, #2, etc.).
STA groups [2]
...
AP
Factory, etc.
Group #1 (AGVs, etc.)
Group #2
(Robots, etc.)
Each group, working in the same location or performing the same task, requires low-latency transmission simultaneously.
※The details of other applications are omitted from this slide.

## Slide 11
AGVs report location information to the associated AP while moving
AP
...
At Server
(Path planning)
UL Data
...
Some location information may become obsolete in terms of calculating the optimal route plan at a given moment.
※The details of other applications are omitted from this slide.
AGV #1
AGV #2 ...
AGV #N
...
AP
The Application ID facilitates the transmission of traffic associated with SCSIDs within a specified period
AGV #1
AGV #2 ...
AGV #N
...
AP
Appendix: Possible Use-case
In order to the route plan accurately calculated ...