## Slide 1: Signaling for UHR PPDU
Date: 2024-08-14
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Introduction
Spatial domain unequal modulation (UEQM) has been approved.
  TGbn defines unequal modulation over different spatial streams.
Suggested UEQM patterns have been discussed in a variety of contributions [1-6].
This contribution discusses potential signaling, for non-TB case first. The TB case may potentially follow non-TB case and will be discussed later. And this contribution is for non-ELR case.
We focus on per user field. Assume common field will basically follow 11be.

## Slide 3: Recap – 802.11be EHT-SIG signaling
User field for non-MU-MIMO in EHT-SIG is as follows:
  11be only defines up to 8SS per user, hence MSB of NSS can be seen as reserved.
User field for MU-MIMO in EHT-SIG is as follows:
  11be later decides to support NSS_total to 8, hence, like 802.11ax, 4 bit is enough for spatial configuration, two bits can be saved.

## Slide 4: 802.11bn UHR-SIG signaling
For UHR-SIG, if we can reuse the previous structure. It is easy for implementation, regarding signaling parsing, encoding/decoding block.
Whilst it is a newly designed SIG field, we can increase the per user field length if indeed needed. The field order/position can also be different from 11be.

## Slide 5: UHR-SIG signaling - EQM
One feature needed to consider so far is UEQM. For non-MU-MIMO User field, let’s first see the EQM case.
  The EQM case is first shown as follows. B19 is used as a EQM/UEQM flag as an example.
  Here, we still assume max 8 SS as 11ax and 11be. There exists 11ax and 11be products with >4SS capability. And it is good to maintain the same max data rate as before.
  Regarding longer LDPC codeword, besides potential signaling, an alternative way could be following 11ax and 11be style, and defines equations to choose codeword length.
EQM:

## Slide 6: UHR-SIG signaling - UEQM
For non-MU-MIMO User field, let’s further see the UEQM signaling. There could be several options:
  Opt 1: First indicate EQM/UEQM, indicate base MCS, indicate NSS, and indicate UEQM pattern variations of the other NSS-1 SS using a table.
    Max 4SS to reduce the pattern variations. May group larger NSS if needed.
    LDPC only, TxBFed is assumed for UEQM： bits in EQM case are repurposed to indicate UEQM pattern variations.
  UEQ QAM variation for a specific NSS (e.g., NSS=2) could be:
Index | UEQM pattern variations | 
 | 1st Stream | 2nd Stream
00 | QAM (Base MCS) | QAM-1
01 | QAM | QAM-2

## Slide 7: UHR-SIG signaling - UEQM
NSS and UEQM pattern variations could be also merged:
  Opt 2: First indicate EQM/UEQM, indicate base MCS, then indicate NSS and UEQM pattern variations of the other NSS-1 SS at the same time using a table
  UEQM pattern variations (3 bit as an example) for a all NSS (NSS=2,3,4) could be:
    Can be extended to 4 bits to include more patterns
Index | NSS | Unequal QAM variation patterns |  |  | 
 |  | 1st Stream | 2nd Stream | 3rd Stream | 4th Stream
000 | 2SS | QAM | QAM-1 |  | 
001 |  | QAM | QAM-2 |  | 
010 | 3SS | QAM | QAM | QAM-1 | 
011 |  | QAM | … | … | 
100 |  | QAM | … | … | 
101 | 4SS | QAM | QAM | QAM | QAM-1
110 |  | QAM | … | … | …
111 |  | QAM | … | … | …

## Slide 8: UHR-SIG signaling – MU-MIMO
For MU-MIMO, if UEQM is not applied then we have the following format:
If UEQM is applied then we have the following format for EQM and UEQM case.
  The bit position of coding is changed compared with 11be.
  May also use joint MCS and UEQM pattern variations indication to enable one reserved bit
EQM:
UEQM:

## Slide 9: Summary
In this contribution, we talk about the User field signaling for non-TB, non-ELR case.
An EQM/UEQM flag is introduced to contain different information for EQM and UEQM case.
A base MCS field and UEQM pattern variations field are proposed to simplify the parsing.
  Similar as EQM case
  Compared with joint QAM combinations in 11n

## Slide 10: Straw Poll 1
Do you agree to include the following into the 11bn SFD?
  For a (non-ELR) UHR MU PPDU, in the UHR-SIG field, the length of a User field is 22 bit.
  Y
  N
  A

## Slide 11: Straw Poll 2
Do you agree to include the following into the 11bn SFD?
  For a (non-ELR) UHR MU PPDU, there exists a EQM/UEQM flag in a User field for non-MU-MIMO in the UHR-SIG field.
  Y
  N
  A

## Slide 12: Straw Poll 3
Do you agree to include the following into the 11bn SFD?
  For a (non-ELR) UHR MU PPDU, when EQM/UEQM flag indicates UEQM in a User field for non-MU-MIMO, there exists a (base) MCS field and a field indicating UEQM pattern variations of the other NSS-1 SS based on a base MCS.
  Y
  N
  A

## Slide 13: Reference
11-24-0890-01-00bn-unequal-pattern-discussion, Ross Jian Yu (Huawei)
11-24-0474-02-00bn-uhr-unequal-modulation-pattern-and-new-mcs, Rui Cao (NXP)
11-24-0498-01-00bn-unequal-modulation-in-mimo-txbf-and-new-mcs-for-11bn, Alice Chen (Qualcomm)
11-24-0176-01-00bn-unequal-modulation-over-spatial-streams, Hao Song (Intel Corporation)
11-24-0734-01-00bn-on-ueqm-and-ueq-mcs, Ron Porat (Broadcom)
11-24-0507-02-00bn-ueqm-further-details, Ron Porat (Broadcom)