## Slide 1: DPWiFi revA
Date: 2024-10-17
Authors:

## Slide 2: Abstract
TGbn PHY candidate DPWiFi originally proposed in Nov ‘23, an improved radiowave polarization processing model incorporated June ‘24 unearthed a serious, latent flaw in the original Dynamic Polarization Propagation Channel formulation. Since remedied, an updated “DPWiFi revA” Tx-Rx model plus corresponding “DPWiFiTRXv4” MATLAB representation functional validation and performance characterization data, analyses and conclusions are presented herein.

## Slide 3
Legacy WiFi (Static) Polarization Operation
A WiFi Tx antenna “polarizes” by launching RF waveforms S in a precise spatial orientation per an “Orthogonal Polarization Baseline (OPB)”
Linearly Polarized PTX radiates along a fixed angle between 0o (H) or 90o (V)
PTX(S) = H or V, per the OPB
Normal terrestrial propagation may further polarize S by rotating PTX by a “polarization angle” ψ
  LP waveforms propagate fixed-rotated by ψo from PTX(S)
  PTX (S, ψ) = ψ or ψ + 90o
A WiFi Rx antenna “depolarizes” detected waveforms into “Matched-Polarization (MP)” or “Mismatched-Polarization (MMP)” components
PRX (S, ψ) = H or V
MP (PTX (S,ψ)) = cosψ S(t)
MMP (PTX (S, ψ)) = sinψ S(t)
As Legacy WiFi Polarization assumes OPB-aligned Tx and Rx antennas
Legacy WiFi Polarization = PTRX(S) = MP (PTX (S,ψ)) = cosψ S(t)

## Slide 4
Proposed DPWiFi Dynamic Polarization Operation
Channel Polarization further rotates DPTX(S) by ψ
DPTX (S, ψ) = Tx DPC(ψ)
A DPWiFi Rx Antenna depolarizes DPTX into either “Matched-DPC (MDPC)” or “Mismatched-DPC (MMDPC)” elements
DPRX(S) = Rx DPC
MDPC (S, ψ) = (Tx DPC · Rx DPC) S(t)
MMDPC (S, ψ) = f(S(t), cosψ, sinψ)
A DPWiFi Tx Antenna modulates its Polarization by switching orthogonal antenna elements H and V per a binary sequence DPC
DPTX(S) = Tx DPC
As DPWiFi Polarization also assumes OPB-aligned Tx and Rx antennas
DPWiFi Polarization = DPTRX(S) = MDPC (S, ψ) = (Tx DPC · Rx DPC) S(t)

## Slide 5
DPWiFi revA TRX Model
  Given n WiFi-7 RF stream n-vectors [S], [S*] and [S’], and
  The ψ-polarized Propagation Channel nxn matrix [HDP], and
  Walsh n-vectors [TxDPC] and [RxDPC] such that
[TxDPC] = [DPC1 DPC2 … DPCn] = [RxDPC], where
DPCi · DPCj = cosψ if i = j
DPCi · DPCj = (cosψ + sinψ)/2 if i ≠ j
    If [HDP] is Non-Singular there exists an [HDP-1]such that [S’] = [S] x [HDP] x [HDP-1]= [S]

## Slide 6
DPWiFi revA Propagation Channel [HDP]
  Walsh-modulated DPWiFi Polarization establishes that
  S*(t) = cosψ S(t) if Tx DPC = Rx DPC, or S*(t) = (cosψ + sinψ)/2 S(t) if Tx DPC ≠ Rx DPC
  Extending to the case of n Si and corresponding DPCi we obtain [S*] = [S] x [HDP], where
  Noting that for 0o < ψ < 45o
  0.50 ≤ (cosψ + sinψ)/2 ≤ 0.71 and 0.70 ≤ cosψ ≤ 1.00, we can therefore conclude
    The DPWiFi revA Propagation Channel [HDP] is Indeed Non-Singular

## Slide 7
DPWiFi revA Rx MIMO Demultiplexer [HDP-1]
Then:
Equivalently:
Given:
Then:
Equivalently:
    The DPWiFi revA MIMO Demultiplexer [HDP-1] is a Trivial Construct

## Slide 8
DPWiFi rev- vs DPWiFi revA
    DPWiFi rev- was just a Degenerate Manifestation of DPWiFi revA
    Note: DPWiFi rev- and DPWiFi revA are equivalent for ψ < 7.5o

## Slide 9
DPWiFi revA MATLAB Representation: DPWiFiTRXv4
[S] [P] x [ψ] [P] x [HDP-1] = [S’]
[S] x [HDP] x [HDP-1] = [S’]

## Slide 10
DPWiFi revA MATLAB Validation Plan
DPWiFiTRXv4 32x 4kQAM5/6-320MHz DPWiFi Streams BER vs Channel Polarization, Rx Adaptation |  | 
Case | Channel ψ (o) | Rx Adaptation
VP-1 | 0.0 | N
- |  | Y
VP-2 | 1.0 | N
- |  | Y
VP-3 | 1.1 | N
VP-4 |  | Y
VP-5 | 5.0 | N
VP-6 |  | Y
VP-7 | 10.0 | N
VP-8 |  | Y
VP-9 | 25.0 | N
VP-10 |  | Y
VP-11 | 40.0 | N
VP-12 |  | Y

## Slide 11
DPWiFi revA MATLAB Validation Exercise

## Slide 12
DPWiFi revA MATLAB Validation Exercise

## Slide 13
DPWiFi revA MATLAB Validation Exercise

## Slide 14
DPWiFi revA MATLAB Validation Exercise

## Slide 15
DPWiFi revA MATLAB Validation Exercise

## Slide 16
DPWiFi revA MATLAB Validation Exercise

## Slide 17
DPWiFi revA MATLAB Validation Results
Observations
Assessments
  DPWiFi indeed transports 92 Gbps within a 320 MHz channel
  DPWiFi is extraordinarily sensitive to propagation impairments Absent receiver adaptation, even a slight morning mist would irremediably crash a DPWiFi link
  Rx Adaptation, however, comprehensively mitigates any amount of Channel Polarization
Conclusions DPWiFi revA (henceforth simply “DPWiFi”) will be the fastest (Rate), farthest (Range) and toughest (Impairment-impervious) WLAN PHY ever devised
DPWiFi revA BER Performance in Impaired Propagation Channels DPWiFi-32 MCS13 320 MHz vs Channel Polarization, Rx Adaptation |  |  |  |  |  |  | 
Channel Impairment Polarization Angle | None 0.2o | Mist 1.0o | Fog 1.1o | Rain 5.0o | Foliage 10.0o | Grzng Reflection 25.0o | Nr Orthgnl Reflection 40.0o
Ch Polarization Index | 0.5016 | 0.5087 | 0.5095 | 0.5417 | 0.5792 | 0.6645 | 0.7044
BER, No Adaptation | 0.000 | 0.000 | 0.003 | 0.196 | 0.275 | 0.384 | 0.450
BER, Adaptation | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 18
So, What Next? Hardware Validation!
Quick-turn DPWiFi Prototype
8x 11.5 Gbps SMX-4 WiFi-7s 1x 92.2 Gbps PMX-32 DPWiFi

## Slide 19
Summary and Conclusions
TGbn PHY candidate DPWiFi comprises breakthrough MIMO Polarization Multiplexing providing 92 Gbps P2P data transport within 320 MHz at 6 GHz, regardless of propagation impairments.
A MATLAB model has fully simulation-validated the above-claimed DPWiFi functionality and performance.
A WiFi-7 based prototype will attempt to correspondingly hardware-validate DPWiFi by this year’s end.
DPWiFi remains without peer as a candidate TGbn PHY

## Slide 20: References
1. 23/1606r1-UHRSG Dynamic Polarization Multiplexing and Beamforming WLANs Carlos A Rios (Terabit Wireless Internet), 13-Sep-2023
23/1756r3-TGbn MIMO Dynamic Polarization and Beamforming: Proposed IEEE802.11bn PHY Carlos A Rios (Terabit Wireless Internet), 16-Nov-2023
24/0041r12-TGbn DPWiFi MATLAB Validation Carlos A Rios (Terabit Wireless Internet), 02-Feb-2024
24/0440r6-TGbn DPWiFi for IEEE802.11bn WMANs Carlos A Rios (Terabit Wireless Internet), 22-Apr-2024